Vc/21-Jun-04

### Week26  starting 21 June  04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 21 june

| LHC SM18 Magnet Test Facility TBA1 MBBL2053 ICS 4 Final connection 296.9 TBA2 MBAR2015 MM 12 TRU Disconnect 101.7 TBB1 MBAR2031 PT 2 HV Cold Test 2.35 TBB2 MBBL1120 ICS 6 Disconnect Magnet WP07 303.1 TBC1 MBBL2074 Prep 1 Lyre Test 297.4 TBC2 _ _ 298 TBD1 SSS11 PT 12 Warm Up 298.6 TBD2 SSS37 Prep 5 Pumping + Cool Down 2.03 TBE1 MBBL1102 PT 6.1 Training 1 4.6 HV TBE2 MBBL1121 ICS 4 Final connection 296.8 TBF1 MBBL1097 MM3 Full Load Line + Joints 1.9 TBF2 MBAL3142 PT 1 IAP @ cold 4.7 6/21/2004 6:41:31 PM Temperature data are taken from TBSM18 site |  |  |  |  |
| --- | --- | --- | --- | --- |

Test Coordinator this week: Vittorio  ; MTM support on call :  (16-3602).Richard

9 Magnets( 9 dipoles)   Disconnected after tests last week    ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- LHe cooling: with four dipoles cold, quench recovery was very slow everywhere; cryo operators told me that we have only 18 gr/s, and when I mentioned the new capacity of 24 gr/s (which was reported to be implemented in April) they did not understand what I was talking about.

- I was told that 2nd CWU is still out of order

- cooling down from 2.3 to 1.9 K on SSS11 (TBD1) as required for the SSW corrector tests required from 13:00 on Saturday to 15:00 on Sunday.

- Automatic cryo priority allocation; from cryo operators I got clearly the information that the system does NOT work as intended, i.e. the magnets which WE tell them have low priority somehow “steal” resources from the ones having higher priority. If true, this implies that WE should ask explicitly to put low-priority magnets in stand-by

  - SSS work :  HV Insul & “ Hair-dryer”

Bench status  and tests for now( Monday 21/6 at 19.00)  & next few days :  see Video Display

| Magnets under Test on 21-06 6:56:21 PM |
| --- |
| - | Bench | Magnet | Shafts | Start | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | Last Test Desc | Time | I | Temp. | Total |
| 1 | TBA1 | MBBL2053 |  | 18-06 | 73 h. | - | - | - | - | ICS 4 Final connection | 21-06 (09 : 04) | 0 A. | 300 K | 73 hours |
| 2 | TBA2 | MBAR2015 |  | 15-06 | 33 h. | 67 h. | 45 h. | 1 h. | 0 h. | MM 12 TRU Disconnect | 21-06 (16 : 30) | 0 A. | 300 K | 148 hours |
| 3 | TBB1 | MBAR2031 |  | 17-06 | 27 h. | 58 h. | 13 h. | - | - | PT 2 HV Cold Test | 21-06 (06 : 35) | 0 A. | 4.4 K | 98 hours |
| 4 | TBB2 | MBBL1120 |  | 14-06 | 21 h. | 43 h. | 89 h. | 13 h. | 1 h. | ICS 6 Disconnect Magnet WP07 | 21-06 (17 : 23) | 0 A. | 300 K | 168 hours |
| 5 | TBC1 | MBBL2074 |  | 21-06 | 4 h. | - | - | - | - | Prep 2.2 IAP @ warm LF | 21-06 (18 : 44) | 0 A. | 300 K | 4 hours |
| 6 | TBD1 | SSS11 |  | 27-05 | 180 h. | 86 h. | 320 h. | 24 h. | - | PT 12 Warm Up | 20-06 (18 : 43) | 0 A. | Warming | 610 hours |
| 7 | TBD2 | SSS37 |  | 15-06 | 98 h. | 65 h. | - | - | - | Prep 5 Pumping + Cool Down | 19-06 (01 : 45) | 0 A. | Cooling | 163 hours |
| 8 | TBE1 | MBBL1102 |  | 16-06 | 28 h. | 47 h. | 46 h. | - | - | PT 6.1 Training 1 | 20-06 (02 : 00) | 11614 A. | 1.9 K | 121 hours |
| 9 | TBE2 | MBBL1121 |  | 18-06 | 71 h. | - | - | - | - | ICS 4 Final connection | 21-06 (08 : 06) | 0 A. | 300 K | 71 hours |
| 10 | TBF1 | MBBL1097 |  | 14-06 | 40 h. | 51 h. | 80 h. | - | - | MM3 Full Load Line + Joints | 21-06 (12 : 30) | 11850 A. | 1.9 K | 171 hours |
| 11 | TBF2 | MBAL3142 |  | 15-06 | 41 h. | 78 h. | 23 h. | - | - | PT 1 IAP @ cold | 20-06 (19 : 52) | 0 A. | 1.9 K | 142 hours |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBL2053 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR2015 | 10896 Amp. (D1-U-S01) | 11570 Amp. (D1-L-S01) | 11935 Amp. (D2_L_S01) | 12693 Amp. (D1_L_S01) | 12849 Amp. () | - | - | - | - | - | - | - | - |
| 3 | MBAR2031 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBL1120 | 10287 Amp. (D2_U) | 11454 Amp. (D1-U) | 12096 Amp. (D2-L) | 12288.3 Amp. (D1 L) | 12356 Amp. (D2_L) | 12443 Amp. (D1_L) | 12581 Amp. (D1-L) | 12631 Amp. (D2-L) | 12731 Amp. (D1_U) |  | - | - | - |
| 5 | MBBL2074 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS11 | 11758 Amp. (No Data) | 12046 Amp. (I_12) | 12067 Amp. (I-34) | 12423 Amp. (E-12) | 12140 Amp. (E-34-S02) | 12568 Amp. (E 12-S06) | 12778 Amp. (E-34-S06) | 12856 Amp. () | - | - | - | - | - |
| 7 | SSS37 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBBL1102 | 11614 Amp. (D2-L) |  | - | - | - | - | - | - | - | - | - | - | - |
| 9 | MBBL1121 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBL1097 | 11393 Amp. (D1-U-S13) | 11743 Amp. (D2-L-S13) | 11995 Amp. (D1-U-S12) | 12404 Amp. (D2-U-S13) | 12667 Amp. (D1-U-S13) |  | - | - | - | - | - | - | - |
| 11 | MBAL3142 |  | - | - | - | - | - | - | - | - | - | - | - | - |

# Results by Week

| Magnets under Test from 13-06-2004 to 19-06-2004 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA1 | MBAR3063 |  | 11-06-2004 | 37 h. | 78 h. | 18 h. | 21 h. | 14 h. | 18-06-2004 | 168 hours |  |  |
| 2 | TBA2 | MBBL3084 |  | 07-06-2004 | 22 h. | 53 h. | 44 h. | 14 h. | 29 h. | 15-06-2004 | 192 hours |  |  |
| 3 | TBB1 | MBBL1098 |  | 11-06-2004 | 62 h. | 33 h. | 28 h. | 13 h. | 8 h. | 17-06-2004 | 144 hours |  |  |
| 4 | TBB2 | MBBL3081 |  | 08-06-2004 | 35 h. | 33 h. | 47 h. | 23 h. | 5 h. | 14-06-2004 | 144 hours |  |  |
| 5 | TBC1 | MBAL2083 |  | 08-06-2004 | 34 h. | 41 h. | 33 h. | 16 h. | 20 h. | 14-06-2004 | 144 hours |  |  |
| 6 | TBE1 | MBBL1119 |  | 09-06-2004 | 24 h. | 46 h. | 69 h. | 15 h. | 6 h. | 16-06-2004 | 168 hours |  |  |
| 7 | TBE2 | MBBL3067 |  | 12-06-2004 | 80 h. | 43 h. | 15 h. | 16 h. | 8 h. | 18-06-2004 | 144 hours |  |  |
| 8 | TBF1 | MBBL1101 |  | 06-06-2004 | 47 h. | 27 h. | 39 h. | 17 h. | 12 h. | 14-06-2004 | 192 hours |  |  |
| 9 | TBF2 | MBAL2059 |  | 09-06-2004 | 45 h. | 31 h. | 27 h. | 13 h. | 17 h. | 15-06-2004 | 144 hours |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAR3063 | 12008.5 A. (D1-L) | 12513 A. (D1-L-S13) | 12510 A. (D1-L) |  | - | - | - | - | - | - | - | - | - |
| 2 | MBBL3084 | 11230 A. (D2-L-S01) | 12440 A. (D1-L-S01) |  | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBL1098 | 12006 A. (D2-L) | 11998 A. (D2_L) | 12344 A. (D2_L) | 12500 A. (D1-L) |  | - | - | - | - | - | - | - | - |
| 4 | MBBL3081 | 11799 A. (D1-U-S01) | 11801 A. (D2-L-S01) | 12545 A. (D1-L-) | 12781 A. (D1-L-S01) | 12850 A. | - | - | - | - | - | - | - | - |
| 5 | MBAL2083 | 11847 A. (D1-L) | 12379 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 6 | MBBL1119 | 11350 A. (D2-U) | 11476 A. (D1_L) | 11821 A. (D1-L) | 12002 A. (D2-U) | 12200 A. (D1-L) | 12344 A. (D2_L) | 12437 A. (D2-U) | 12557 A. (D1-U) | 12612 A. (D2-L) |  | - | - | - |
| 7 | MBBL3067 | 12090 A. (D2_L) |  | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBBL1101 | 11665 A. (D2_L) | 12318 A. (D2_L) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAL2059 | 11638 A. (D2_L) | 11836 A. (D2_L) | 12006 A. (D2-L) | 12404 A. (D2-U) | 12749 A. (D2-l) | 12850 A. | - | - | - | - | - | - | - |

- General Problems last week :

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _15_M | TBD2 | WP04 forgotten. | MTM/ICS |  | Stephane informed by P.Poulnais. he advised to proceed. For SSS connection , MTM perform WP04 |
| Thursday _15_N | TBF2 | MBAL 3142: IAP at warm : error in TT821 value. Cable connected to the MM fixed rack connected in the wrong connector. | MTM |  | Cable connected in the proper position then OK. |
| Thursday _15_N | TBB1 | MBBL 1098: First quench at 12005 with value of Direct voltage close to 50 V: higher than usual. Second ramp to 12000 for the de-excitation test. It quenched at 11998. | MTM |  | Stephane informed. He checked the quenches and asked for a third ramp. Then OK. |
| Thursday _17_A | TBB2 | LF provoked quench : AQA shows 920 Amps instead of 1500 Amps. HF provoked quench was OK | MTM |  | Giorgio checked and conclude that it was due to a too short pre-trigger time. |
| Thursday _17_A | TBC2 | HV test final at cold on SSS31 with rack 2. At the second step error “Error while putting megger on remote mode “. Tried four times : same error | MTM | HV | Rack changed and problem disappeared. |
| Wednesday _16_N Thursday _17_A | TBC2 | MQT corrector could not be powered properly. Inductance seems to be different to that expected. Main quadrupole : Main power supply got faulty for currents above 5 kA. |  |  | Investigation by AB/PO expert, Giorgio, Guy and Andrejz. They found a short circuit between MQT and MQ via VT located un the clamp. |
| Thursday _17_N | TBC2 TBC1 | Warming up quench : No hf file created . Problem remains for IAP at cold in TBC1. For the file qco2, no hf file | AB/CO | Hf IAP | Giorgio advised to reset the crates before doing another quench. Test repeated . |
| Friday_18_A | TBF | PC problem: level of water too low but old configuration of the front face card | SL/PO |  | Giorgio increased the level of the water in the PC and asked first line to change the corresponding card. |
| Saturday_19_A | TBB2 | 1120 magnet : after training quench hf DAQ did not rearm. | AB/CO | hf | Giorgio found that 3 cards were not put automatically in run mode after the re-arming. |
| Saturday_19_A | TBF2 | 3142 magnet : HV test not OK: It failed for Cold Temp sensor vs ground. | MTM |  | Check by Richard Monday. NC report filled. |
| Saturday_19_A | TBB2 | 1120 magnet : warm up started instead of going to 4.4 K (procedure for sick magnets). | MTM/ ACR |  | Origin of the mis-understanding ? |
| Saturday_19_N |  | Compressors did not work properly: pumping limited. | ACR |  |  |
| Saturday_19_N | TBB2 | 1120 magnet 5th quench: wrong date and wrong time in the file. AQA says “faulty quench” because only part of the information were copied in the proper folder. | AB/CO |  | Giorgio informed. He checked the results in the sun MTA33. He confirmed the bug. |
| Sunday_20_M | TBB2 | 1120 magnet: Current ramp could not start: PC blocked on “on stand by”. Error 222 checking serial port. Done but then PC switched from “on stand by “ to “PC fault”. | SL/ PO |  | As it appeared to be a communication error, Giorgio suggested to quit the “power” application before resetting the Digital Controller or disconnecting the RS232 cable. Giorgio called first line intervention of SL/PO. The circuit breaker was damaged and replaced by first line. |
| Monday_21_M | TBA2 | 2015 magnet (shaft 24/26): Problem in rotation for aperture 1 (shaft 24). | MTM |  | Stephane informed: he checked the results. He suggested to Marco to stop the measurements in aperture 1. The origin of the problem has to be investigated. |