Vc/20-Apr-05

### Week 16  starting 18 April 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  18 April 05 @ 4/18/2005 2:04:50 PM

| 11 | A1 | MBBR3316 | PT 13.1 IAP @ Warm | 294.46 |
| --- | --- | --- | --- | --- |
| 5 | A2 | MBAL2169 | PTE Min. NRJ 3KA Diode Test | 4.32 HV |
| 7 | B1 | SSS170 | PT 3 QH Measure | 2.31 HV |
| 2 | B2 | SSS130 | PT 12 Warm Up | 6.90 |
| 10 | C1 | MBBL1111 | Prep 5 Cool Down | 279.92 |
| 6 | C2 | MBBL1218 | Prep 5 Cool Down | 1.90 |
| 1 | D1 | SSS151 | Stretched Wire Warm SW13 | 292.67 |
| 4 | D2 | SSS095 | PT 9 CDAP HV | 1.91 |
| 8 | E1 | MBBL2164 | ICS 4 Final connection | 293.21 |
| 3 | E2 | MBBL1216 | PT 6.2 Training 2 | 1.90 |
| 9 | F1 | MBAR3329 | Prep 5 Cool Down | 285.53 |
| 12 | F2 | MBBR3242 | ICS 1 WP04 HV Test Warm | 292.05 |

Temperature data are taken from TBSM18 site

Coordinator this week: V Chohan; MTM support on call :   16-3602 .

19  complete Magnet Tests cycles   ( 3636 counted twice)

12  dipoles( 1 with MM)+ 6  SSS( 0  with MM) +  0  SSSS (with MM)

Disconnected after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Situation on Repair :

General Points

        - SSS on D1 Next

        - New e-Traveller upgrades for Shafts

## Tests

| Magnets under Test from 10-04-2005 to 16-04-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | # | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |
| 1 | TBA1 | MBBL1213 |  |  | 09-04-2005 | 1 | 28 h. | 28 h. | 30 h. | 15 h. | 7 h. | 13-04-2005 | 108 h. | Stripping |  |
| 2 | TBA2 | MBAL1205 |  |  | 10-04-2005 | 1 | 38 h. | 30 h. | 25 h. | 16 h. | 8 h. | 15-04-2005 | 117 h. | Stripping |  |
| 3 | TBA2 | MBBR3307 |  |  | 04-04-2005 | 1 | 38 h. | 25 h. | 39 h. | 17 h. | 10 h. | 10-04-2005 | 129 h. | Stripping |  |
| 4 | TBB1 | SSS132 |  |  | 11-04-2005 | 1 | 21 h. | 34 h. | 16 h. | 7 h. | 12 h. | 15-04-2005 | 90 h. | Stand By |  |
| 5 | TBB1 | SSS133 |  |  | 08-04-2005 | 1 | 28 h. | 13 h. | 16 h. | 10 h. | 8 h. | 11-04-2005 | 75 h. | Stripping |  |
| 6 | TBB2 | SSS010 |  |  | 10-04-2005 | 1 | 26 h. | 17 h. | 33 h. | 17 h. | 6 h. | 15-04-2005 | 99 h. | Stripping |  |
| 7 | TBB2 | SSS092 |  |  | 05-04-2005 | 1 | 37 h. | 15 h. | 27 h. | 11 h. | 19 h. | 10-04-2005 | 109 h. | Stripping |  |
| 8 | TBC1 | MBBL3636 |  |  | 07-04-2005 | 2 | 22 h. | 37 h. | 60 h. | 16 h. | 0 h. | 13-04-2005 | 135 h. | Not Found |  |
| 9 | TBC1 | MBBL3636 |  |  | 13-04-2005 | 2 | 0 h. | 35 h. | 32 h. | 16 h. | 9 h. | 16-04-2005 | 92 h. | Stand By |  |
| 10 | TBC2 | MBAL2168 |  |  | 10-04-2005 | 1 | 30 h. | 47 h. | 19 h. | 22 h. | 13 h. | 16-04-2005 | 131 h. | Stand By |  |
| 11 | TBC2 | MBAR3320 |  |  | 05-04-2005 | 1 | 38 h. | 20 h. | 27 h. | 14 h. | 15 h. | 10-04-2005 | 114 h. | Stand By |  |
| 12 | TBD1 | SSS102 |  |  | 07-04-2005 | 1 | 39 h. | 17 h. | 17 h. | 8 h. | 23 h. | 11-04-2005 | 104 h. | Stripping |  |
| 13 | TBD2 | SSS095 |  |  | 07-04-2005 | 2 | 70 h. | 16 h. | 25 h. | 7 h. | 2 h. | 12-04-2005 | 120 h. | Not Found |  |
| 14 | TBE1 | MBBR3318 |  |  | 08-04-2005 | 1 | 29 h. | 31 h. | 18 h. | 14 h. | 6 h. | 12-04-2005 | 98 h. | Stripping |  |
| 15 | TBE2 | MBAL1208 |  |  | 10-04-2005 | 1 | 23 h. | 30 h. | 24 h. | 17 h. | 5 h. | 14-04-2005 | 99 h. | Stripping |  |
| 16 | TBE2 | MBBL2160 |  |  | 06-04-2005 | 1 | 22 h. | 26 h. | 20 h. | 16 h. | 12 h. | 10-04-2005 | 96 h. | Stripping |  |
| 17 | TBF1 | MBAR3303 |  |  | 12-04-2005 | 2 | 24 h. | 34 h. | 21 h. | 19 h. | 9 h. | 16-04-2005 | 107 h. | Stripping |  |
| 18 | TBF1 | MBBR3246 |  |  | 08-04-2005 | 1 | 25 h. | 24 h. | 23 h. | 16 h. | 11 h. | 12-04-2005 | 99 h. | Stripping |  |
| 19 | TBF2 | MBAL2153 |  |  | 09-04-2005 | 1 | 34 h. | 26 h. | 17 h. | 17 h. | 5 h. | 13-04-2005 | 99 h. | Stripping |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBL1213 | 12475 A. (D1_L) | 12626.5 A. (D2-L) | 12694 A. (D2-L) |  | - | - | - | - | - | - | - | - | - |
| 2 | MBAL1205 | 11863 A. (D1_L) | 12520 A. (D1 - U) | 12630 A. (D1 - U) |  | - | - | - | - | - | - | - | - | - |
| 3 | MBBR3307 | 12230.7 A. (D2 - U) | 12680 A. (D2-L) | 12848 A. (D2_U) |  | - | - | - | - | - | - | - | - | - |
| 4 | SSS132 | 12233.7 A. (QI_12) | 12396.4 A. (QE-34) | 12842 A. (QI_12) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS133 | 12340 A. (QI_12) | 12340 A. (QE_34) | 12458 A. (QE-34) |  | - | - | - | - | - | - | - | - | - |
| 6 | SSS010 | 11684 A. (QI-34) | 12067 A. (QI-12) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS092 | 11588 A. (QI-12) | 11782 A. (QI-34) | 11796.3 A. (QI_34) | 12196 A. (QE-12) | 12326 A. (QI-34) | 12850 A. | - | - | - | - | - | - | - |
| 8 | MBBL3636 | 9129 A. (D2_U) | 11759 A. (D2_U) | 11729 A. (D2_U) | 12004 A. (D1-U) | 12065 A. (D2_U) | 12371.7 A. (D2-U) | 12651 A. (D2-U) | 12800 A. (D2-U) | 12850 A. | - | - | - | - |
| 9 | MBBL3636 | 11011 A. (D1-L) | 12045 A. (D2_L) | 11980 A. (D2-L) | 0 A. (No Data) | 12288 A. (D2_U) |  | - | - | - | - | - | - | - |
| 10 | MBAL2168 | 12019 A. (D1-U) | 12617 A. (D2_L) | 12508 A. (D1-U) |  | - | - | - | - | - | - | - | - | - |
| 11 | MBAR3320 | 10849 A. (D2-L) | 12644.8 A. (D1-U) | 12734 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 12 | SSS102 | 11900 A. (QI - 12) | 12429 A. (QI-12) | 12540 A. (QI-34) |  | - | - | - | - | - | - | - | - | - |
| 13 | SSS095 | 12192.5 A. (QE_34) | 0 A. (No Data) | 11714 A. (QI-12) | 11897 A. (QE34) | 12791 A. (QE34) | 12850 A. | - | - | - | - | - | - | - |
| 14 | MBBR3318 | 12757.2 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 15 | MBAL1208 | 12720.3 A. (D1-L) | 11858 A. (D1_L) | 12632.9 A. (D1-L-S01) | 12856 A. | - | - | - | - | - | - | - | - | - |
| 16 | MBBL2160 | 11270.7 A. (D2 - U) | 11834.1 A. (D1-U) | 12258.5 A. (D2-U) | 12444 A. (D1-L) |  | - | - | - | - | - | - | - | - |
| 17 | MBAR3303 | 11923 A. (D2-U) | 12253 A. (D2-U) | 12572 A. (D2-U) |  | - | - | - | - | - | - | - | - | - |
| 18 | MBBR3246 | 12450 A. (D2-U-S01) | 12549 A. (D2_L_S01) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 19 | MBAL2153 | 11451 A. (D1-L) | 12087 A. (D2 - U) | 12513 A. (D2-L) |  | - | - | - | - | - | - | - | - | - |

### Week 15  :  10 April to 16 April 05  (19 Magnet Tests)

### [   3636 On bench rapid Thermal cycle   ]

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _12_N Thursday _14_N Monday_18_A | TBE2 TBE1 TBC2 | HV test - cold initial. Magnet was at 1.9K, but checks by the PLC of the HV rack (signal taken from the PLCSE) are indicating that the phase is not stable and impede to do the measurement.. HV at cold not able to run PLC error " Wrong cryo phase", though HV-OK signal is available according to Cryo operators. | ACR ACR ACR |  | Guy called and disabled the PLC check. Advise of Richard :In case of problems during HV tests, related with the cryo phase, ask the cryo OP team will look to the trends to see if the signal "Cold_HV signal" is stable. If not wait until it becomes stable. Guy, suggested to wait for more time the stability of the phase. Impossible to restart the test. Richard investigated with ACR the problem. Bug in the ACR software when two benches of the same cluster were in HCV conditions.? Same problem |
| Tuesday _12_N Wednesday _13_N | TBB2 | Rack XMTY92: BNC connector of cable nr 16 for the passive bus terminal need to be repaired. Only 2 HV racks were present, we could not locate 3rd Rack, so HV test PT9 was not launched | MTM |  | Richard removed the rack for repair. Repaired Thursday morning. Only 2 racks available Wednesday. 3 tests at the same time cannot be done. |
| Wednesday _13_M | TBA2 | Faulty quench at 40A on MBB1205 | MTM |  |  |
| Wednesday _13_N | TBC2 | Cryo OK (HV) lost during HV test (2 times) | ACR |  | Test aborted. |
| Thursday _14_M | TBC2 | Noise apparent on signals for training quench 1 on C2 MBAL2168 alarm: D1-2 Dirvt direct voltage jump exceeded 10V | MTM |  | File checked by Guy: OK to continue. |
| Thursday _14_M | TBB1 | Resistance of one quench heater of the SSS132 (those of the dummy resistors) is not correct. | MTM |  | Guy found that he discharge damaged the dummy resistor and its power supply. He changed the faulty power supply and the dummy resistors. |
| Thursday _14_A Thursday _14_N Fridday_15_M Saturday_16_A | TBD1 | SPA at 5000 A and at 11850 A. SPA during training quench | ACR? |  | Problem in the level gage in the exchanger : peak of He level in the exchanger detected. |
| Thursday _14_N Friday_15_M | TBD1 | Wire broken during FS measurement at 760 A. Idem Config. Files related to the longitudinal position of correctors are also missing. | MTM |  | Test repeated. Guy inserted the files |
| Friday _15_N | TBF1 | Magnet names on F1 and F2 are not shown on TEMA screen. Communication error “No info from UDP socket”. | AB/CO |  | Guy switched off/on the sun. |
| Friday _15_N | TBD1 | XY axis measurements in aperture 2 with the SSW system n3 give bas results (DC measurements). | AB/CO |  | OP team called Guy who came and decided to change the measurements system. The system n2 was installed. |
| Saturday _16_A | TBF2 | Not possible to launch TEMA on the server. Communication problem from the VME crate | AB/CO |  | Guy reset the crates and OK. |
| Saturday _16_N | TBD1 | Shaft not rotating correctly (sliding) in aperture 2 |  |  | Guy came and repaired the clutch. |
| Sunday _17_A | TBB1 | EF Corrector measurements on SSS170 not possible, | ICS |  | Guy suspected an inversion of voltage taps. He fixed the problem by disabling the Potaim cards of these Vtaps. |
| Monday_18_M | TBB2 | SPA during training quench | ACR |  | Too low He gaz flow for the regulation due to a too low loss in these CFB, unable maintain the current leads at correct temperature. |
| Monday_18_M | TBA1 | IAP@warm final on MB3316: error in D1,D2 values. | MTM |  | Federico checked. Faulty potaim card. Magnet OK. |
| Monday_18_M | TBD2 | Potential has been received during voltage taps disconnection (switch in CC position). To be clarified.??? | MTM |  |  |
| Monday_18_A | TBE2 | HF DAQ could not be armed. | AB/CO |  | Exit from all applications & started Tema after reseting the crates, problem solved. |