Eric VERYUNES/23-May-05

### Week 20 starting 15 May. 05

### SM18 Operation Meeting (Tuesdays)

Bench status:

LHC SM18 Magnet Test Facility

|  | A1 | MBBL3116 | PT 6.1 Training 1 | 1.95 HV |
| --- | --- | --- | --- | --- |
| 8 | A2 | MBAL1226 | ICS 4 Final connection | 295 |
| 1 | B1 | SSS253 | PT 6.6 Training 6 | 1.91 |
| 9 | B2 | SSS153 | Prep 0 Scan Bench | 296.34 |
| 5 | C1 | MBBR3266 | PT 13.2 Resist. Meas. | 298.58 |
| 6 | C2 | MBAR3350 | ICS 4 Final connection | 295.8 |
| 4 | D1 | SSS156 | Stretched Wire Cold SC11 | 1.91 |
| 7 | D2 | SSS116 | Prep 5 Cool Down | 4.67 HV |
| 12 | E1 |  |  | 296.34 |
| 10 | E2 | MBBL2181 | ICS 1 WP04 HV Test Warm | 298.04 |
| 2 | F1 | MBBR3335 | ICS 5 Traveller Last | 298.58 |
| 11 | F2 | MBBL2166 | ICS 5 Traveller Last | 295.36 |

- Coordinator this week: P. Pugnat;

- MTM support on call : G. Deferne .

- 16  Magnets Tested    : 9  dipoles ( 2 with MM, MB1182, MB1223 ) + 7  SSS (1-Thermal cycle (SSS155))

- Situation From Cryogenics:  ACR Rep.

  - Flow meter on TBA2

- Situation From Mechanics: (J.Halik)

  - Bench E1: rotating wheel.

- AOB:

  - SSS155: Origin of the non compensation found.

  - MB2166: HV test failed MB vs ground at cold.

  - TBD1: PLCSE blocked (origin, action).

  - Polarity switch: all revised last week. Procedures to be followed up carefully.

  - AQA version 6.2.

| Magnets under Test from 15-05-2005 to 21-05-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBAL1182 |  | 14-05-2005 | 36 h. | 27 h. | 39 h. | 20 h. | 9 h. | 20-05-2005 | 131 h. | Stripping |
| 2 | TBA2 | MBAR3300 |  | 11-05-2005 | 87 h. | 26 h. | 85 h. | 26 h. | 10 h. | 20-05-2005 | 234 h. | Stripping |
| 3 | TBB1 | SSS112 |  | 16-05-2005 | 33 h. | 14 h. | 15 h. | 15 h. | 7 h. | 20-05-2005 | 84 h. | Stripping |
| 4 | TBB1 | SSS196(2) |  | 13-05-2005 | 15 h. | 5 h. | 30 h. | 13 h. | 11 h. | 16-05-2005 | 74 h. | Stripping |
| 5 | TBB2 | SSS009(2) |  | 12-05-2005 | 15 h. | 31 h. | 53 h. | 10 h. | 15 h. | 18-05-2005 | 124 h. | Stripping |
| 6 | TBC1 | MBBR3334 |  | 12-05-2005 | 30 h. | 26 h. | 17 h. | 14 h. | 11 h. | 16-05-2005 | 98 h. | Stripping |
| 7 | TBC2 | MBAR3250 |  | 11-05-2005 | 19 h. | 21 h. | 20 h. | 17 h. | 12 h. | 15-05-2005 | 89 h. | Stripping |
| 8 | TBC2 | MBBL1643(2) |  | 15-05-2005 | 36 h. | 27 h. | 35 h. | 8 h. | 0 h. | 20-05-2005 | 106 h. | Thermal cycle |
| 9 | TBD1 | SSS118 |  | 15-05-2005 | 37 h. | 23 h. | 57 h. | 10 h. | 9 h. | 20-05-2005 | 136 h. | Stripping |
| 10 | TBD1 | SSS154 |  | 11-05-2005 | 26 h. | 15 h. | 22 h. | 12 h. | 22 h. | 15-05-2005 | 97 h. | Stripping |
| 11 | TBD2 | SSS155(3) |  | 13-05-2005 | 32 h. | 15 h. | 17 h. | 7 h. | 13 h. | 16-05-2005 | 84 h. | Stand By |
| 12 | TBD2 | SSS155(3) |  | 16-05-2005 | 0 h. | 70 h. | 41 h. | 5 h. | 0 h. | 19-05-2005 | 116 h. | Thermal cycle |
| 13 | TBE1 | MBBL2176 |  | 12-05-2005 | 26 h. | 31 h. | 18 h. | 15 h. | 17 h. | 17-05-2005 | 107 h. | Stripping |
| 14 | TBE2 | MBBR3313 |  | 12-05-2005 | 42 h. | 30 h. | 20 h. | 13 h. | 11 h. | 17-05-2005 | 116 h. | Stripping |
| 15 | TBF1 | MBAL3048 |  | 14-05-2005 | 34 h. | 22 h. | 25 h. | 15 h. | 11 h. | 18-05-2005 | 107 h. | Stripping |
| 16 | TBF2 | MBAL1223 |  | 12-05-2005 | 28 h. | -14 h. | 104 h. | 14 h. | 14 h. | 18-05-2005 | 146 h. | Stripping |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL1182 | 11387 A. (D1_L_S01) | 12683 A. (D1-L-S13) | 12850 A. | - | - | - | - | - | - | - |
| 2 | MBAR3300 | 8864 A. (D1_U) | 11332 A. (D1-U) | 12145 A. (D1-U) | 12451 A. (D1-U) | 12758.3 A. (D2-L) | 12828 A. (D2-L) | 12812 A. (D2-L) | 12850 A. | - | - |
| 3 | SSS112 | 12172 A. (QE-12) | 12538.3 A. (QI-12) | 12703.9 A. (QI-34) |  | - | - | - | - | - | - |
| 4 | SSS196 | 12460 A. (QI-34) | 12822.4 A. (QI-34) |  | - | - | - | - | - | - | - |
| 5 | SSS009 | 11875 A. (QI_12) | 12256 A. (QE-34) | 12291 A. (QE-34) |  | - | - | - | - | - | - |
| 6 | MBBR3334 | 11514 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - |
| 7 | MBAR3250 | 11220 A. (D1-L) | 11838 A. (D1-U) | 12574 A. (D2-U) | 12507 A. (D2-U) |  | - | - | - | - | - |
| 8 | MBBL1643 | 11266 A. (D1-L) | 11501 A. (D1_L) | 11734.8 A. (D1-L) | 11864 A. (D1-U) | 12014.5 A. (D1-L) | 12020.9 A. (D1-L) | 12083.7 A. (D1-L) | 12147 A. (D1-U) | 12216 A. (D1 - L) |  |
| 9 | SSS118 | 12374.5 A. (Q_I-34) | 12646.2 A. (Q-I-34) | 12718 A. (QI-12) |  | - | - | - | - | - | - |
| 10 | SSS154 | 11120 A. (QE-34) | 11907.8 A. (QI-34) | 12732 A. (QE-34) | 12847.1 A. (QI-34) |  | - | - | - | - | - |
| 11 | SSS155 |  | - | - | - | - | - | - | - | - | - |
| 12 | SSS155 | 11405.6 A. (QI-12) | 11717 A. (QI-34) | 11868 A. (QI-12) | 11904 A. (QI-12) | 12132.6 A. (Q-I-12) | 12236.5 A. (Q-I-12) | 12317 A. (Q-E-34) | 12372.4 A. (QI-34) | 12468 A. (QI-12) | 12489 A. (QI-34) |  |
| 13 | MBBL2176 | 10977 A. (D1-U) | 12068 A. (D1-U) | 12566 A. (D2_L) |  | - | - | - | - | - | - |  |
| 14 | MBBR3313 | 12001 A. (D1_U) | 12600 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - |  |
| 15 | MBAL3048 | 11178 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - |  |
| 16 | MBAL1223 | 11288 A. (D2-U-S13) | 11700 A. (D2_U_S13) | 12095 A. (D2_L_S01) | 12487 A. (D2_L-S13) | 12687.5 A. (D2_L-S01) | 12765.2 A. (D2_U-S13) | 12860 A. (D1_U-S01) | 12850 A. | - | - |  |

### Week  08 May 15 to 21 May 05

Thermal Cycle

Light green: Connect + Pump down

Blue :  Wait + Cool down

Ivory: Tests at Cold (36 hr)

Red :  Wait + Warm up (12 hr)

Dark Green: Disconnect (8 hr)