### Chohan /21--Nov-05

### Week 47 starting  21 Nov 05

### SM18 Operation Meeting (Tuesdays)

Bench status on Monday 21 Nov 05:

11/21/2005 2:30:21 PM

| 7 | A1 | MBAR2226 | ICS 4 Final connection | 291.6 |
| --- | --- | --- | --- | --- |
| 1 | A2 | MBAL3378 | PT 12 Warm Up | 6.03 |
| 8 | B1 | SSS149 | ICS 3 Traveller after warm test | 291.6 |
| 5 | B2 | SSS147 | PT 13.2 Resist. Meas. | 298.04 |
| 2 | C1 | MBAR2249 | PT 12 Warm Up | 281.79 |
| 3 | C2 | MBAR2246 | Prep 5 Cool Down | 88.17 |
| 9 | D1 | SSS208 | Prep 1 Lyre Test | 290.71 |
| 10 | D2 | SSS289 | PT 13.2 Resist. Meas. | 293.57 |
| 4 | E1 | MBAL1088 | Prep 5 Cool Down | 101.94 |
| 12 | E2 | MBBR3388 | Prep 0 Scan Bench | 291.96 |
| 6 | F1 | MBBL1192 | Prep 5 Cool Down | 289.1 |
| 11 | F2 | MBBR3339 | ICS 2 Connect Magnet (ICS) | 290.17 |

Coordinator this week: Nikolay; MTM support: 16-3602

18 complete Magnet Tests cycles  12 Dipoles  + 6 SSS + 0 SSSS

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

[ 2140 ROBTC ; sss277 3rd time; 2179 2nd time ]

Situation From Cryogenics:  J-P Lamboy or ACR Rep.

Special Points:

- Lots of quenches  on SSS277 ?

Results from 3139 ?

What was wrong with 2179 ?

Next Special SSS Q6 on D2 (J Halik  , Marco)  SSW @warm to start

AOB

| Magnets under Test from 13-11-2005 to 19-11-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBAL1093 |  |  | 10-11-2005 | 33 h. | 27 h. | 18 h. | 13 h. | 8 h. | 14-11-2005 | 99 h. | Stripping |
| 2 | TBA2 | MBAL3398 |  |  | 12-11-2005 | 29 h. | 21 h. | 18 h. | 15 h. | 10 h. | 16-11-2005 | 93 h. | Stripping |
| 3 | TBB1 | SSS277 |  |  | 08-11-2005 | 30 h. | 15 h. | 93 h. | 10 h. | 29 h. | 15-11-2005 | 177 h. | Stand By |
| 4 | TBB2 | SSS157 |  |  | 09-11-2005 | 32 h. | 24 h. | 18 h. | 7 h. | 36 h. | 14-11-2005 | 117 h. | Stripping |
| 5 | TBB2 | SSS225 |  |  | 14-11-2005 | 31 h. | 11 h. | 15 h. | 8 h. | 12 h. | 17-11-2005 | 77 h. | Stripping |
| 6 | TBC1 | MBAL1181 |  |  | 09-11-2005 | 28 h. | 31 h. | 14 h. | 16 h. | 15 h. | 14-11-2005 | 104 h. | Stand By |
| 7 | TBC1 | MBAR3328 |  |  | 14-11-2005 | 24 h. | 19 h. | 20 h. | 14 h. | 9 h. | 17-11-2005 | 86 h. | Stripping |
| 8 | TBC2 | MBAL3414 |  |  | 11-11-2005 | 26 h. | 21 h. | 14 h. | 19 h. | 17 h. | 15-11-2005 | 97 h. | Stripping |
| 9 | TBC2 | MBBR3364 |  |  | 16-11-2005 | 25 h. | 21 h. | 13 h. | 15 h. | 9 h. | 19-11-2005 | 83 h. | Stripping |
| 10 | TBD1 | SSS123 |  |  | 11-11-2005 | 36 h. | 13 h. | 14 h. | 8 h. | 15 h. | 15-11-2005 | 86 h. | Stripping |
| 11 | TBD2 | SSS179 |  |  | 10-11-2005 | 27 h. | 24 h. | 22 h. | 6 h. | 15 h. | 14-11-2005 | 94 h. | Stripping |
| 12 | TBD2 | SSS193 |  |  | 14-11-2005 | 29 h. | 18 h. | 16 h. | 10 h. | 10 h. | 17-11-2005 | 83 h. | Stripping |
| 13 | TBE1 | MBAR2242 |  |  | 14-11-2005 | 47 h. | 21 h. | 21 h. | 14 h. | 10 h. | 19-11-2005 | 113 h. | Stripping |
| 14 | TBE1 | MBBL2179 |  |  | 07-11-2005 | 31 h. | 21 h. | 54 h. | 16 h. | 45 h. | 14-11-2005 | 167 h. | Stand By |
| 15 | TBE2 | MBBL2140 |  |  | 07-11-2005 | 65 h. | 25 h. | 59 h. | - | - | 14-11-2005 | 149 h. | Not Found or Thermal cycle |
| 16 | TBE2 | MBBL2140 |  |  | 14-11-2005 | 0 | 23h | 10h- | 22h- | 10h- | 17-11-2005 | 65 h. | Stripping |
| 17 | TBF1 | MBAR2232 |  |  | 09-11-2005 | 28 h. | 23 h. | 25 h. | 16 h. | 25 h. | 14-11-2005 | 117 h. | Stripping |
| 18 | TBF2 | MBBR1281 |  |  | 12-11-2005 | 29 h. | 20 h. | 18 h. | 14 h. | 7 h. | 16-11-2005 | 88 h. | Stripping |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL1093 | 11582.3 A. (D1 - L) | 12542.4 A. (D2_U) | 12600.2 A. (D1_L) |  | - | - | - | - | - | - | - |
| 2 | MBAL3398 | 11789.4 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 3 | SSS277 | 10313 A. (QI_34) | 10952 A. (QI-34) | 11188 A. (QI-34) | 11027 A. (QI-34) | 11286 A. (QI-34) | 11427 A. (QI-34) | 11089.8 A. (QI34IC4) | 11522.7 A. (QE_12_) | 11610 A. (QI-34) | 11353 A. (QI-34) | 11312 A. (QI-34) |
| 3 | SSS277 | 11307.5 A. (QI_34) | 11549.4 A. (QI_34) | 11601 A. (QI_12) | 11570 A. (QI_34) | 11157.7 A. (QI-34-C4) |  |  |  |  |  |  |
| 4 | SSS157 | 11801.7 A. (QI-34) | 12004.6 A. (QE-12) | 12370.2 A. (QI_12) |  | - | - | - | - | - | - | - |
| 5 | SSS225 | 12583.9 A. (QI_34-12) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 6 | MBAL1181 | 12226.4 A. (D2_L) | 12433 A. (D2 - L) | 12777.1 A. (D2_L) |  | - | - | - | - | - | - | - |
| 7 | MBAR3328 | 11571.4 A. (D1-L) | 11871.7 A. (D1-U) | 12227.3 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - |
| 8 | MBAL3414 | 12698 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 9 | MBBR3364 | 12757 A. (D1_L) | 12849 A. | - | - | - | - | - | - | - | - | - |
| 10 | SSS123 | 12070.8 A. (QI - 12) | 12261 A. (QE-12) | 12400 A. (QI-12) |  | - | - | - | - | - | - | - |
| 11 | SSS179 | 12112.6 A. (QE-34) | 12126.6 A. (QI_12) | 12449.8 A. (QI-34) |  | - | - | - | - | - | - | - |
| 12 | SSS193 | 11852.9 A. (QI-12) | 12443.3 A. (QI-34) | 12670.3 A. (QI-12) |  | - | - | - | - | - | - | - |
| 13 | MBAR2242 | 11992.4 A. (D1-U) | 12849.4 A. (D1 - U) | 12856 A. | - | - | - | - | - | - | - | - |
| 14 | MBBL2179 | 12564.4 A. (D1_U) | 11790.2 A. (D1-U) | 12338.1 A. (D1-U) | 11846.9 A. (D1-U) | 12473 A. (D1-U) | 12649 A. (D1-U) | 12700.8 A. (D1_L) |  | - | - | - |
| 15 | MBBL2140 | 10858.8 A. (D1-U) | 11943.3 A. (D2-L) | 12705 A. (D1_U) | 11894.7 A. (D1_U) | 12771.3 A. (D1_U) | 12218.5 A. (D1-U) | 12255.1 A. (D1-U) | 12315 A. (D1_U) | 12710.7 A. (D1_U) |  | - |
| 16 | MBBL2140 | 12653.9 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 17 | MBAR2232 | 10905.7 A. (D1_U) | 11920.7 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - |
| 18 | MBBR1281 | 11369 A. (D1_U) | 12276.5 A. (D2_L) | 12297.5 A. (D1-U) |  | - | - | - | - | - | - | - |

2140 ROBTC ;  2179 2nd time round (Vjump) & lots of tests but magnet accepted anyway; SSS277  3rd time & also why so many quenches?

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Wednesday_16_M | TBC1 | Power cut. Storage down. First training quench for MB3328 was analysed in local sun. |  |  |  |
| Wednesday_16_A | TBC1 | Training quench 3 on MB3328: bump observed in the current discharge indicating that the diode is conducting. | AB/PO? |  | Guy informed. Delay in the FPA? Power converter is checked. |
| Wednesday_16_A | TBB1 | Errors in voltage taps signals displayed during IAP at warm on SSS161. | MTM |  |  |
| Wednesday_16_N | TBD1 | Leak on SSS165. | ICS? |  | Magnet re-opened. |
| Thursday_17_M | TBF1 | TT821 value not correct seen in MB3139. | MTM |  | Guy informed. He found that one connection V+ is opened. NC opened. |
| Thursday_17_A | TBA1 | MM2 on MB2201: rms of the rotation speed is above 2% on aperture 2. | MTM |  | Guy informed Stephane. He advised to continue with load-line and asked to verify if during the measurements the situation degrades. |
| Thursday_17_N | TBA2 | MB3378: Leak found in a flexible during magnet connection. | ACR |  | Wait up to the morning to repair. Solved Friday mid day? |
| Thursday_17_N | TBA1 | HV test final @4.5 K on MB2201 could not be carried out immediately because of bad temperature regulation. | ACR |  |  |
| Friday_18_M | TBB1 | SSS161:QH resistance measurement at warm: offset value slightly above the threshold with one multi-meter (0.173 ohms) of the SSS measurement rack. | MTM |  | Multi-meter changed (for the dipole) and offset in specification. |
| Friday_18_M | TBD1 | Powering of corrector IJ for the SSS165: test failed because a PC fault appeared when the current is ramped. | AB/PO? |  | Guy checked. The test passed after the changing of the power supply. Control of the power supply asked to AB/PO people. |
| Saturday_19_N | TBC1 | MB2249: Alerts during PT 5.2 (HF heater provoked quench): QH1,3 tminV<500 and QH3 Vmin>15.0 | MTM | AQA |  |
| Sunday_20_M | all | Cryo OK lost for all magnets at 1.9K. Liquefactor down. | ACR |  | OK after 5 hours. |
| Sunday_20_M | TBC1 | MB2249: Alerts on Minv and TminV for QH3 | MTM | AQA | OK by TC and Guy after checks. |
| Sunday_20_A | TBC1 | MB2249:Noise in Triggers & current in quench no.1 PT6.1. | MTM | AQA | OK by TC as there is no alert in AQA. If the noisy signals persist in the second quench he advised to stop the training and perform HV test. |
| Sunday_20_A | TBD1 | SSS165: Wrong inductance value for the circuit EF (MO) in the TEMA setting. | MTM |  | Inductance value of 3mH set manually and test performed. The setting has to be corrected. |