vc/12-Sep-03

### Week 37 starting 08 Sept 03

### SM18 Operation SCHEDULE Meeting (Tuesdays)

Schedule for this week :

| BENCH | CURRENT MAGNET | STATUS Today(09/09) | Forward look, & Next Magnet |
| --- | --- | --- | --- |
| TBA1 |  | Empty | CFU REPAIRED BY ACR GROUP – Next Magnet 2012 Expected 09 or 10 Sept. |
| TBA2 | 3028 | Being Cooled | COLd Tests start by Wednesday 10th? |
| TBC1 | 3046 | cold | After Thermal Cyc Tests & warm up & disconnection by 11th |
| TBC2 | SSS1 | Warm | Mech. Mods. To prepare for SSS1 then, Connection of SSS1 |
| TBE1 | 2018 | Disconnected but cannot be removed due to SM18 floor painting | 2018 needs removal & bring 3043 for connection |
| TBE2 | 1031 | cold | Cold Tests ; Disconnect on 10th Bring New after(2010 ?) |
| TBF1 | 2025 after F2 done? |  | Prepare For Commissioning AFTER F2 |
| TBF2 | 2025 proposed |  | Prepare For Commissioning FIRST |

- Test Coordinator this week:  P Pugnat     MTA Technician on call:  (16-3602) : Guy

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Other General Issues

- Portable Phone(s)

- Problems from Operation Last week (Stephane + Test Supervisor )

| Date | Problem | Type | Application/soft. | Action/advise |
| --- | --- | --- | --- | --- |
| Monday 1_M | IAP @warm (TBE1): one amplifier crate was not powered | MTM |  | Equip.support called Solved |
| Monday 1_A | TBA1: TT821 sensor for the 3028: during 4 wires measurement resistance circuit was found to be open. Circuit open between I+/I- | MTM | IAP | Euip.support called. Bricolage (shortening of the opened wire in the rack) |
| Monday 1_A | TBC1: Problem in the measurement of the magnetic field using shaft 24 (ap2). | MTM |  | Stephane, Marco called. Investigation on going. Stephane advised to perform full load line as well. Problem not resolved. |
| Monday 1_A | TBC1: PLC OK lost during full load line at 7000 A.Work-station blocked. | CO |  | Test aborted and repeated |
| Monday 1_N | MTF transfer file problem: create a new document. | MTM/EDMS |  |  |
| Monday 1_N | TBC1: minimum energy at 3 kA : launch thermal cycle with no Tcoil | MTM |  | . |
| Thursday 2_M | TBA1: HV test (insulation problem Dipole/earth) | MTM |  | R.Mompo and equip.support called. Disconnection of the magnet and test of the CFU. Problem in the CFU (position of the heaters modified) Change of bench for the magnet Same problem in TBA2 Solved now. |
| Thursday 2_A | TBC1: SSL at 4.2 K PLC gives not OK. Software problem: new version of appli for PLC not updated. | AB/CO |  | Resolved: old version loaded. |
| Thursday 28_A Thursday 28_N | TBC : faulty quench in the clamp (x 2) | ACR |  | Not resolved. |
| Thursday 28_A | TBE1. Communication problem in TEMA | AB/CO |  | Equip.support called. “Check communication test” launched. |
| Wednesday 3_M | TBE2 : IAP@warm unable to remove the trigger state in V_supra_ext and V_clamp _ext potaim cards | MTM |  | Equip.support called. VT1 5 lead in the CFB is open. Resolved by shorting VT1_4 with another tap. |
| Wednesday 3_M | TBE2: :IAP@warm : PLC interlock not OK. Magnet300_airX2 not OK. | ACR | IAP | Software implemented by A.Tovar not corresponding to the logic of IAP. Problem solved. |
| Thursday 4_M | TBE1:LF on line and IAP did not show proper temperature through TT821 | MTM | IAP/LF | Old version of IAP installed by equip.support. |
| Thursday 4_M | Problem for HV test for correctors (TBC1/3046) | MTM |  | Done with the megger in the plate-form. Non conformity open for 3046. |
| Thursday 4_N | TBE 2 : Intercon cannot be configured properly. | AB/CO |  | Investigation of the communication between PLCSE and server. Solved by AB/CO. New version replaced by the old version of the module of communication. |
| Friday 5_M | TBE 2 : TT821 reading not correct during 8 K instead of 50 K cool down | AB/CO |  | Bad contact in the connector |
| Friday 5_M | TBC1: voltage does not correspond to the 2 A send to the magnet. 1.9 V instead of the 12 V (at warm) | MTM |  | Magnet with Left diode. Current flow through the diode. Polarity of terminals power supply reversed. |
| Friday 5_M | TBA2: IAP @warm not started. Two of the four quench heater power cannot be reset. | MTM |  | Two cards in the safety matrix not placed in the good slot. Re by piquet. |
| Friday 5_N | TBC1: Provoked quench at 1.5 kA (1 LF). Faulty quench displayed by AQA | MTM |  | Test repeated. Then OK |
| Saturday 6_A | TBA2 (3028) : Leak in the manchette. Cool down did not start | ACR/ICS |  | Leak not localized. Cool down started. |
| Saturday 6_A | TBE2 (1031) : MIITS (36 )and Iearth too high (12 mA) | MTM |  | Test coordinator informed. |
| Saturday 6_A | TBE2 (1031) : Resistance of the cryo-heaters and temperature sensors too high. | MTM |  | Test coordinator informed. |
| Saturday 6_A | TBE2 (1031) : Lfweb.vi could not be seen in the screen and could not be re-launched from TEMA | MTM |  | TEMA re-started. |
| Sunday 7_A | TBC1 (3028) : 1.5 kA quenches (with HF) in Vbus. | MTM | ACR | Not solved. |
| Sunday 7_A | TBE2:MM: over-range in sector of the heads (sector 1) in Ap1 and sector 0607 (ap 2). | MTM |  | Bad contact (Ap1) and pin removed for a connector in Ap2. |
| Sunday 7_A | TBE2:IAP at cold. Offset errors in potaim cards and amplitude errors | MTM |  | Adjusted at the minimum possible. New range to be defined? |
| Sunday 7_A | TBE2 Tcoil . Problem with the connection of the terminals. | MTM |  | Temporary cabling present Friday. Now fixed and definitive cabling. Solved by Giorgio. |
| Sunday 7_N | TBE2 Tcoil : MM current reading is zero in aperture 2 | SL/PO |  | Problem with one card in the power supply and one cable was not working. |
| Monday 8_A | TBE2: MXI errors. At the start of the LHC cycle. | AB/CO | MMP | Reset of the crates VME |