vc/27-Nov-03

### Week 48 starting 24 nov 03

### SM18 Operation SCHEDULE Meeting (Tuesdays)

Schedule for this week :

| BENCH | CURRENT MAGNET | STATUS Today(25/11/03) | Forward look, & Next Magnet |
| --- | --- | --- | --- |
| TBA1 | NOT Active |  | Bench de-activated – preparation for D bench “Park” here 2001 ( moved from D bench ) |
| TBA2 | 1028 | Pump down? |  |
| TBC1 | 1029 | cold | 3021 next ? |
| TBC2 | SSS04 |  |  |
| TBE1 | 2027 | cold |  |
| TBE2 | 2029 | disconnection | 1032 next ? |
| TBF1 | 3065 | Connection | Arrived yesterday |
| TBF2 | 1027 | cooldown |  |

In pipeline Next 3015

Test Coordinator this week:  Marco B;  MTM  Tech. on call:  (16-3602) :

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Other General Issues

  - Hardware Recog. System implementation/use

  - AOB

Problems of Last week

| Date | Problem | Type | Application/soft. | Action/advise |
| --- | --- | --- | --- | --- |
| Tuesday 18_A | TBE2: IAP@warm (all HF) Trigger generate two files. qa01 was faulty | MTM | IAP |  |
| Tuesday 18_A | TBE2: QH measurements: MCDO is showing 1.16 ohms | MTM |  | Non conformity issued |
| Tuesday 18_N | TBF2 : Problem with the TRU Change of CPU no results | MTM/AB-CO |  | Solved Wednesday by changing a crate. |
| Tuesday 18_N | TBF2: Full load line aborted at 7800 A due to cryo OK lost. Problem during recuperation 7hrs lost | ACR |  | Repeated. Bad parameters for cryo control |
| Tuesday 18_N | TBA2 : RRR could not be performed because of no stable value of Temperature. | ACR |  |  |
| Tuesday 18_N | TBA2 : Sun MTA 1 hang: impossible to launch the warm up. |  |  |  |
| Wednesday 19_M | TBA2 : LHC cycle failed Cryo OK lost. | ACR |  | Repeated. |
| Wednesday 19_A | TBE1 : Problem on Tanticryo due to unconnected cable. | ICS |  |  |
| Wednesday 19_A | TBE2 : 78 faulty triggers files deleted from dacqdisk | MTM |  |  |
| Thursday 20_M | TBA2 (3022): QH measurements at warm forgotten. | MTM |  | Instructions given by Nick- QH resistance measured outside the SM18 |
| Thursday 20_A | TBA2 (3022) : Problem with provoked quench (all LF). Before the change of shift, change of protection LF to HF. Next shift believed that quench was wrong because the switch was not in correct position | MTM |  | See comments by Prashant. |
| Thursday 20_N Till Monday 23 _M | TBF1 (3059): HV test at cold failed (1850 V dipole vs ground) | MTM |  | Identification of the circuit and investigation step by step. Change of the IFS box… Test with portable megger… Check By A.Siemko Warm up the magnet. Non conformity created by test coordinator. |
| Friday 21_M | TBF1: HV test :problem to read the data. | AB/CO | HV | Application transferred to sun MTA 26 . |
| Friday 21_ | TBE2: Water problem on power supply “vane” for cable cooling closed . | SL/PO |  |  |
| Saturday 22_N | TBC1 (3059): IAP@cold without shaft Error in V_T cat et VT_ano | MTM |  | I |
| Sunday 23_M | TBC1: Slow power abort could not be launched. Power supply could not start. Interlock due to Tprobe in the current leads out of use. | ACR |  | Magnet warmed and then cooled down again. |
| Sunday 23_M | TBE1: Tcoil testing D1/S01 not OK | MTM |  |  |
| Sunday 23_A Sunday 23_N | TBE1: MM0: Problem in the 24 V power supply of motor 1 (card in the control module loose) Problem in b11 aperture 1 | MTM | MMP | For this aperture measurement with 13 sectors: failed Other strategy chosen: measurements from sector 2 to sector 13 . Problem with the implementation of the shift. Solved by Guy/Ewald. |
| Monday 24_A | TBF1: IAP @warm PLC errors Problem with rotary switch in CC position | MTM | IAP | Giorgio called |
| Monday 24_A | TBA2: (1028) VT resistance not OK | MTM |  | Non conformity opened. |