Vc/27-Jul-04

### Week31 starting 26 July  04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 12 july  16.20hrs

| TBA1 | MBAL3177 | ICS 3 Traveller after warm test | 299.6 |
| --- | --- | --- | --- |
| TBA2 | MBBL3189 | Prep 5 Pumping + Cool Down | 182.1 |
| TBB1 | MBBL1098 | ICS 6 Disconnect Magnet WP07 | mistake |
| TBB2 | MBAL3180 | PT 5.1 1.5 KA Quench LF | 1.9 |
| TBC1 | MBAL3172 | ICS 2 Connect Magnet (ICS) | 298.6 |
| TBC2 | SSS031 | PT 1 IAP @ cold | 1.9 |
| TBD1 | SSS023 | Prep 5 Pumping + Cool Down | 2.35 |
| TBD2 | SSS017 | FINISHED ? | 1.91 |
| TBE1 | MBBL2091 | PT 12 Warm Up | 185.5 |
| TBE2 | MBBL2035 | CRYO Needs Repair Wed 28July04 | 134.6 |
| TBF1 | MBBL1129 | PT 12 Warm Up | 192.9 |
| TBF2 | MBBL2085 | PTE Min. NRJ 3KA Diode Test | 1.9 |

7/26/2004 4:19:52 PM    Temperature data are taken from TBSM18 site

Coordinator this week: V Chohan  ; MTM support on call :  (16-3602).

11 Magnets( 9 dipoles+ 2 SSS)   Disconnected after tests last week    ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.(Jerome ?)

- Repair of E2 leak on Wed morning

Priorities & Board stickup :session for OP thurs aft.at 13.30

  - SSS work :

B Cluster Aux Power Supplies tests :richard

Bench status  and tests for now( Monday 26/7at 18.00 hrs)  & next few days :  see Video Display

| Magnets under Test on 26-07 5:54:08 PM |
| --- |
| - | Bench | Magnet | Shafts | Start | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | Last Test Desc | Time | I | Temp. | Total |
| 1 | TBA1 | MBAL3177 |  | 25-07 | 33 h. | - | - | - | - | ICS 3 Traveller after warm test | 25-07 (15 : 28) | 0 A. | 300 K | 33 hours |
| 2 | TBA2 | MBBL3189 |  | 24-07 | 46 h. | 14 h. | - | - | - | Prep 5 Pumping + Cool Down | 26-07 (03 : 18) | 0 A. | Cooling | 60 hours |
| 3 | TBB1 | MBBL1098 |  | 24-07 | 39 h. | 17 h. | - | - | - | ICS 6 Disconnect Magnet WP07 | 26-07 (10 : 25) | 0 A. | 300 K | 56 hours |
| 4 | TBB2 | MBAL3180 |  | 22-07 | 95 h. | - | - | - | - | PT 5.2 1.5 KA Quench HF | 26-07 (15 : 12) | 1500 A. | 1.9 K | 95 hours |
| 5 | TBC1 | MBAL3172 |  | 26-07 | 5 h. | - | - | - | - | ICS 2 Connect Magnet (ICS) | 26-07 (14 : 12) | 0 A. | 300 K | 5 hours |
| 6 | TBC2 | SSS031 |  | 22-07 | 69 h. | 24 h. | 3 h. | - | - | PT 2 HV Cold Test | 26-07 (16 : 55) | 0 A. | 1.9 K | 96 hours |
| 7 | TBD1 | SSS023 |  | 19-07 | 98 h. | -84 h. | 157 h. | - | - | Prep 5 Pumping + Cool Down | 23-07 (16 : 29) | 0 A. | Cooling | 171 hours |
| 8 | TBD2 | SSS017 |  | 02-07 | 178 h. | 147 h. | 251 h. | - | - | PT 9 CDAP HV | 26-07 (16 : 46) | 0 A. | 1.9 K | 576 hours |
| 9 | TBE1 | MBBL2091 |  | 21-07 | 16 h. | 88 h. | 21 h. | 5 h. | - | PT 12 Warm Up | 26-07 (12 : 59) | 0 A. | Warming | 130 hours |
| 10 | TBE2 | MBBL2035 |  | 23-07 | 37 h. | -27 h. | 63 h. | - | - | Prep 5 Pumping + Cool Down | 25-07 (05 : 44) | 0 A. | Cooling | 73 hours |
| 11 | TBF1 | MBBL1129 |  | 19-07 | 35 h. | 66 h. | 71 h. | - | - | PT 12 Warm Up | 26-07 (10 : 09) | 0 A. | 1.9 K | 172 hours |
| 12 | TBF2 | MBBL2085 |  | 21-07 | 8 h. | 8 h. | 102 h. | - | - | MM1 MM position | 26-07 (17 : 42) | 0 A. | 1.9 K | 118 hours |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL3177 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBBL3189 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBL1098 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAL3180 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 5 | MBAL3172 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS031 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS023 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 8 | SSS017 | 11325 Amp. (Q_E 12) | 11607 Amp. (QI_12) | 12095 Amp. (QI-12) | 12541 Amp. (QI-34) | 11431 Amp. (No Data) | 12850 Amp. () | - | - | - | - | - | - | - |
| 9 | MBBL2091 | 11983 Amp. (D2_U) | 12859 Amp. () | - | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBL2035 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 11 | MBBL1129 | 12217 Amp. (D2_L-S01) | 12589 Amp. (D2_U_s13) |  | - | - | - | - | - | - | - | - | - | - |
| 12 | MBBL2085 |  | - | - | - | - | - | - | - | - | - | - | - | - |

# Results by Week for PREVIOUS week

## Tests

| Magnets under Test from 18-07-2004 to 24-07-2004 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA2 | MBAR1137 |  | 16-07-2004 | 51 h. | 65 h. | 71 h. | 20 h. | 11 h. | 24-07-2004 | 192 hours |  |  |
| 2 | TBB1 | MBAL3176 |  | 18-07-2004 | 28 h. | 61 h. | 21 h. | 19 h. | 9 h. | 24-07-2004 | 144 hours |  |  |
| 3 | TBB1 | MBAL3181 |  | 13-07-2004 | 31 h. | 31 h. | 29 h. | 14 h. | 13 h. | 18-07-2004 | 120 hours |  |  |
| 4 | TBB2 | MBAR2036 |  | 17-07-2004 | 28 h. | 44 h. | - | - | - | 22-07-2004 | 120 hours |  |  |
| 5 | TBC1 | MBAR3026 |  | 12-07-2004 | 24 h. | 95 h. | 20 h. | 19 h. | 11 h. | 19-07-2004 | 168 hours |  |  |
| 6 | TBC2 | SSS024 |  | 07-07-2004 | 67 h. | 50 h. | 224 h. | 14 h. | 21 h. | 22-07-2004 | 360 hours |  |  |
| 7 | TBD1 | SSS020 |  | 25-06-2004 | 136 h. | 88 h. | 290 h. | 12 h. | 24 h. | 18-07-2004 | 552 hours |  |  |
| 8 | TBE1 | MBAL3179 |  | 15-07-2004 | 36 h. | 50 h. | 27 h. | 17 h. | 9 h. | 21-07-2004 | 144 hours |  |  |
| 9 | TBE2 | MBAL3149 |  | 17-07-2004 | 21 h. | 53 h. | - | - | - | 23-07-2004 | 144 hours |  |  |
| 10 | TBF1 | MBBL3187 |  | 14-07-2004 | 18 h. | 61 h. | 20 h. | 19 h. | 6 h. | 18-07-2004 | 96 hours |  |  |
| 11 | TBF2 | MBBL3128 |  | 13-07-2004 | 22 h. | 117 h. | - | - | - | 21-07-2004 | 192 hours |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAR1137 | 12181 A. (D1-U) | 12357 A. (D1-L) | 12703 A. (D2_L) |  | - | - | - | - | - | - | - | - | - |
| 2 | MBAL3176 | 11800 A. (D1-U) | 12094 A. (D1-U) |  | - | - | - | - | - | - | - | - | - | - |
| 3 | MBAL3181 | 12085 A. (D1-U) | 12334 A. (D1-U) |  | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAR2036 | 11424 A. (D1_L_MRB) | 12034 A. (D1-U-??) | 12572 A. (D2_L) |  | - | - | - | - | - | - | - | - | - |
| 5 | MBAR3026 | 12851 A. (D2-L) | 12851 A. | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS024 | 11599 A. (QE_34-12) | 11819 A. (QE_34-12) | 12580 A. (QE-12) | 12579 A. (QI-12) | 12820 A. (QI-12) | 12793 A. (QI-34) | 12850 A. | - | - | - | - | - | - |
| 7 | SSS020 | 11197 A. (I-12 s6) | 12059 A. (E-34-S04) | 12149 A. (QI-12-S4) | 12470 A. (QE 34) | 12706 A. (QI-12) | 12699 A. (QE-34) | 12850 A. | - | - | - | - | - | - |
| 8 | MBAL3179 | 10445 A. (D2-U) | 11711 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAL3149 | 9546 A. (D1-U) | 12523.1 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBL3187 | 10913 A. (D1 U) | 12391 A. (D2_U) |  | - | - | - | - | - | - | - | - | - | - |
| 11 | MBBL3128 | 11715 A. (D1 U) | 12798 A. (D2 L) |  | - | - | - | - | - | - | - | - | - | - |

General Problems last week :

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_20_N | TBE2 | IAP@Cold. At the first attempt, HF files were not created, LF was created OK. At the second attempt (after resetting the crates) HF files were created, but with the time stamp of the previous LF files! Subsequent attempts were synchronised. | MTM |  | Switch off the water for another cluster, reset the PC, then switch on the water again. |
| Tuesday_20_N | Any | Several quenches produced WARNINGS about DirVT voltage Jumps exceeding 6V: TBB2 2036 G0407210343.a01 TBA1 1136 D0407202211.a07 TBE2 3149 E0407210428.ka01 Is this just a coincidence? Maybe it should be checked. | MTM |  | If this pick of voltage are high inform test coordinator. For Information: The average of Ansaldo is 6V. Alstom and Noel are around 2V. (By Eric FLOCH) |
| Tuesday_20_N | TBD2 | SSS 023: comment by Federico: the connector C11 that was hard to (un)plug has been changed. | MTM |  | Some storage of this connector are require. |
| Thursday_22_M | TBB1 | Quench during PTE (Diode Test), perhaps the ramp at 50A/s, quench the magnet. | OP |  | Ramp rate changed to 20A/s & done the test manually. |
| Thursday _22_A | TBD2 | Lead Temperature interlock when starting a test. The current leads are extremely hot. Cryo called their piquet to fix the problem. | CRYO |  | Ask Cryo specialist? |
| Thursday _22_N | TBB1 | When PT8 was launched in B1, there was a small quench. The temperature of the magnet did not increase. The test was immediately launched again and was completed successfully. | OP |  | ? Per haps Ramp rate problem. |
| Friday_23_M | TBC2 | SSS031:HV @ Warm Initial test failed while executing the step " Sextapole Vs M(x) - M(x) - F Correctors". Message appeared was " Applied voltage has passed 10% of the pecified value". | OP |  | ? |
| Friday _23_M | TBC2 | HVtest "Warm before connection" re-done with the corrector leads disconnected. | ICS |  | E-traveller problem because dipole secance is not the same than SSS. |
| Friday _23_A | TBD | There is a water interlock fault coming from the power converter, actually the flow is 50L/min but the interlock does not reset. Federico called AB-PO standby support 16.36.68 for intervention, he is coming later on | PO |  | Check and adjusted by PO support. |
| Friday _23_N | TBF1 | Problem with HW rec system while launching IAP@cold-T-coil test. Config file contain ORACLE errors HW stopped because of an "invalid count of equipment having hcxmtc_017-cr000006 as parent", | IT/MTM |  | Federico edited files manually and try to correct the errors that were related to the sectors S1819 (D1S10). test is going on. |
| Friday _23_N | All cluster | Cryo problem temperature problem with CWU2, the cryo piquet has called and he will come tomorow morning to check that. The CWU1 works but the capacity is limited at only 1 magnet to cooling down and warming up. | CRYO |  | Ask Cryo specialist? |
| Friday _23_N | TBC1 | During PTE, a quench occurred at 147 A. The test was conducted by manually ramping the current to 3000 A at 20 A/s (50 A/s is the default value when the test is launched by TEMA |  |  | Ramp rate changed to 20A/s & done the test manually. |
| Friday _23_N | All cluster | Cryo problem temperature problem with CWU2, the cryo piquet has called and he will come tomorow morning to check that. The CWU1 works but the capacity is limited at only 1 magnet to cooling down and warming up. | CRYO |  | Ask Cryo specialist? |
| Friday _23_N | TBD2 | TBD2: SPA happened during 2nd measurement. | CRYO |  | Cryo OK lose during measurement. |
| Saturday _24_M | TBC1 | Tau jump too high in LF IAP@warm. |  |  | ? |
| Saturday _24_N | TBF1 | TBF1 : Min energy @ 3000 A. Few seconds after reaching 3000 Amps current ramped down and after reaching zero ramped to 3000 Amps automatically. Printout for IDCCT_LF during this period enclosed in shift log book. | CO |  | Ramp rate changed to 20A/s & done the test manually. |
| Saturday _24_N | TBF1 | Min NRJ test @3000A. AQA Warning : I_earth abnormal signal shape, D1-2 : DirVT voltage Jump exceeded 6 V, Vmin out of time frame, However there is no AQA alerts for training quench. | MTM |  | Check by specialist. |
| Saturday _24_N | TBD1 | During SSW cold measurements towards the end of the test current in MQ ramped down automatically to '0' from 5000 A. Reason unknown. Magnet powered again and test repeated. |  |  | Reason unknown. |
| Sunday_25_M | TBB1 | MBBL 1098, the problem of sensor TT821 is confirmed, Federico checked the input of LF DAQ (V.input = 5.9V, V.range = 6.2V). On connector C10 of the magnet the resistance between pins 1,2 = 178.4 Ohm and between pins 5,6= open (pin 5 is ok, but pin 6 is open) | MTM |  | Federico intervention. |
| Sunday_25_A | TBE1 | MBBL2091: While launching PT4 (SPA), PC main fault occured due to water supply problem even though water flow looked to be adequate. Water supply to Cluster C was stopped and subsequently after resetting PC locally, fault got cleared. | MTM |  |  |
| Sunday_25_A | TBF2 | Min NRJ @3000 Amps. AQA Warning : D1-2 : DirVT voltage Jump exceeded 6 V, Vmin out of time frame, These warnings are similar to that appeared for same test on F1 bench the previous day | MTM |  | Test coordinator was inform. |
| Sunday_25_N | TBE1 | Min NRJ @3000 Amps. AQA Warning : I_earth abnormal signal shape D1-2 : DirVT voltage Jump exceeded 6 V, QH1-4 Vmin out of time frame, These warnings are similar to that appeared for same test on F1 bench the previous day & F2 bench today | MTM |  | Test coordinator was inform. |
| Sunday_25_N | TBB2 | HVtest with rack SMTP.MY92. Switchbox error, some relays not in correct position. Rack changed and test ok | MTM |  | Equipment Support. |
| Monday_26_M | TBF2 | Note about MM, the HW system will probably give an error related to the settings files later on, it is due to an ORACLE error into MTF for shatf #26, should it appear, call eq. support, he will come to correct the files manually. | MTM |  | Equipment Support. |
| Monday _26_M | TBB1 | It was a mistake that this magnet came back - was tested already in June.Magnet still at 300K. Tests terminated after Prep3 (HV Insul after bolting ) /Vacuum broken by Cryo now/ V.Chohan |  |  |  |
| Monday_27_A | All cluster | The traveller is not possible to signed cooling down of A1, signed is refuse | OP |  | The problem was resolved in the end of the day. |
| Monday_27_A | TBD2 | HV blocked in Cryogenic heater vs Ground. | MTM |  | Equipment support was inform |