Eric VERYUNES/13-Jun-05

### Week 21 starting 22 May. 05

### SM18 Operation Meeting (Tuesdays)

Bench status:

LHC SM18 Magnet Test Facility

| 7 | A1 | MBAR3298 | ICS 2 Connect Magnet (ICS) | 299.65 |
| --- | --- | --- | --- | --- |
| 2 | A2 | MBAR3344 | MM3 Full Load Line | 1.90 |
| 5 | B1 |  |  | 299.11 |
| 1 | B2 | SSS197 | PT 12 Warm Up | 245.91 |
| 8 | C1 | MBBL2179 | Prep 5 Cool Down | 4.55 HV |
| 9 | C2 | MBBR3338 | Prep 1 Lyre Test | 299.02 |
| 3 | D1 | SSS156 | PT 12 Warm Up | 299.2 |
| 10 | D2 | SSS613 | PTE 3 Correctors Powering | 1.90 |
| 11 | E1 | MBAR3346 | ICS 4 Final connection | 299.56 |
| 6 | E2 | MBAR3327 | PT 1 IAP @ cold | 1.90 |
| 4 | F1 | MBAL3147 | PT 13.2 Resist. Meas. | 300.28 |
| 12 | F2 |  |  | 297.59 |

- Coordinator this week: J. Miles;

- MTM support on call : F. Chuisano.

- 19  Magnets Tested    : 13  dipoles ( 1 with MM, MB3116 ) + 6  SSS (2-Thermal cycle (SSS253, SSS155)).

- Situation From Cryogenics:  ACR Rep.

- Situation From Mechanics (J.Halik).

-silver shoe change in TBF2.

- SSS613.

- AOB:

-Connection of Dipole Orbital corrector, the cable insulation provoked some damage on the current lead (Cluster B).

| Magnets under Test from 22-05-2005 to 28-05-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBBL3116 |  | 20-05-2005 | 38 h. | 28 h. | 32 h. | 17 h. | 11 h. | 25-05-2005 | 126 h. | Stripping |
| 2 | TBA2 | MBAL1226 |  | 20-05-2005 | 77 h. | 22 h. | 20 h. | 22 h. | 8 h. | 27-05-2005 | 149 h. | Stripping |
| 3 | TBB1 | SSS253(2) |  | 20-05-2005 | 39 h. | 14 h. | 32 h. | 10 h. | 0 h. | 24-05-2005 | 95 h. | Thermal cycle |
| 4 | TBB1 | SSS253(2) |  | 24-05-2005 | 9 h. | 64 h. | 14 h. | 14 h. | 10 h. | 26-05-2005 | 111 h. | Stripping |
| 5 | TBB2 | SSS111 |  | 18-05-2005 | 29 h. | 28 h. | 27 h. | 8 h. | 13 h. | 23-05-2005 | 105 h. | Stripping |
| 6 | TBB2 | SSS153 |  | 23-05-2005 | 33 h. | 20 h. | 21 h. | 7 h. | 14 h. | 27-05-2005 | 95 h. | Stripping |
| 7 | TBC1 | MBBL2175 |  | 24-05-2005 | 22 h. | 33 h. | 18 h. | 14 h. | 10 h. | 28-05-2005 | 97 h. | Stripping |
| 8 | TBC1 | MBBR3266(2) |  | 16-05-2005 | 23 h. | 24 h. | 58 h. | 24 h. | 0 h. | 22-05-2005 | 129 h. | Thermal cycle |
| 9 | TBC1 | MBBR3266(2) |  | 22-05-2005 | 0 h. | 14 h. | 11 h. | 14 h. | 20 h. | 24-05-2005 | 59 h. | Stripping |
| 10 | TBC2 | MBAR3350 |  | 22-05-2005 | 28 h. | 20 h. | 16 h. | 17 h. | 12 h. | 26-05-2005 | 93 h. | Stripping |
| 11 | TBC2 | MBBL1643(2) |  | 20-05-2005 | 8 h. | 24 h. | 11 h. | 15 h. | 10 h. | 22-05-2005 | 68 h. | Stripping |
| 12 | TBD2 | SSS116 |  | 22-05-2005 | 27 h. | 19 h. | 38 h. | 14 h. | 9 h. | 26-05-2005 | 107 h. | Stripping |
| 13 | TBD2 | SSS155(3) |  | 19-05-2005 | 0 h. | 18 h. | 15 h. | 8 h. | 14 h. | 22-05-2005 | 55 h. | Stand By |
| 14 | TBE1 | MBBR3332 |  | 17-05-2005 | 32 h. | 22 h. | 30 h. | 14 h. | 46 h. | 23-05-2005 | 144 h. | Stripping |
| 15 | TBE2 | MBBL2181 |  | 23-05-2005 | 20 h. | 24 h. | 41 h. | 13 h. | 13 h. | 28-05-2005 | 111 h. | Stripping |
| 16 | TBE2 | MBBL3040 |  | 17-05-2005 | 49 h. | 47 h. | 19 h. | 14 h. | 7 h. | 23-05-2005 | 136 h. | Stand By |
| 17 | TBF1 | MBAL3147(2) |  | 23-05-2005 | 25 h. | 24 h. | 54 h. | 7 h. | 0 h. | 28-05-2005 | 110 h. | Thermal cycle |
| 18 | TBF1 | MBBR3335 |  | 18-05-2005 | 28 h. | 37 h. | 33 h. | 12 h. | 9 h. | 23-05-2005 | 119 h. | Stripping |
| 19 | TBF2 | MBBL2166 |  | 18-05-2005 | 27 h. | 28 h. | 18 h. | 19 h. | 39 h. | 23-05-2005 | 131 h. | Stand By |
| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| 1 | MBBL3116 | 10441 A. (D2_U_S11) | 12235 A. (D2_U_S02) | 12537 A (D2-U-S01) |  | - | - | - | - | - | - |
| 2 | MBAL1226 | 12395 A. (D1_L) | 12700 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - |
| 3 | SSS253 | 11504.8 A. (QE_12) | 11640 A. (QI-12) | 12107 A (QE_12) | 12338 A (QI_34) | 12428.5 A (QI-34) | 12526.1 A (QE-12) | 12612.8 A (QE-12) | 12633.4 A (QE-12) | 12557 A (QE-12) |  |
| 4 | SSS253 | 11975.6 A. (QE_12) | 12211 A. (QI-34) |  | - | - | - | - | - | - | - |
| 5 | SSS111 | 11476 A. (QI-34) | 12370 A. (QE-12) | 12216 A (QE-12) | 12279 A (QE-34) | 12411 A (QE-34) | 12327.5 A (QE-34) |  | - | - | - |
| 6 | SSS153 | 11655 A. (QI_34) | 12385 A. (QI-34) | 12550 A (QI-12) |  | - | - | - | - | - | - |
| 7 | MBBL2175 | 11262 A. (D2 - U) | 12460 A. (D1 - L) | 12596 A (D1-U) |  | - | - | - | - | - | - |
| 8 | MBBR3266 | 10439 A. (D2-L) | 11975.6 A. (D2-L) | 12084 A. (D2 - L) | 12582 A. (D1-U) | 12640 A. (D1-U) | 12589.4 A. (D2_U) | 12706.2 A. (D2_U) | 12756.5 A. (D2_L) | 12835 A. (D1_U) |  |
| 9 | MBBR3266 | 12013 A. (D1-L) | 12651 A (D1-U) |  | - | - | - | - | - | - | - |
| 10 | MBAR3350 | 8839 A. (D2-L) | 10789 A (D1-U) | 12259 A. (D2-L) | 12531 A. (D2-U) |  | - | - | - | - | - |
| 11 | MBBL1643 | 12115.6 A. (D1-U) | 12264.8 A (D1-L) |  | - | - | - | - | - | - | - |
| 12 | SSS116 | 11668.8 A. (QI_12) | 12300 A (QE_12) | 12515.5 A. (QE_12) |  | - | - | - | - | - | - |
| 13 | SSS155 | 11549 A. (QI-12) | 12100 A. (QI-12) |  | - | - | - | - | - | - | - |
| 14 | MBBR3332 | 10765 A. (D2-L) | 11261 A (D1-U) | 11827 A. (D1-L) | 12121 A. (32) | 12448.9 A. (D1_U) | 12836 A. (D2_L) | 12858 A. | - | - | - |
| 15 | MBBL2181 | 10699.8 A. (D1-L) | 10951.1 A (D2-L) | 11875 A. (D2_L) | 12027 A. (D2-L) | 12393 A. (D2 - U) | 12578 A. (D1-L) | 12614 A. (D2-U) | 12644.9 A. (D2_L) | 12850 A. | - |
| 16 | MBBL3040 | 11508.1 A. (D2_U) | 12263.5 A. (D2-U) | 12563.2 A. (D2_U) |  | - | - | - | - | - | - |
| 17 | MBAL3147 | 9875 A. (D2_L) | 11820 A. (D2 - L) | 11965 A. (D1-U) | 12028.2 A. (D2_U) | 12450 A. (D1-U) | 12559.7 A. (D1_U) | 12679 A. (D1_U) | 12771.8 A. (D1-U) | 12849 A. (D2-U) |  |
| 18 | MBBR3335 | 11569.1 A. (D2-U) | 11814.2 A. (D1-U) | 12013 A. (D2-L) | 12244.6 A. (D1-U) | 12475.4 A. (D1-U) | 12727 A. (D1_U) | 12861 A. | - | - | - |
| 19 | MBBL2166 | 10332 A. (D2_U) | 11773 A. (D1_U) | 12758 A. (D1_L) |  | - | - | - | - | - | - |

### May 22 to 28 May 2005

Thermal Cycle

Light green: Connect + Pump down

Blue :  Wait + Cool down

Ivory: Tests at Cold (36 hr)

Red :  Wait + Warm up (12 hr)

Dark Green: Disconnect (8 hr)

With a good connection, the current leads are damaged, because of Hardware not compatible with this current lead.

Insulation make a deformation each time for cluster B.

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _24_A | TBD1 | SSS156:Potaim card sextupole in-ext always triggering. | ICS |  | Giorgio and A.Stafiniak made investigations. |
| Tuesday _24_A | TBC1 | MB3350: diode signal no present after diode test. | MTM |  | Check if diode is present or not. But diode file not updated. |
| Wednesday_25_M | TBD2 | HV/PLCSE communication error.. | AB/CO? |  | Guy disabled the PLCSE to perform a check. |
| Wednesday_25_N | TBF1 | Potaim card damaged. Offset could not be compensated. | AB/CO? |  | Guy disabled the PLCSE to perform a check. |
| Wednesday_25_N | TBB2 | Cooling down under 2 K of SSS not possible | ACR |  | Exchanger problem?. |
| Friday_27_M | TBD2 | SSS613: ICS complained that they could not connect the cable for powering correctors because they are too short. | MTM |  | Guy informed. He said that the power test of the corrector is not necessary? |
| Friday_27_A | TBB2 | Triggers on potaim cards on SSS153 | ICS |  | Giorgio found that the clamp was not correctly done. ICS was informed to investigate and rectify the problem. |
| Friday_27_N | TBF1 | SSL on MB3147: quench at 10340A | MTM |  | TC advised to continue with the warm up for a thermal cycle. |
| Friday_27_N | TBB1 | IAP corrector check could not be launched due to "Mag300air" PLCSE interlock. Cryo confirmed that The magnet is in "air" condition. | MTM |  | Test was run locally to bypass the error. |
| Friday_27_N | TBD1 | IAP@cold: HW recognition found config. files missing, and T-Coil converted readings were showing zero in LF hardware diagnostics. | MTM |  | Guy informed.. He solved the problem with the "Retry" button on the HW Recognition error window. This forced a regeneration of the configuration files. |
| Saturday_28_M | TBA1 | IAP @ cold :D1-L-U could not be adjusted : 151 mV (Limit 150mV) | MTM | IAP | Restarted application in control room and local machine. Quench heaters discharged when the training was launched. Spurious file was generated. |
| Saturday_28_M | TBD1 | MM2: Some sectors don't have data. Oracle problem?. | IT? |  | Guy informed. He tried to lunch manually the test. |
| Saturday_28_M | TBA1 | Temperature anticryostat not OK | MTM |  | During the scanning, the anticryostats were reversed. |
| Saturday_28_A | TBA1 | Hf DAQ not getting armed | AB/CO | hf | Restarted application in control room and local machine. Quench heaters discharged when the training was launched. Spurious file was generated. |
| Saturday_28_N | TBD1 | MM on sextupole circuit: not possible from TEMA Ramp at 2 A/s instead of 5 A/s | MTM | HWREC | Errors in configuration files. Setting changed by Guy. |
| Saturday_28_N | TBC1 | Quench at 12850 A in the bus bar (Vbus_int). | ACR |  | Helium flow in the current leads increased . |
| Saturday_28_N | TBC1 | During PLCSE in the wrong state: leds on the CPU module flashing. The intercon box seems not to work. 3 potaim cards triggered the quench. | MTM |  |  |
| Sunday_29_A |  | XMT.MY93 HV rack is not working. The megger seems to be getting the power, but the PLC does not switch on | MTM |  |  |
| Sunday_29_N | TBA2 | Quench in the bus –bar when ramping at 50 A/s | MTM |  | Trial at 40 A/s. OK |
| Sunday_29_N | TBA2 | MM positioning not performed because wrong shaft name in the setting, | MTM | MMP | Test went on with power test. |
| Sunday_29_N | TBB2 | File for second training quench not available on Vol12 server. | AB/CO |  | File available on the local SUN server. |
| Monday_30_M | TBA2 | Quench ? (Discharge of the heaters) when power converter is going in the status “ on stand by”. | MTM |  | Federico solved the problem. |
| Monday_30_M | TBB2 | Communication problem with the PLCSE. Unable to launch the training. | MTM |  | Federico solved the problem. |
| Monday_30_A | TBE2 | Lf DAQ not armed: "arm error 1 and 2". | AB/CO |  | Adrian called. Bad contact for one card found.. |