### Week 18 starting 01 May 06

### SM18 Operation Meeting (Tuesdays) 2 May 06

Bench status  on Monday  01-05-2006 at: 5/1/2006 11:03:24 AM

| 12 | A1 |  |  | 299.47 |
| --- | --- | --- | --- | --- |
| 3 | A2 | MBAL1387 | ICS 5 Traveller Last | 299.65 |
| 5 | B1 | SSS182 | PT 9 CDAP HV | 1.90 |
| 1 | B2 | SSS232 | ICS 3 Traveller after warm test | 299.65 |
| 2 | C1 | MBBL2180 | CR 1 Leak Test | 298.04 |
| 8 | C2 | MBAR1323 | PT 1 IAP @ cold | 1.91 |
| 11 | D1 | SSS636 | Cryo problem | 298.31 |
| 9 | D2 | SSS609 | PT 1 IAP @ cold | 2.35 |
| 7 | E1 | MBAR2317 | PT 14 Magnet MAPS | 300.82 |
| 4 | E2 | MBAR2236 | PT 12 Warm Up | 260.22 |
| 10 | F1 | MBBR1344 | Prep 5 Cool Down | 62.88 |
| 6 | F2 | MBAR1297 | PT 6.1 Training 1 | 7.81 |

Supervisor: stephane/        Eq support : 16-3602 :

14 Magnet Tests completed :  8 Dipoles (),    5 Arc-SSS  ( 182 to be  REPEATed)

:		 1 500-series ( 503 )

:							 0  600-series (  )

- { D1:636 Leak problems: waited whole weekend 22-23April till Mon 24th ..no luck  Now disconnected since Friday 28th but could not be moved }waiting for 635 on D1

- ROCLA ACCIDENT LAST Wednesday evening 26 -4-06: blocked usage till Safety green light (24 hrs) + not able to access to A cluster at all ;	Final removal from front of A2 on Friday 28th evening; we were blocked for removals also for cluster E,F( & D) because ROCLA could not be used neither from outside big door Jura end ..due to outside metal floor goodness ?

General Points :

- C Cluster & Output !! no dipole magnets done yet  after 1 week of changeover!!

Need Arc-SSS buffer of  ‘to test’ magnets as well as for  ‘non-MM’  SSSS

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- News /Situation from (SSS, SSSS)  :  J Halik

- Situation SSSS  :OP issues :

- A.O.B.

| Magnets under Test from 23-04-2006 to 29-04-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBAR2323 |  |  | 21-04-2006 | 32 h. | 29 h. | 23 h. | 15 h. | 15 h. | 26-04-2006 | 114 h. | Stripping |  |  |
| 2 | TBA2 | MBAR1272 |  |  | 19-04-2006 | 34 h. | 21 h. | 56 h. | 22 h. | 10 h. | 25-04-2006 | 143 h. | Stripping |  |  |
| 3 | TBB1 | SSS182 |  |  | 25-04-2006 | 25 h. | 21 h. | - | - | - | 29-04-2006 | 83 h. | Not Found or Thermal cycle |  |  |
| 4 | TBB1 | SSS322 |  |  | 21-04-2006 | 30 h. | 16 h. | 15 h. | 13 h. | 19 h. | 25-04-2006 | 93 h. | Stripping |  |  |
| 5 | TBB2 | SSS247 |  |  | 22-04-2006 | 29 h. | 12 h. | 32 h. | 22 h. | 10 h. | 26-04-2006 | 105 h. | Stripping |  |  |
| 6 | TBC1 | SSS291 |  |  | 20-04-2006 | 30 h. | 19 h. | 22 h. | 7 h. | 11 h. | 24-04-2006 | 89 h. | Stripping |  |  |
| 7 | TBC2 | SSS246 |  |  | 20-04-2006 | 29 h. | 25 h. | 33 h. | 8 h. | 43 h. | 26-04-2006 | 138 h. | Stripping |  |  |
| 8 | TBD2 | SSS503 |  |  | 20-04-2006 | 49 h. | 15 h. | 28 h. | 7 h. | 22 h. | 25-04-2006 | 121 h. | Stripping |  |  |
| 9 | TBE1 | MBBL1236 |  |  | 18-04-2006 | 32 h. | 22 h. | 42 h. | 13 h. | 11 h. | 23-04-2006 | 120 h. | Stand By |  |  |
| 10 | TBE1 | MBBL2180 |  |  | 23-04-2006 | - | - | - | - | - | 25-04-2006 | 37 h. | Not Found or Thermal cycle |  |  |
| 11 | TBE2 | MBAR2236 |  |  | 24-04-2006 | 34 h. | 26 h. | 32 h. | 16 h. | 0 h. | 29-04-2006 | 108 h. | Not Found or Thermal cycle |  |  |
| 12 | TBE2 | MBBR1313 |  |  | 19-04-2006 | 24 h. | 19 h. | 55 h. | 14 h. | 9 h. | 24-04-2006 | 121 h. | Stripping |  |  |
| 13 | TBF1 | MBBR2298 |  |  | 22-04-2006 | 29 h. | 22 h. | 28 h. | 15 h. | 49 h. | 28-04-2006 | 143 h. | Stripping |  |  |
| 14 | TBF2 | MBAR1336 |  |  | 20-04-2006 | 26 h. | 25 h. | 32 h. | 5 h. | 3 h. | 24-04-2006 | 91 h. | Stripping |  |  |
| 15 | TBF2 | MBBR2283 |  |  | 24-04-2006 | 28 h. | 19 h. | 21 h. | 15 h. | 6 h. | 28-04-2006 | 89 h. | Stripping |  |  |
| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| 1 | MBAR2323 | 12074.3 A. (D2_L) | 12853 A. | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR1272 | 12729 A. (D2_L) | 12852.2 A. (D1_L) | 12852 A. | - | - | - | - | - | - | - | - | - | - |
| 3 | SSS182 | 10786.3 A. (QE_34) | 11754.8 A. (QE_34) | 12070.6 A. (QE_34) | 12211.3 A. (QE_12) | 12298 A. (QE_34) | 12432.4 A. (QE_34) | 12422.9 A. (QE_34) | 12553.3 A. (QE_12) | 12642.5 A. (QE_12) |  | - | - | - |
| 4 | SSS322 | 10950 A. (No Data) | 11983 A. (QI_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 5 | SSS247 | 12525.8 A. (QE_12) | 12853 A. | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS291 | 11956.2 A. (QE-12) | 12817 A. (QE_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS246 | 12225.7 A. (QI-12) | 12416.7 A. (QE_34) |  | - | - | - | - | - | - | - | - | - | - |
| 8 | SSS503 | 11854.3 A. (QE_34) | 12277.7 A. (QE_12) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | MBBL1236 | 10890.1 A. (D1_L) | 11941 A. (D2_U) | 12134 A. (D1_L) | 12296.8 A. (D1_U) | 12467.2 A. (D1_L) | 12573.9 A. (D2_U) | 12720.8 A. (D1_U) | 12652 A. (D1_L) | 12702 A. (D1-L) |  | - | - | - |
| 10 | MBBL2180 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 11 | MBAR2236 | 11881.3 A. (D2_L) | 12403.1 A. (D1_U) | 12247.9 A. (D1_U) | 11843.7 A. (D1_U) | 11403.3 A. (D1_U) | 11069.1 A. (D1_U) | 11492.3 A. (D1_U) | 12614 A. (D2_U) |  | - | - | - | - |
| 12 | MBBR1313 | 12272 A. (D1-U) | 12633.4 A. (D2-U) | 12708.4 A. (D2-L) |  | - | - | - | - | - | - | - | - | - |
| 13 | MBBR2298 | 10422.8 A. (D1-U) | 12263 A. (D1 - U) | 11030 A. (D2-U) | 12574.8 A. (D1_L) | 12669.9 A. (D2_L) | 12728.6 A. (D1-U) | 12829.5 A. (D1_U) | 12850 A. | - | - | - | - | - |
| 14 | MBAR1336 | 11992 A. (D2-U) | 12289.4 A. (D1-L) | 12404 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |
| 15 | MBBR2283 | 11448.8 A. (D2_U) | 12182.5 A. (D1_L) | 12334 A. (D2_L) |  | - | - | - | - | - | - | - | - | - |

No  600 series at all this week;  ROCLA Accident effect for removal on 2298 ( on F  cluster) ; To dipole Conversion for C cluster on SSS246

SSS182 Thermal cycle;  2180 on E was removed because HV failure after Connection( before was ok!); Now 2180 on C cluster & again a problem  & had to be warmed up & disconnected & reconnected & re-cooled !

FOR APRIL 06  SM18 TESTS OUTPUT

ROCLA ACCIDENT STORY EMAILS

From: Ingo Ruehl
Sent: Fri 28/04/2006 17:39
To: Sylvain Weisz; Lyn Evans; Paolo Ciriani; Philippe Lebrun; Lucio Rossi; Alain Poncet; Louis Walckiers; Andrzej Siemko; Vinod Chohan
Cc: Claude Hauviller; Ralf Trant; Laurent Colly; Serge Pelletier; Oliver Boettcher
Subject: RE: Accident ROCLA

Bonsoir,

A short update:

The accident zone in SM18 was cleared up this afternoon without any incidents.

The driving mechanism of the damaged ROCLA 3 (CH545) is operational. The main concern remains the replacement of the lifting mechanism which may have to include the gear box according to the assessment of ROCLA's mechanical engineer who was on site all day. A more detailed analyze can be done once the disassembly works start on Tuesday next week. We requested a support team from the manufacturer for the repair works. Nevertheless, we estimate a minimum of two weeks to bring the vehicle back in service.

The fine adjustment of the newly installed cable on ROCLA 1 (CH500) is still under way. The reassembling will be finished tonight so that the load tests can be carried out on Tuesday morning (in agreement with the users in SM18).

Regards, 
Ingo Rühl / TS-IC

-----Original Message----- 
From: Sylvain Weisz 
Sent: Thursday, April 27, 2006 7:33 PM 
To: Lyn Evans; Paolo Ciriani; Philippe Lebrun; Lucio Rossi; Alain Poncet; Louis Walckiers; Andrzej Siemko; Vinod Chohan 
Cc: Claude Hauviller; Ralf Trant; Laurent Colly; Serge Pelletier; Oliver Boettcher; Ingo Ruehl 
Subject: RE: Accident ROCLA

Bonsoir à tous, 
     Vous trouverez ci-dessous la conclusion de SC-GS (Ralf Trant et Laurent Colly) en ce qui concerne la remise en route des véhicules ROCLA. Pour le court terme, cela veut dire:

1) que le ROCLA2, qui est en configuration MB, est de nouveau en service; 
2) que l'on remplace les câbles du ROCLA1, qui est en configuration SSS: le véhicule sera prêt pour un test en charge demain en début d'après-midi et pourra ensuite être mis en service;

3) que le ROCLA3 peut être déchargé et enlevé une fois la procédure établie et validée par SC-GS. Des représentants de ROCLA viendrons dans la matinée pour faire leur propre analyse de l'accident et pour évaluer les réparations à entreprendre sur ce véhicule. La procédure d'évacuation de l'aimant et du ROCLA3 sera disponible demain dans la matinée: après validation par SC-GS, cette évacuation se fera dans l'après-midi.

Bonne soirée, 
                                                        Sylvain

Par mesure de sécurité, suite à l'incident survenu mercredi soir sur le véhicule de transport d'aimants ROCLA n° CH-545 au SM18, les 2 autres véhicules ROCLA ont été consignés.

En regard des résultats de l'examen réalisé par M. VERDUYN de la Société APAVE sur les 3 véhicules, et suite à la réunion SC/GS - TS/IC/HM tenue cet après-midi, les dispositions suivantes ont été retenues:

- compte tenu de l'absence de fil cassé ou de détérioration sur les 4 câbles de levage du ROCLA2 (CH-501), ce véhicule peut immédiatement être remis en service. Cette autorisation d'utilisation est soumise aux dispositions d'inspection renforcée des câbles décrites plus bas.

- l'examen a démontré la nécessité de remplacer les 4 câbles de levage du ROCLA1 (CH-500). Leur remplacement sera suivi d'une réception avant remise en service. En cas d'autorisation de remise en service à l'issue de cette réception, les dispositions d'inspection renforcée des câbles seront également appliquées.

- Rocla3: les analyses de SC/GS sont terminées. Le véhicule est laissé à la disposition de TS/IC/HM. 
NOTA: 
- les câbles détériorés et remplacés seront conservés afin de permettre leur analyse ultérieure. 
- la procédure d'évacuation de l'aimant endommagé et du Rocla3 devra être approuvée par SC/GS 
Disposition d'inspection renforcée des câbles des véhicules Rocla: 
- périodicité: 2 semaines 
En fonction du résultat des inspections ou/et de l'intensité d'utilisation des véhicules, la périodicité pourra être aménagée.

- Un descriptif précis sera défini la semaine prochaine (procédure, critères de dépose des câbles). 
Laurent Colly - SC/GS

-----Original Message----- 
From: Sylvain Weisz 
Sent: jeudi, 27. avril 2006 08:22 
To: Lyn Evans; Paolo Ciriani; Philippe Lebrun; Lucio Rossi; Alain Poncet; Louis Walckiers 
Cc: Claude Hauviller 
Subject: Accident ROCLA

Nous avons eu un accident avec le ROCLA Nr 3 au SM18 hier soir: un des 2 câbles porteurs s'est rompu sous la charge d'un dipole. Il n'y a pas de blessé, l'aimant est tombé ~1m sur une extrémité. Le système est actuellement en sécurité et nous cherchons l'origine de l'usure du câble. Les autres ROCLAs sont consignés jusqu'à ce que nous en sachions plus. Je vous tiens au courant dès que j'ai des informations plus précises.

Sylvain

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_22_A | TBE2 | MB2236 : TT 821 temperature sensor reading error. | MTM |  | NC opened. |
| Tuesday_25_N | TBE1 | MB2317 : Error in temperature sensor reading in IAP at warm-Prep 2.1 and 2.2. (shows 80K instead of 300K). | MTM |  | Maryline advised to proceed to further tests. NC opened in CDW1. |
| Tuesday_25_N | TBD1 | SSS636: Cryo leak problem not solved. | CRI |  | The SSS636 is being warmed up and then will be removed for repair. |
| Wednesday_26_A | TBA1 | Accident of the MBB2252: the magnet failed down from ROCLA due to arm-thread cable broken. |  |  | Test coordinator and Nick informed ICS responsible has asked firemen to come. Actions taken by A. Siemko due to Rocla accident: - No intervention on TBA1 and TBA2 - Forbidden access to prohibited zone around Rocla - Guardians will frequently survey the area - All Roclas operation stopped till further notice - OP should put warning messages and transmit the information. |
| Wednesday_26_N | TBB2 | SSS234: Prep2.2C could not be completed (Clamp connection CD ). LF data didn't save, even though LF gets armed and gets triggered ( by 1A current ). During check application after switching on DA switches, the following error message was observed " could not find USR_open.vi ". Check application didn’t complete in TEMA. | AB/CO |  | OP team tried to reset DA switches after exiting web view from TEMA and all programs from sunMTA Eq. support contacted Thursday morning |
| Wednesday_26_N | TBE2 | MB2236: HV sequence failed at Cryogenic heater Vs Ground. | MTM |  | Eq. Support contacted Thursday morning. Equip. support advised to skip the step and continue with further tests. NC opened. |
| Thursday_27_A | TBB1 | SSS182: HF DAQ did nor arm while launching PT5.3. | AB/PO |  | Problem with on/stand-by power supply. |
| Thursday_27_A | TBE2 | MB2236 : During PT8 (ramping up to 12000A) a quench occurred | MTM |  | TC has been contacted and advised to repeat the same test. Repeated test was successful. |
| Thursday_27_N | TBE2 | MB2236: Next training (warm up quench) attempted after HV. Magnet showed detraining behavior 12247A. TC contacted for further course. He suggested to train the magnet till ultimate. | MTM |  | Detraining is continuing. Magnet will undergo a thermal cycle. |
| Thursday_27_N | TBA2 | MB1387 : For safety reason (ROCLA accident)TC instructed to stop work and put the magnet on 4.2K stand by till Saturday 9 AM and ask for further instruction |  |  |  |
| Thursday_27_N | TBE1 | MB2137 :PT1 on TBE1 shows error in D1-D2. | MTM |  | Potaim cards not adjusted as training is on in E2. Therefore magnet in E1 is kept at cryo ok 4.2K. |
| Thursday_27_N | TBB1 | TEMA showing error message 'Magnet Absent in the Active Bench'. Not possible to launch PT 6.3. OP team tried to re-start TEMA and revalidate the scanned data of magnet through Mobic, but no success. | IT | HWREC | Maryline contacted. She asked to put off HWREC and then enter the magnet names of B1 and B2 manually and proceed. |
| Friday_28_A | TBD2 | SSS609: Permanent trigger on Vclamp/Vsupra int/Ext | MTM |  | Maryline contacted. |
| Friday_28_A | TBB1 | SSS182: PLCSE communication lost during the training test. | AB/CO |  | PLCSE reset by switching off/on. |
| Friday_28_N | TBA1 | New magnet cannot be installed because big bellow and Y line are missing. | ICS |  | TC asked ICS Sunday to put another dipole with below. TC contacted Halik. A.Siemko has the key to open ICS store and get a new bellow |
| Friday_28_N | TBA2 | MB3187: PLCSE fault: Powering of the magnet could not be launched. | MTM |  |  |
| Friday_28_N | TBC1 | MB2180: During QH test at 1.5 kA, trigger on the Vclamp Vtaps. Current not ramping, quench heaters getting discharged and files are generated. | ICS |  | Maryline informed. With TC they asked perform HV test final and warm up the magnet and check the connection in the M3 line. Magnet re open Sunday afternoon. Connection re-done and warm test re-started. Training rules as for the first run applied but warm test results in the folder _3. In fact problem with power supply parameter. |
| Friday_28_N | TBC2 | MB1323: Voltage Tap error in Prep2.1. | ICS |  | PLCSE blocked & Vtaps connectors on the top of CFB were inversed. Solved by equip support? |
| Saturday_29_M |  | Cryo OK lost for 4 benches at 1.9 K (A2, B2, C1, E1) | ACR |  | ACR team has no explanation. |
| Saturday_29_M | TBD2 | SSS609: SSS connection. Paper traveler missing | MTM |  | Who has it ? ICS, MTM mechanics? |
| Saturday_29_A | TBB2 | SSS234: Corrector circuits GH and IJ not possible to power. | MTM |  | Fast stop was pushed. |
| Saturday_29_A | TBC1 | MB2180: Final HV test before warm up. Test failed dipole quench-heater vs Ground. HV Rack MY92:- Rack seems faulty. Tried 3 times on TBB2. PLCSE communication error. | MTM |  | Maryline contacted. She suggested to re-run and skip the failing steps. On 2nd run with different rack HV successful. |
| Sunday_30_M | TBB1 | SSS182: 1st training = 12046 A, then 2 wrong PT8 (quench at less than 12000 & not detected + PLSCE problem). PTC6.4 = 12427 A and good analysis; before next PT8, V-power QH 4 discharged by its own | MTM |  | TC asked to redo a training quench and then PT8. TC informed A. Siemko. He asked to perform 9 quenches or reach ultimate. |
| Monday_01_M | TBF2 | MB1297: PT6.1 - TEMA stopped executing the step RAMP to 12850 A (training quench) when switching to 10 A/s. | MTM |  | Shift leader executed the ramp manually. |
| Monday_01_M | TBD2 | SSS609: Quench while going to Standby. The magnet ramped to 50A but quenched again during the ramp-down to "OFF". | MTM |  | A.Siemko tried changing the threshold of MQY1&2_E-I. He suggested verifying the compensation and measuring QH resistances again to see if all is OK before continuing. |
| Monday_01_M | TBC2 | MB1323: During Slow Power Abort Test, Power Converter is not going to standby. | MTM |  | Guy contacted. Same problem as in C1. Internal parameter in the power supply not correct. Corrected by AB/PO support. |
| Monday_01_A | TBA2 | MB2338: Wrong magnet name on the code bar which could not be validated by the MOBIC | ICS |  | NC opened by OP team |