### vc/Week 33 starting 14 aug 06

### SM18 Operation Meeting (Tuesdays) 15 Aug 06

Bench status  on Monday  14-08-2006 at 8/14/2006 9:07:32 AM

|  | A1 | MBBR2367 | ICS 4 Final connection |  |
| --- | --- | --- | --- | --- |
|  | A2 | 1307 |  |  |
|  | B1 | SSS304 | PT1 IAP@1.9K, Part III |  |
|  | B2 | SSS664 | Prep 5 Cool Down |  |
|  | C1 |  |  |  |
|  | C2 | SSS307 | PT5.3: Powering Corrector CD |  |
|  | D1 | SSS648 | S4 Field Strength |  |
|  | D2 | SSS651 | PT 5.2 1.5 KA Quench HF |  |
|  | E1 | MBBR2365 | Prep 5 Cool Down |  |
|  | E2 | MBBR2294 | PT 13.2 Resist. Meas. |  |
|  | F1 | MBAL2281 | PT 6.1 Training 1 |  |
|  | F2 | MBAR2274 | Min Energy @ 6500 |  |

CONFIG :  D 6 - AS 3 -  IRSSS 3 ;

Supervisor: marta  ;Eq support : 16-3602

16 Magnet Tests completed ( 510 not done, 2368 neither)

7 Dipoles (2281 hv problems),

5 Arc-SSS  tests

1  500-series [ 528 (137 hrs)]

2  600-series [ 646 (143 hrs), 618 (142 hrs) ]

General Points :

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- News /Situation from (SSS, SSSS)  :  J Halik

- Situation SSSS  :D1 & D2 issues; SSW & 648 & anticryo alignment etc

- A.O.B..

WEEK 32

Benches A, C, E, F

Bench D

Bench B

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR2362 | 12852 A. | - | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR2333 | 11723.3 A. (D2-U) | 12810 A. (D2-U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 3 | SSS308 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 4 | SSS314 | 11900.9 A. (QI_12) | 12362.4 A. (QE_12) | 12512.1 A. (QI-12) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS510 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS528 | 10636.3 A. (QE_12) | 11824 A. (QE_34) | 12453.3 A. (QE_34) | 12657.9 A. (QE-12) |  | - | - | - | - | - | - | - | - |
| 7 | SSS276 | 12647 A. (QI_34) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 8 | SSS306 | 12197 A. (QI_34) | 12340.9 A. (QI_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 9 | SSS336 | 12471.8 A. (QI_12) | 12574.7 A. (QI_34) | 12616.9 A. (QI_34) |  | - | - | - | - | - | - | - | - | - |
| 10 | SSS646 | 3828.7 A. (Ex_MQ_12) | 4276 A. (Ex_MQ_34) | 4475 A. (MQMLI_34) | 4643 A. (MQMLI_12) | 4650 A. | - | - | - | - | - | - | - | - |
| 11 | SSSS618 | 5279.1 A. (Ex_MQM_2) | 5820 A. | - | - | - | - | - | - | - | - | - | - | - |
| 12 | MBAR1303 | 11836.9 A. (D1_U) | 12797 A. (D2-U) | 12853 A. | - | - | - | - | - | - | - | - | - | - |
| 13 | MBBR2364 | 10359.8 A. (D2_L) | 12046.5 A. (D1_U) | 12836.9 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |
| 14 | MBAL2281 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 15 | MBBR2368 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 16 | MBAR1301 | 12166.9 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 17 | MBBR1365 | 12274.2 A. (D1_L) | 12848.1 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |

2368 & 510 were never tested but taken off bench without; 2281 had long ‘history’ of on-bench ‘ fiddles’ for 10 + days, 2362 had ROBTC & passed superbly

|  |  | (08-AUG06 TUE-Morning to 14-AUG 06 MON-Night) |  |
| --- | --- | --- | --- |
| 08M (TUE) |  | SM18 water supply interruption | Resumed in Afternoon shift |
| 09M (WED) | TBF2 MBAR2274 | SMS "Temp too low AC bench F2". Observed that the AC cables interchanged while connection, at CFB side of magnet | ICS corrected the same |
| " | TBE2 MBAR2368 | In Prep2.2 IAP analysis, error in QH4 values | Giorgio opened NC in CQW1. The magnet has to removed from bench immediately. Necessary steps to remove magnet to be carried out by MTM. |
| 09A (WED) | TBD2 S4-618 | After generating the report for WP27, the report was generated for S651 magnet though the test was carried out on S618. This is due to scanning of S651 before the test was carried out | Giorgio is informed about this and he told that necessary correction will be done |
| 11M (FRI) | TBB2 SSS510 | Standby.ICS Could not connect the magnet due to mechanical problems. No test is carried out except for scanning and MTR printing. |  |
| 11N (FRI) |  | The E-traveller displays only three channels ( F1,F2,E2). E-traveller signature could not be done for any other benches. GHH contacted. | The problem of e-traveller has been solved by J. Axensalva by 12th Morning.ICS enterd a wrong magnet number with blocked the all e-traveller. |
| " | TBD1 S4-648 | QH Error and warning during training-3 | Giorgio informed that it is due to the 4th QH of this SSSS that has a larger value at warm and cold than expected. |
| 12M (SAT) | TBB2 S4-664 | Prep 2.2 launched (2 times) and no data for voltage taps was there both times | Euipment support contacted. He analysed the result and informed that this is because of difference in the channel names for S4 Magnets and continue for the next text |
| 12A (SAT) |  | While launching the test from the TEMA the magnet names are disappearing. So could not be launched.Georgeo was contacted. | he switched OFF HWREC and entered the magnet name manually in all clusters. The origin of the problem must be the same as for TTS:database ?! |
| 12A (SAT) |  | The problem of HWREC not accessing MTF data is still present. Giorgio contacted Oracle DB support and Netops, as well as AB-CO best effort to try to solve the problem. | Alessandro of AB/CO arrive and try to understand where the problem came from. He found that a library on AFS used by the Maciej script where not accessible |
| 12N (SAT) | TBD1 S4-648 | SSW. Bad results for the "error" parameter in the Field Strength measurements even after replacing the wire and changing the aperture. Noticed a piece of wire stuck behind the roller on the A stage maybe causing a short circuit (but wire resistance OK at .5Mohm) - impossible to remove the wire. | TBD1: SSW. The result of strength is within tolerance: 150 +/- 5. But the software made is showing larger error. TC advised that he will decide after looking on all the availble results |
| 12N (SAT) | TBF1 MBAL2281 | MBAL2281 is failing most of its HV tests at cold again (repeat due to the same problem) Inform Eq Supp and TC in the morning. | HV problem solved by removing the cover of IFS box: there must be a leak in the capillary which bring some He gas in the IFS box |
| 13N (SUN) |  | NO Power Test has been performed during the night shift as Cryo phase out problem since the beginning of night shift. | one of cold helium compressor is not working & job is ON. Presently Cryo is working on limited capacity. |
| 14M (MON) |  | (IT Helpdesk) was called in connection with the e traveller problem. | They said that the problem will be attended to by the piquet immediately. |
| " | TBA2 MBBR1368 | MTF is still reading old magnet name. Could not upload WP04. |  |
| 14N (MON) |  | The link 'MTF-Active' in SM18 operation home page leads to incorrect MTF page. However the link SMTMS -> Easy MTF shows correct MTF page. Do not upload the files using the direct MTF link from SM18 operation home page. |  |
| " | TBF1 MBAL2281 | TBF1: Signed for cryo_OK 1.9K, but Cryo team refused to cool down the magnet due to the leak in IFS box. | informed that it will remain in standby until a decision is taken tomorrow morning. |