### VC- /Week 47 starting 27 Nov  06

### SM18 Operation Meeting (Tuesdays) 28 Nov 06

Bench status  on Monday 27-Nov-2006 at: 11/27/2006 9:37:27 AM

| 12 | A1 |  |  | 295 |
| --- | --- | --- | --- | --- |
| 8 | A2 | MBAR2412 | Prep 5 Cool Down | 4.47 HV |
| 11 | B1 |  |  | 294.64 |
| 3 | B2 | SSS522 | ICS 5 Traveller Last | 296.34 |
| 1 | C1 | SSS373 | ICS 3 Traveller after warm test | 294.64 |
| 7 | C2 | SSS052 | PT5.3: Powering Corrector CD | 1.91 |
| 2 | D1 | SSS622 | PT 6.9 Training 9 | 2.35 |
| 6 | D2 | SSS675 | PT 14 Magnet MAPS | 295.36 |
| 9 | E1 | MBAR2410 | ICS 4 Final connection | 296.43 |
| 4 | E2 | MBAL2282 | PT 14 Magnet MAPS | 295.89 |
| 5 | F1 | MBBR1371 | PT 13.1 IAP @ Warm | 295.18 |
| 10 | F2 | MBBR1366 | PT 5.1 1.5 KA Quench LF | 1.90 |

CONFIG :  D 6 - AS 2 -  IRSSS 4 ;

Supervisor: Marta ;        Eq support 16-3602 :

10 Magnet Tests completed ( 5 Magnet Stripped ) ;

6 Dipoles tests + 1406 not tested HV fail at beginning	( 3 signed stripping)

1 Arc-SSS (  363 )

1 500-series ( 517  )

2  600-series [ 671 (170 hrs) , 650 (129 hrs) 3rd runnow retest without antiCryo]

General Points:

- Work load & 8 benches free on last Tues & full excessive work on Fri/sat/sun !

- SSS363  orbit correctors power ?;  SSS >360 in number issues ?

- Situation from Cryogenics:  J-P Lamboy or ACR Rep : next Monday 4 Dec power cut ?

- Situation SSSS  :D1 & D2 issues J Halik

- A.O.B

| Magnets under Test from 19-11-2006 to 25-11-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBAL1402 |  |  | 15-11-2006 | 45 h. | 28 h. | 57 h. | 17 h. | 14 h. | 22-11-2006 | 161 h. | Stripping |  |  |
| 2 | TBA1 | MBAL1406 |  |  | 22-11-2006 | - | - | - | - | - | 24-11-2006 | 5 h. | Stand By |  |  |
| 3 | TBA2 | MBAR1372 |  |  | 18-11-2006 | 43 h. | 24 h. | 30 h. | 18 h. | 21 h. | 24-11-2006 | 136 h. | Stripping |  |  |
| 4 | TBB1 | SSS517 |  |  | 15-11-2006 | 34 h. | 23 h. | 37 h. | 12 h. | 44 h. | 21-11-2006 | 150 h. | Stand By |  |  |
| 5 | TBB2 | SSS650 |  |  | 16-11-2006 | 21 h. | 40 h. | 46 h. | 10 h. | 12 h. | 22-11-2006 | 129 h. | Stand By |  |  |
| 6 | TBC1 | SSS363 |  |  | 15-11-2006 | 31 h. | 12 h. | 14 h. | 6 h. | 11 h. | 21-11-2006 | 74 h. | Stripping |  |  |
| 7 | TBD1 | SSS671 |  |  | 16-11-2006 | 80 h. | 16 h. | 50 h. | 12 h. | 12 h. | 20-11-2006 | 170 h. | Stand By |  |  |
| 8 | TBE1 | MBAL1416 |  |  | 19-11-2006 | 29 h. | 27 h. | 35 h. | 16 h. | 49 h. | 25-11-2006 | 156 h. | Stand By |  |  |
| 9 | TBE2 | MBAL2282 |  |  | 15-11-2006 | 49 h. | 39 h. | 67 h. | 29 h. | 7 h. | 23-11-2006 | 191 h. | Stand By |  |  |
| 10 | TBF1 | MBAR1341 |  |  | 16-11-2006 | 38 h. | 34 h. | 18 h. | 18 h. | 7 h. | 22-11-2006 | 115 h. | Stripping |  |  |
| 11 | TBF2 | MBBR2325 |  |  | 15-11-2006 | 39 h. | 25 h. | 36 h. | 16 h. | 23 h. | 21-11-2006 | 139 h. | Stripping |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL1402 | 12411.8 A. (D1_L) | 12047.8 A. (D1-L) | 12441.1 A. (D1_L) | 12537.8 A. (D1_U) | 12628.8 A. (D1_U) |  | - | - | - | - | - | - | - |
| 2 | MBAL1406 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 3 | MBAR1372 | 11313.6 A. (D1_L) | 12314.4 A. (D2_L) | 12533.6 A. (D2_U) | 12657 A. (D1_L) |  | - | - | - | - | - | - | - | - |
| 4 | SSS517 | 10578.5 A. (QE_34) | 12207.4 A. (QE_12) | 12538.2 A. (QE_34) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS650 | 3957 A. (?) | 4243.7 A. (No Data) | 4297.3 A. (No Data) | 4347.8 A. (E_MQML_1) | 4394.5 A. (I_MQML_1) | 4424.7 A. (Int_MQML) | 4484.3 A. (I_MQML34) | 4541.3 A. (ExMQML34) | 4586.3 A. (ExMQML12) | 4646.3 A. (ExMQML12) | 4650 A. | - | - |
| 6 | SSS363 | 11350.3 A. (QE_12) | 12580.7 A. (QI_12) | 12792.2 A. (QI_34) |  | - | - | - | - | - | - | - | - | - |
| 7 | SSS671 | 3724.8 A. (In_MQY_2) | 3703.3 A. (Ext-Mqy2) | 3721.6 A. (Int_MQY2) | 3710.2 A. (Ext_MQY2) | 3726.7 A. (Int_MQY1) | 3739.5 A. (I_MQY_1) | 3739 A. (E_MQY_2) | 3747.7 A. (E_MQY_2) | 3754.3 A. (I_MQY_1) | 3756.8 A. (E_MQY_2) | 3763.3 A. (Int_MQY2) | 3768.7 A. (I_MQY_1) | 3766 A. (Int_MQY1) |  |
| 8 | MBAL1416 | 10727.8 A. (D2-U) | 12170.8 A. (D1_L) | 12446.1 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |  |
| 9 | MBAL2282 | 9431.8 A. (D1_U) | 11015.2 A. (D1_U) | 12135.1 A. (D1_U) | 12262.4 A. (D1_L) | 12592 A. (D1-L) | 12680.9 A. (D2_U) | 12727.3 A. (D1_U) | 12761.5 A. (D2_L) | 12848 A. (D1-U) | 12850 A. | - | - | - |  |
| 10 | MBAR1341 | 11437.7 A. (D2_U) | 12313 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |  |
| 11 | MBBR2325 | 12314 A. (D2-L) | 12772.1 A. (D2-L) | 12000 A. (No Data) | 12850 A. | - | - | - | - | - | - | - | - | - |  |

Back to Homepage | For print (Test/Quench/Graph)| For print (Waiting time\Disconnect time\Graph)

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_21_N | TBE2 | MB2282 : Signed for warm-up as the magnet reached ultimate in 10th Training. No AQA alarms in PT10. AQA. Warning : Dir VT voltage peak exceeds 150V (181.8 for D1 and -185.5 for D2). Dir VT voltage jump exceeded 10V (10.6 for D1 and 10.4 for D2) | MTM |  | A.Siemko, Giorgio informed. |
| Wednesday_22_M | TBE1 | MBAL 1416: NC generated because TT821 give wrong value 45K, | MTM |  | Guy and Giorgio found U+ open. A bridge with I+ has been done to continue the test with T_value.. |
| Wednesday_22_A | TBF2 | MB1366: WP04 HV test failed.. Main magnet is shorted to ground. | MTM |  | Richard asked to remove the magnet out of the bench in order to pump the humidity. |
| Wednesday_22_A | TBB2 | SSS522: Clamp connection Prep2.2C could not be done. | ICS |  | Giorgio asked ICS for reconnection |
| Wednesday_22_N | TBA1 | MB1406: WP04 test failed on magnet. |  |  | Guy contacted. Special test carried out: QH 211 failed. |
| Thursday_23_M | TBE2 | MB2282: During PT13.2 R_(VTaps) gave wrong value R= 32 Ohms. | MTM |  | Giorgio checked it. The problem disappeared strangely after a while. Nevertheless NC is generated. |
| Thursday_23_N | TBC1 | SSS297: Cryo OK not stable, pressure fluctuation..(2 magnets cold!). | ACR |  | After investigation, cryo discovered that a compressor is blocked. Cold compressor stopped and re-generated. No hope of 1.9K before Friday afternoon. |
| Friday_24_N | TBC1 | SSS297: Long recovery time after a quench. Existence of a leak is mentioned??? | MTM |  | OP team will warn cryo team before the quench. |
| Friday_24_N | TBD1 | SSS622: anticryostat cables not correctly corrected?? | MTM |  |  |
| Friday_24_N | TBF2 | MB1366: Between IAP test Prep 2.1 and IAP test Prep 2.2, TT821 value changed from 282.7 to 273.1. | MTM | IAP |  |
| Saturday_25_M | TBE2 | MB2282: Quench launched on magnet 2282. After warm_up quench, HF and LF generated an auto trigger and a file was generated. | MTM |  | Guy informed. He asked to inform him if it occurred again. |
| Saturday_25_A | TBD1 | SSS622: Cryo OK lost | ACR |  |  |
| Saturday_25_N | TBC2 | SSS522: corrector powering CD circuit could not be launched: error message: "34 log waiting" message (33 bad state). | AB/PO |  | Guy informed. After investigation he called the AB/PO on stand_by. Power supply OK after changing a card in the power supply. |
| Sunday_26_A | TBC2 | SSS522: Potaim card CD are triggering when setting the converter to ONSTBY mode | ICS? |  | Guy came. Magnet put in stand_by till Monday Morning with investigation with AB/PO. Monday , ramp to 600 A could be done but some doubt remains in the Vtaps close to the clamp. Connection to be checked during the opening. |
| Sunday_26_A | TBF1 | MB1371: During final IAP at warm errors detected Magnet seems to have reverse polarity at the end of cold test, it was not seen during previous test. Diode test showed a bad resistance and wrong signal. | MTM |  | Guy suggested to repeat the test with left adapter at D20 (although this magnet has right polarity). Investigation by Giorgio Monday to sort out the problem : inversion was in the IFS box. |
| Sunday_26_A | TBB2 | SSS522: During resistance measurement at warm the values in CD corrector magnet is found in reverse order. | MTM | IAP | Guy informed: template is found to be wrong. |
| Saturday_25_N | TBE2 | MB2282: HV test at warm after cold test failed “dipole vs Ground”. | MTM |  | Investigation by Guy. He asked to open a NC. Richard found the short at the diode level. Problem with dust in the diode? |