ss13-Jun-03

#### Week 25: (16/06 to 20/06)

### SM18 Operation SCHEDULE (Monday Morning) Meeting

- Test Coordinator this week:   S.Sanfilippo (16-4641)

- MTA Technician on call:  (16-3602) E.Effinger.

- Planning for this week :

- TBA1:   3014  :  Test at 1.9 K.

- TBA2:   1016 Test at 1.9 K _end and warm up.

- TBC2 :  1026 :  Test at 1.9 K (1 run foreseen)

- TBC1 : 1024  Waiting for removal: 2008 will come

- Problems from Operation Last week ( Olav+ Federico)

- Rotary switch : be gentle with it.

- Problem with DCCT during one quench (TBA2). Solved?

- Offset in TT821: solved?

- Resistance too low across the magnet 5.7 Ohm: new IFS box

- TT821sp not OK and no spare.

- TBC2 : Anticryostat cables not connected and temperature OK?

- TBC2 : LF file wrong (temperature too low)

- AQA problem: LF file missing: problem with transfer file.

- Still problem in saving quench table files after changing PC.

- AFS problem in the console used for TBA2.

- MM problems : Check that the coil factor corresponds to the position of the switch in the rack.

- VME (communication) errors during a MM : Integrator problem.

- During the export of MM (cable coupling current) no confirmation.

- Remember please to fill test sequence, quench tables and check MM with display (fill the protocols to report errors)

- Situation From Cryogenics:  J-P Lamboy

- Other General Issues