vc/1-Sep-03

### Week 36 starting 01 Sept 03

### SM18 Operation SCHEDULE Meeting

Schedule for this week :

| BENCH | CURRENT MAGNET | STATUS Today(01/09) | Forward look, & Next Magnet |
| --- | --- | --- | --- |
| TBA1 | 2020 | Disconnection | Bring in 3028 ASAP |
| TBA2 | 2017 | Warm by midday 1 sept | Rapid disconnection & bring new : 2021 |
| TBC1 | 3046 | cold | Cold Tests Continue till Wed Morning- then Thermal cycle |
| TBC2 | SSS1 | Warm | Mech. Mods. To prepare for SSS1 then, Connection of SSS1 |
| TBE1 | 2018 | Warm | Disconnection ASAP & bring in new 2010 :{ to test after TBE2} |
| TBE2 | 1031 | Under connection but flange missing | Flange Missing to finish connection( commissioning issue) ; earliest work resumption: Tuesday 2nd |
| TBF1 | 2025 proposed |  | Prepare For commissioning |
| TBF2 | 2025 after F1 commissioned ? |  | Prepare For commissioning |

- Test Coordinator this week(35):  N Smirnov      MTA Technician on call:  (16-3602) : Federico

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Other General Issues

- Paper File for Resistances and good housekeeping, Shift strt status, Rotary Switch Writeup, new SSW Proc., CallOut Register in Logbook & Rules,

- MTF , Resistance of Tempr. Sensor(4Wire)

- News passing & Faults-e-Logbook as well for Monday Novelties

- Exchanging Shifts

- Portable Phone(s)

- Problems from Operation Last week (Stephane + Test Supervisor )

| Date | Problem | Type | Application/soft. | Action/advise |
| --- | --- | --- | --- | --- |
| Monday 25_M Tuesday 26_M | MM : File export problems (TBA1) | CO | MMP | Solved |
| Monday 25_M | IAP@cold : Vtaps Error in D1_D2_U | MTM | IAP | Euip.support called: Measure repeated and correct. Connection with the magnet forgotten? |
| Tuesday 26_M | IAP@cold : No trigger | ACR |  | Acquisition cards were disabled. |
| Tuesday 26_N | Quench at 4.2 K: Quench in the bus bar at 272 A | ACR |  | Test repeated and correct Origin not found. |
| Wednesday 27_N | HV test: Connector for corrector not connected. | MTM |  | Connector connected and Test repeated and correct |
| Wednesday27 _N | TBC1 : CDW1 could not be entered in MTF | MTM |  | Name of steps are changed. |
| Thursday 29_A | IAP@warm (TBC1) Error in quench heater file | MTM | IAP | New resistance of heaters (24 Ohm). IAP tuned for 22 Ohms. OK from Giorgio |
| Thursday 28_A | IAP@warm (TBC1) Continuous trigger in TEMA | MTM |  | RVLB8 Cable not properly connected |
| Thursday 28_A | SSW | MTM |  | New stretched wire procedure in blue folder |
| Thursday 28_A | Cryo lost :…delay for SSW SSW has to be completed during the night | ACR |  |  |
| Friday 29_M | Slow power abort 1 kA (TBA2) Error 222 serial communication: Serial port D connector not plugged in power supply | MTM |  | Equip.support called. Solved. |
| Thursday 28_A Friday 29_M | Problem in exporting data in MTF CDW1, CDBP… | EST |  | To find HCL.. Select the option “assembly only” EDMS support contacted. “put file” : is not present. Problem with SM0P login? |
| Friday 29_A | MM: test at 1.5 kA 1 sector over range and 1 head with the wrong polarity. | MTM |  | Equip.support called. Solved |
| Friday 29_N | MM: MXI error at the start of LHC cycle. Application blocked because power application hidden behind MMP | CO |  | Kill MMP application |
| Friday 29_N | TBA2 (sun MTA2): Full load line: Problem with DVM DAQ (error code 211 and acquisition stopped) | CO | DVM DAQ |  |
| Friday 29_N | TBA2 : TEMA blocked when launching Full load line (checking of VME) : MMP was visible and disappeared again. After re-launching all the application DVM-DAQ was hung. | CO | TEMA/MMP/DVM DAQ | Quit TEMA |
| Saturday 30_M | MXI error during magnetic positioning of the shaft | CO |  | On/off of GPIB controller |
| Saturday 30_A | LHC cycle: cryo loss Current and temperature readings not correct. | ACR |  | Test coordinator decision. |
| Sunday 31_M | TBE1 : Problem with T-coil (10-11 shorted) | CO |  |  |