vc/26-Jan-04

### Week 05  starting 26Jan 04

### SM18 Operation SCHEDULE Meeting (Tuesdays)

Schedule for this week :

| BENCH | CURRENT MAGNET | STATUS Today(18/01/04) | Forward look, & Next Magnet |
| --- | --- | --- | --- |
| TBA1 | NOT Active |  |  |
| TBA2 | NOT Active |  |  |
| TBC1 | 2041 | Tempr sonde repair |  |
| TBC2 | SSS08 | SunWS + PLC pblms |  |
| TBD1 | 1063 no diode | Bench NEEDS COMMISSIONING |  |
| TBD2 | 3074 |  |  |
| TBE1 | 1030 | Bench REPAIRed?: |  |
| TBE2 | 3076 | new |  |
| TBF1 | 3015 | cold |  |
| TBF2 | 3025 |  |  |

Test Coordinator this week:  Stephane ;  MTM  Tech. on call:  (16-3602) :

- Announcements

  - No Diode Tests

  - No diodes in New Delivery

  - Magnets without Qloc or MM  ( no shafts)  : Backlog List Printout

  - Whitebooard  & keeping track ( test Coord )

  - May need Qloc  for poor magnets means installing shafts late if feasible

  - no RRR

  - no 4.4 K Quenches

  - 10KA Quench to Warm up

  - Dec Review & Limiting Quenches :Generally  2 Quenches at most

  - No quench to 9T rule : provoke 1 quench at 8.33T  ; do MM , CDAP, & 2nd quench to warm up

  - 2 Quench rule :  stop training if 2nd Quench exceeds 12000A  (~ 8.4  T); do usual MM , CDAP , 3rd Quench to warm up

  - What if 1st Quench >12000A ? Do MM, CDAP Continue training and if 9T reached without quench then, need to provoke a 2nd quench at 8.33T & warm up ; else if 2nd Quench is before 9T, use that as  a warm up quench

  - 12000A &  not 12200A  for MM  rule

  - Poor magnets & continue to train to 8 Quenches to  9T ;

  - Thermal cycle  if needs  >5 Q to arrive at 9T ; After Thermal Cycle, 8.6T  reached in 1 Quench

  - Traveller Signing at end & stripping or Standby ; MAPS form;  Test Coord.  involvement

- BRIEFING & NOVELTIES

  - CRYO

  - POWER

  - CONTROLS

  - WATER & PLC ( Federico +Eric)

AOB

Bench Status ( Tues 2 dec at 1800 hrs)

Problems of Last week

| Date | Problem | Type | Application/ soft. | Action/advise |
| --- | --- | --- | --- | --- |