Vc/27-Sep-04

### Week38 starting 13Sept  04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 13 Sept 04  ~15.30 hrs

| TBA1 | MBAL3208 | ICS 3 Traveller after warm test | 299.1 |
| --- | --- | --- | --- |
| TBA2 | MBAL3203 | PT 12 Warm Up | 55.2 |
| TBB1 | _ | _ | 298.6 |
| TBB2 | MBAR1140 | PT 12 Warm Up | 301.4 |
| TBC1 | MBAL3205 | PT 6.4 Training 4 | 4.6 |
| TBC2 | MBBL2086 | Prep 5 Pumping + Cool Down | 104.2 |
| TBD1 | SSS043 | Finished Ready to go Final scan | 298.7 |
| TBD2 | SSS046 | Prep 5 Pumping + Cool Down | 298.8 |
| TBE1 | MBBL1132 | Prep 5 Pumping + Cool Down | 58.6 |
| TBE2 | MBBL1144 | PT 12 Warm Up | 13.4 |
| TBF1 | MBBL1143 | ICS 6 Disconnect Magnet WP07 | 299 |
| TBF2 | MBBL1125 | PT 12 Warm Up | 296.9 |

9/13/2004 3:29:42 PM    Temperature data are taken from TBSM18 site

Coordinator this week: Marco; MTM support on call :  (16-3602).

RECORD !!  13 Magnets [ 9  dipoles( 3 with MM)+ 2 SSS]   Disconnected after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

Priority settings …

1140 came back 3rd time ?

- SSS work :   Wire Breakages

Nair + Arun leaving

Back to Homepage

## Tests

| Magnets under Test from 05-09-2004 to 11-09-2004 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA2 | MBAL2047 |  | 31-08-2004 | 26 h. | 77 h. | 39 h. | 34 h. | 5 h. | 08-09-2004 | 192 hours |  |  |
| 2 | TBB1 | SSS035 |  | 30-08-2004 | 74 h. | 57 h. | 69 h. | 19 h. | 45 h. | 10-09-2004 | 264 hours |  |  |
| 3 | TBB2 | MBAL3206 |  | 06-09-2004 | 27 h. | 47 h. | 26 h. | 20 h. | 8 h. | 11-09-2004 | 120 hours |  |  |
| 4 | TBB2 | MBBL2107 |  | 30-08-2004 | 28 h. | 40 h. | 32 h. | 25 h. | 6 h. | 06-09-2004 | 168 hours |  |  |
| 5 | TBC1 | MBAL3145 |  | 02-09-2004 | 1 h. | 14 h. | 15 h. | 20 h. | 6 h. | 05-09-2004 | 72 hours |  |  |
| 6 | TBC1 | MBAL3202 |  | 05-09-2004 | 38 h. | 39 h. | 31 h. | 15 h. | 14 h. | 10-09-2004 | 120 hours |  |  |
| 7 | TBC2 | MBBL1099 |  | 05-09-2004 | 38 h. | 72 h. | 20 h. | 13 h. | 7 h. | 11-09-2004 | 144 hours |  |  |
| 8 | TBC2 | MBBL1146 |  | 27-08-2004 | 23 h. | 52 h. | 57 h. | 50 h. | 6 h. | 05-09-2004 | 216 hours |  |  |
| 9 | TBD2 | SSS038 |  | 24-08-2004 | 130 h. | 31 h. | 107 h. | 9 h. | 22 h. | 07-09-2004 | 336 hours |  |  |
| 10 | TBE1 | MBAL3159 |  | 02-09-2004 | 26 h. | 112 h. | 24 h. | 23 h. | 9 h. | 11-09-2004 | 216 hours |  |  |
| 11 | TBE2 | MBBL3195 |  | 01-09-2004 | 21 h. | 109 h. | 25 h. | 25 h. | 12 h. | 09-09-2004 | 192 hours |  |  |
| 12 | TBF1 | MBAR1133 |  | 29-08-2004 | 39 h. | 55 h. | 36 h. | 71 h. | 8 h. | 07-09-2004 | 216 hours |  |  |
| 13 | TBF2 | MBAL3146 |  | 31-08-2004 | 17 h. | 100 h. | 58 h. | 17 h. | 10 h. | 09-09-2004 | 216 hours |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL2047 | 11852 A. (D1-U-S12) | 9201 A. (No Data) | 12353 A. (D1-L-S12) |  | - | - | - | - | - | - | - | - | - |
| 2 | SSS035 | 12064 A. (QI-34) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 3 | MBAL3206 | 12011 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBL2107 | 10347 A. (D2-U) | 12539 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 5 | MBAL3145 | 12580 A. (D1_U) | 12655 A. (D2-L) |  | - | - | - | - | - | - | - | - | - | - |
| 6 | MBAL3202 | 10082 A. (D1-U) | 11583 A. (D1-U) | 12096 A. (D1-U) | 12654 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - |
| 7 | MBBL1099 | 12178 A. (D2-U) | 12219 A. (D1-U) |  | - | - | - | - | - | - | - | - | - | - |
| 8 | MBBL1146 | 12461 A. (D2-L) | 12462 A. (D1 L) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | SSS038 | 12661 A. (QE_34) | 12856 A. (QE-12) |  | - | - | - | - | - | - | - | - | - | - |
| 10 | MBAL3159 | 10396 A. (D2-U) | 12284 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 11 | MBBL3195 | 11521 A. (D1-L) | 12596 A. (D2_U) |  | - | - | - | - | - | - | - | - | - | - |
| 12 | MBAR1133 | 12118 A. (D1_U S03) | 12318 A. (D1-L-S01) |  | - | - | - | - | - | - | - | - | - | - |
| 13 | MBAL3146 | 11780 A. (D2-U) | 11534 A. (D1-U) | 11862 A. (D2-L) | 12178 A. (D2-U) | 12268 A. (D1-U) | 12381 A. (D2_L) | 12526 A. (D1-L) | 12660 A. (D2-U) | 12828 A. (D1-U) |  | - | - | - |

Bench status  and tests for now (13/09/2004 15:33)  & next few days :  see Video Display

| Magnets under Test on 13-09 3:32:16 PM |
| --- |
| - | Bench | Magnet | Shafts | Start | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | Last Test Desc | Time | I | Temp. | Total |
| 1 | TBA1 | MBAL3208 |  | 13-09 | 4 h. | - | - | - | - | ICS 3 Traveller after warm test | 13-09 (14 : 59) | 0 A. | 300 K | 4 hours |
| 2 | TBA2 | MBAL3203 |  | 08-09 | 22 h. | 64 h. | 16 h. | 21 h. | - | PT 12 Warm Up | 12-09 (18 : 54) | 0 A. | Warming | 123 hours |
| 3 | TBB2 | MBAR1140 |  | 12-09 | 39 h. | - | - | - | - | PT 12 Warm Up | 13-09 (12 : 41) | 0 A. | Warming | 39 hours |
| 4 | TBC1 | MBAL3205 |  | 10-09 | 22 h. | 32 h. | 14 h. | - | - | PT 6.4 Training 4 | 13-09 (14 : 13) | 0 A. | 1.9 K | 68 hours |
| 5 | TBC2 | MBBL2086 |  | 11-09 | 22 h. | 32 h. | - | - | - | Prep 5 Pumping + Cool Down | 12-09 (07 : 06) | 0 A. | Cooling | 54 hours |
| 6 | TBD1 | SSS043 |  | 01-09 | 52 h. | 63 h. | 121 h. | 5 h. | 43 h. | Finished Ready to go Final scan | 13-09 (14 : 07) | 0 A. | 300 K | 285 hours |
| 7 | TBD2 | SSS046 |  | 07-09 | 138 h. | - | - | - | - | Prep 5 Pumping + Cool Down | 12-09 (01 : 30) | 0 A. | 300 K | 138 hours |
| 8 | TBE1 | MBBL1132 |  | 11-09 | 12 h. | 48 h. | - | - | - | Prep 5 Pumping + Cool Down | 11-09 (15 : 35) | 0 A. | Cooling | 60 hours |
| 9 | TBE2 | MBBL1144 |  | 09-09 | 20 h. | 50 h. | 21 h. | 2 h. | - | PT 12 Warm Up | 13-09 (13 : 36) | 2 A. | Warming | 93 hours |
| 10 | TBF1 | MBBL1143 |  | 07-09 | 33 h. | 37 h. | 44 h. | 17 h. | 1 h. | ICS 6 Disconnect Magnet WP07 | 13-09 (03 : 38) | 0 A. | 300 K | 144 hours |
| 11 | TBF2 | MBBL1125 |  | 09-09 | 20 h. | 47 h. | 35 h. | -5 h. | - | PT 12 Warm Up | 13-09 (20 : 30) | 0 A. | Warming | 97 hours |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL3208 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAL3203 | 12151 Amp. (D1-L) | 12852 Amp. () | - | - | - | - | - | - | - | - | - | - | - |
| 3 | MBAR1140 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAL3205 | 10996 Amp. (D1-U) | 11491 Amp. (D2_U) | 12499 Amp. (D2-L) | 0 Amp. (No Data) |  | - | - | - | - | - | - | - | - |
| 5 | MBBL2086 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS043 | 11632 Amp. (QE-34) | 12315 Amp. (No Data) | 12339 Amp. (QI-34) | 12708 Amp. (E_34_S06) | 12856 Amp. () | - | - | - | - | - | - | - | - |
| 7 | SSS046 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBBL1132 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 9 | MBBL1144 | 11540 Amp. (D1-U) | 12517 Amp. (D1-L) |  | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBL1143 | 11606 Amp. (D1-L-S13) | 11858 Amp. (D1-L) | 12199 Amp. (D2-L s01) | 12347 Amp. (D1 L S11) | 12535 Amp. (D1 L S11) | 12416 Amp. (D1-L_S11) |  | - | - | - | - | - | - |
| 11 | MBBL1125 | 12506 Amp. (D1-L) | 12406 Amp. (D1-U) |  | - | - | - | - | - | - | - | - | - | - |

General Problems last week :

| Date | Bench | Problem | Type | Application/soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _07_A | TBE2 | Quench data not saved in hf.. | AB/CO | hf | Guy informed. Giorgio analyse the quench using lf file. Switch off and on the DAQ hardware. |
| Tuesday _07_N | TBD1 | Tcoil: Reistance did not match. | MTM |  | Guy informed. Shaft not scanned No sticker for scanning.. |
| Tuesday _07_N | TBD2 | In the connection box, one channel not connected D21-A2.. | MTM |  | Corrected by Jackie. |
| Tuesday _07_N Wednesday _08_A | TBF2 TBE2 TBC1&TBD1 | Quench data file not getting uploaded into data storage. Idem Idem. | AB/CO | Hf, lf |  |
| Wednesday _08_M | TBD1 | 3 sectors not working (16-17, 00-01) | MTM |  | OK to continue like this, it will be repaired after cold test. |
| Wednesday _08_A | TBD1 | Load-line failed Test repeated: failed again because de-ramp of current. | ? |  |  |
| Wednesday _08_A | TBE1 | Interlock on QH for E1: Qheaters 2 &4 not present. | MTM |  | Faulty contactor in the switch box. Switch fron X2 to X1 then OK. |
| Wednesday _08_A | TBB1 | SSW measurement : wire broke | MTM |  | . |
| Wednesday _08_N | TBD1 | Not possible to power the MQT. Trigger in ext. auxiliary | SL/PO |  | Guy informed.Investigation : Probably coming from connection of Vtaps on clamp. Test skipped. |
| Wednesday _08_N | TBD1 | Cross calibration measurements blocked: Error in CPU address. Origin : Motor touching the end stop. | AB/CO |  |  |
| Thursday_09_A | TBC2 | Provoked quench with LF heaters at 1.5 kA. Alarm on tfire. | MTM |  | Origin ? Problem with QH time scaling: Fixed by Boris. |
| Thursday_09_N | TBB2 | SPA on dipole 3206:launched 4 times. It stopped at 60 A and current ramp down. Setting SSS loaded instead of dipole | AB/CO? IT? |  | Correct setting loaded then OK. |
| Thursday_09_N | TBD1 | 4 SPA on D bench. | AB/CO? IT? |  |  |
| Friday_10_A | TBA1 TBF1 | Qloc compensation problem Qloc compensation problem | MTM |  | Guy informed D20 connector not connected (TBA1)! |
| Friday_10_A | TBF1 | Interlock Ext2 on PC. | MTM |  | Manual valves of water supply of PC closed. |
| Friday_10_N | TBD2 | Anticryostat problem (long, aperture 1) in SSS. | MTM |  | One resistance shorted to the ground (the heating one). Guy informed. OK given to continue. Investigation planned during the disconnection. |
| Saturday_11_M | TBD1 | CDAP at 1.9 K : HV problem for orbit correctors | MTM |  | Guy informed : test re-launched then OK. |
| Saturday_11_N | TBD1 | SSW measurements with system 1 : problem with the tension imposed by the motor:. | MTM |  | Guy informed. He found that the new controller needs a special configuration. Guy exchange with system 2. Joe Dimarco will be contacted. |
| Sunday_12_M | TBF1 | On 1143 CDAP OK on sun station but not in the generated report. | MTM | HV | Guy will inform Richard Monday. |
| Sunday_12_M | TBC1 | 3205: First training quench: No data transferred : analyse done locally | AB/CO | Hf-lf |  |