Vc/27-Sep-04

### Week40 starting 27Sept  04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 27 Sept 04  ~16.30 hrs

|  | A1 | MBBL1148 | CR 1 Leak Test |  |
| --- | --- | --- | --- | --- |
|  | A2 | MBBL1122 | PT 6.8 Training 8 |  |
|  | B1 | SSS602 | ICS 6 Disconnect Magnet WP07 |  |
|  | B2 | MBBL3213 | PT 6.2 Training 2 |  |
|  | C1 | MBAR2037 | ICS 2 Connect Magnet (ICS) |  |
|  | C2 | MBAR1142 | Thermal cycle |  |
|  | D1 | SSS050 | ICS 1 WP04 HV Test Warm |  |
|  | D2 | SSS046 | ICS 6 Disconnect Magnet WP07 |  |
|  | E1 | MBAR2033 | PT 12 Warm Up |  |
|  | E2 | MBBL3220 | Prep 3 CDW1 HV |  |
|  | F1 | MBAL2094 | Prep 5 Pumping + Cool Down |  |
|  | F2 | MBBL2103 | ICS 5 Traveller Last |  |

9/27/2004 4:34:46 PM    Temperature data are taken from TBSM18 site

Coordinator this week: John Miles; MTM support on call :  (16-3602).

10 Magnets [ 8 dipoles( 3 with MM)+ 1 SSS + 1 SSSS]   Disconnected after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

Priority settings …

- SSS work :   A & B type clarifications

- Special SSS :

- Cluster C Rotary Switch Modifications : expected to be finished on ?

## RESULTS of Tests LAST WEEK

| Magnets under Test from 19-09-2004 to 25-09-2004 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA2 | MBAR2038 |  | 14-09-2004 | 140 h. | 11 h. | 13 h. | 17 h. | 14 h. | 22-09-2004 | 192 hours |  |  |
| 2 | TBB2 | MBAR1134 |  | 13-09-2004 | 39 h. | 45 h. | 52 h. | 13 h. | 7 h. | 20-09-2004 | 168 hours |  |  |
| 3 | TBC1 | MBAL3185 |  | 15-09-2004 | 16 h. | 67 h. | 37 h. | 15 h. | 4 h. | 21-09-2004 | 144 hours |  |  |
| 4 | TBC2 | MBAR1142 |  | 16-09-2004 | 30 h. | 99 h. | 74 h. | 39 h. | 0 h. | 25-09-2004 | 216 hours |  |  |
| 5 | TBD1 | SSS045 |  | 15-09-2004 | 77 h. | 17 h. | 108 h. | 14 h. | 1 h. | 24-09-2004 | 216 hours |  |  |
| 6 | TBE1 | MBBL3212 |  | 16-09-2004 | 28 h. | 44 h. | 25 h. | 25 h. | 6 h. | 22-09-2004 | 144 hours |  |  |
| 7 | TBE2 | MBBL3214 |  | 15-09-2004 | 25 h. | 46 h. | 19 h. | 42 h. | 5 h. | 20-09-2004 | 120 hours |  |  |
| 8 | TBF1 | MBAL2088 |  | 18-09-2004 | 22 h. | 63 h. | 49 h. | 24 h. | 10 h. | 25-09-2004 | 168 hours |  |  |
| 9 | TBF2 | MBAL3209 |  | 14-09-2004 | 20 h. | 33 h. | 46 h. | 12 h. | 1 h. | 19-09-2004 | 120 hours |  |  |

### +1 SSSS ? = sss602

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAR2038 | 10581 A. (D1_L) | 12274 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR1134 | 11555 A. (D1 U) | 11714 A. (D2-L) | 11733 A. (D2_U) | 11864 A. (D1-L) | 11980 A. (D2-U) | 12069 A. (D1_U) | 12041 A. (D1-L) | 12124 A. (D2-U) | 12180 A. (D1_L) |  | - | - | - |
| 3 | MBAL3185 | 11124 A. (D1-U-S13) | 12521 A. (D1-U-S13) |  | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAR1142 | 11585 A. (D1-L-S01) | 11909 A. (D2-U-S13) | 12146 A. (D2-U-S13) | 12395 A. (D1-U-S01) | 12573 A. (D1-U-S01) | 12639 A. (D2-L-S13) | 12728 A. (D2_U_S13) | 12706 A. (D1-L-S13) | 12793 A. (D1_U_S01) |  | - | - | - |
| 5 | SSS045 | 12148 A. (Q_I_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 6 | MBBL3212 | 11268 A. (D2-U) | 12857 A. | - | - | - | - | - | - | - | - | - | - | - |
| 7 | MBBL3214 | 12431 A. (D2 U) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBAL2088 | 11515 A. (D1-L-S13) | 12543 A. (D1-U-S11) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAL3209 | 11075 A. (D1-U) | 12345 A. (D2_U) |  | - | - | - | - | - | - | - | - | - | - |

Bench status  and tests for now (27/09/2004 16:33)  & next few days :  see Video Display

| Magnets under Test on 27-09 4:40:24 PM |
| --- |
| - | Bench | Magnet | Shafts | Start | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | Last Test Desc | Time | I | Temp. | Total |
| 1 | TBA1 | MBBL1148 |  | 26-09 | 19 h. | 9 h. | - | - | - | CR 1 Leak Test | 27-09 (15 : 21) | 0 A. | 300 K | 28 hours |
| 2 | TBA2 | MBBL1122 |  | 22-09 | 20 h. | 54 h. | 43 h. | - | - | PT 6.8 Training 8 | 27-09 (13 : 21) | 12574 A. | 1.9 K | 117 hours |
| 3 | TBB1 | SSS602 |  | 15-09 | 40 h. | 77 h. | 75 h. | 17 h. | 13 h. | ICS 6 Disconnect Magnet WP07 | 24-09 (22 : 48) | 0 A. | 300 K | 288 hours |
| 4 | TBB2 | MBBL3213 |  | 20-09 | 42 h. | 117 h. | 17 h. | - | - | PT 6.2 Training 2 | 27-09 (12 : 10) | 12375 A. | 1.9 K | 176 hours |
| 5 | TBC1 | MBAR2037 |  | 27-09 | 2 h. | - | - | - | - | ICS 2 Connect Magnet (ICS) | 27-09 (14 : 49) | 0 A. | 300 K | 2 hours |
| 6 | TBC2 | MBAR1142 |  | 26-09 | 31 h. | - | - | - | - | Thermal cycle | 26-09 (09 : 11) | 0 A. | 300 K | 31 hours |
| 7 | TBD1 | SSS050 |  | 24-09 | 70 h. | - | - | - | - | ICS 1 WP04 HV Test Warm | 24-09 (23 : 30) | 0 A. | 300 K | 70 hours |
| 8 | TBD2 | SSS046 |  | 07-09 | 249 h. | 97 h. | 92 h. | 15 h. | 14 h. | ICS 6 Disconnect Magnet WP07 | 27-09 (08 : 49) | 0 A. | 300 K | 475 hours |
| 9 | TBE1 | MBAR2033 |  | 22-09 | 25 h. | 71 h. | 33 h. | 4 h. | - | PT 12 Warm Up | 27-09 (12 : 11) | 2 A. | Warming | 133 hours |
| 10 | TBE2 | MBBL3220 |  | 27-09 | 8 h. | - | - | - | - | Prep 3 CDW1 HV | 27-09 (15 : 28) | 0 A. | 300 K | 8 hours |
| 11 | TBF1 | MBAL2094 |  | 25-09 | 28 h. | 24 h. | - | - | - | Prep 5 Pumping + Cool Down | 26-09 (16 : 50) | 0 A. | Cooling | 52 hours |
| 12 | TBF2 | MBBL2103 |  | 19-09 | 43 h. | 85 h. | 34 h. | 22 h. | 0 h. | ICS 5 Traveller Last | 27-09 (14 : 49) | 0 A. | 300 K | 186 hours |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBL1148 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBBL1122 | 11550 Amp. (D1-L-S01) | 11802 Amp. (D1-L-S13) | 12248 Amp. (D1-L-S11) | 12381 Amp. (D2-L-S13) | 12625 Amp. (D1-U-S01) | 12644 Amp. (D2-L-S09) | 12574 Amp. (D2-L-S09) |  | - | - | - | - | - |
| 3 | SSS602 | 5019 Amp. (M_I_34) | 5477 Amp. (Q_E_34) | 5812 Amp. (Q_I_12) | 5820 Amp. () | - | - | - | - | - | - | - | - | - |
| 4 | MBBL3213 | 10602 Amp. (D2_U) | 12375 Amp. (D1_U) |  | - | - | - | - | - | - | - | - | - | - |
| 5 | MBAR2037 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 6 | MBAR1142 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS050 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 8 | SSS046 | 12162 Amp. (QI_34) | 12782 Amp. (QE-34) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAR2033 | 10654 Amp. (D1-U) | 11633 Amp. (D1-U) | 12358 Amp. (D1-U) | 12847 Amp. (D1-L) | 12850 Amp. () | - | - | - | - | - | - | - | - |
| 10 | MBBL3220 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 11 | MBAL2094 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 12 | MBBL2103 | 11254.6 Amp. (D1-U) | 12413 Amp. (D2 L) |  | - | - | - | - | - | - | - | - | - | - |

General Problems last week :

| Date | Bench | Problem | Type | Application/soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _21_A | TBC2 | MM: Two coils bad in the shaft: | MTM |  | Stephane informed by Federico: he advised to proceed and report the errors.. |
| Tuesday _21_A | TBD1 | Shaft in aperture 2 touched the anticrysotat in Qloc position. The cable connecting the shaft to the TRU was too short. No measurement possible in aperture 1. | MTM |  | OK to proceed : OK for MM not for Qloc. Fabienne informed. She changed the cable. |
| Wednesday _22_M | TBD1 | SSS045: IAP Tcoil: Faulty results for sectors 1, 2, 3 in aperture 1: faulty values in aperture 2 also | MTM |  |  |
| Wednesday _22_A | TBC2 | MM1: -Problem in shaft position. -Current not displayed -Temperature not correct (7.5 K). . | MTM |  | Wrong coil sets Not displayed in manual. Displayed in automatic? |
| Wednesday _22_A | TBF1 | IAP at cold: compensation out of limits. | MTM | IAP | Federico called:He checked all the chain: nothing wrorng. Proceed as is. |
| Wednesday _22_A | TBD1 | LHC cycle could not be exported as the magnet name was not recognized. | MTM |  | Stephane gave the correct name: corrected by Maryline. |
| Thursday_23_M | TBD1 | MinNRJ done to warm up the magnet but only one training quench performed. | MTM |  | TC asked to colldown again the magnet and do a training to warm up the magnet. |
| Thursday_23_M | TBF1 | B11 wrong in one sector (over-range). | MTM |  | Stephane advised to proceed.. |
| Thursday_23_A | TBF1 | SPA during LHC cycle at 5700 A during the measurement cycle | IT |  | Federico called. Stephane informed. He decided not to repeat the measurement. |
| Thursday_23_N | TBF1 | Cryo problem due to LHe level. | ACR |  |  |
| Thursday_23_N | TBD2 | It is not possible to power CD circuit corrector magnet. Current ramp down after powering EF circuit. | MTM |  | Federico called. Files were missing .He also found a permanent trigger in Vclamp_EF. He put a bridge on the ‘sortie double’of the potaim card. |
| Friday_24_N | TBD1 | HV test failed on SSS050(WP04). bad insulation sextupole/MQT. | MTM |  | Federico called : Investigation to see if it come from the IFS box monday. |
| Saturday_25_M | TBC1 TBA2 | Wrong magnet name and shaft name s in MMP. | MTM |  | Federico called : He corrected the setting. |
| Saturday_25_A Sunday_26_M | TBC1 | Over-range in sector 1415 Ap2 Motor position had a problem. | MTM |  | Federico called (shaft:30) He checked but the coli is OK. Origin not found. Stephane advised to continue. Adjusted. |
| Saturday_25_M | TBE2 | 2095 magnet: HV report not generated correctly | MTM | HV | Richard informed by E-mail |
| Sunday_26_N | TBB2 | Quench occurred during diode test at 466 A while ramp at 3 kA. Setting “special magnet” instead of ‘dipole magnet’ used in power application. | MTM |  | Power supply application closed , select the good setting and then OK. |