Vc/25-Oct-04

### Week43 starting 18 oct 04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 18 Oct 04  ~17.30 hrs

|  | A1 | MBBL3131 | PT 2 HV Cold Test |  |
| --- | --- | --- | --- | --- |
|  | A2 | MBAL3224 | PT 8 Fast De-excitation |  |
|  | B1 | SSS053 | Stretched Wire Cold SC21 |  |
|  | B2 | SSS064 | Prep 5 Pumping + Cool Down |  |
|  | C1 | MBAL3234 | PT 6.1 Training 1 |  |
|  | C2 | MBBL3164 | ICS 4 Final connection |  |
|  | D1 | SSS062 | PT 12 Warm Up |  |
|  | D2 | SSS066 | Prep 5 Pumping + Cool Down |  |
|  | E1 | MBBR1075 | Prep 5 Pumping + Cool Down |  |
|  | E2 | MBAL3232 | ICS 2 Connect Magnet (ICS) |  |
|  | F1 | MBAL1156 | Prep 3 CDW1 HV |  |
|  | F2 | MBAL3227 | ICS 5 Traveller Last |  |

10/18/2004 5:44:44 PM    Temperature data are taken from TBSM18 site

Coordinator this week: Nikolay; MTM support on call :  (16-3602).

15 Magnets [ 11 dipoles( 0 with MM)+ 4 SSS +  0 SSSS]   Disconnected after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

AOB

## RESULTS FROM LAST WEEK

PROBLEMS OF LAST WEEK

| Date | Bench | Problem | Type | Application/soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Wednesday _13_M | TBB1 | IAP @ warm : Trigger on potaim cards | MTM |  | One cable was not put back in place after switching from special to arc SSS. Solved by Richard. |
| Wednesday _13_M | TBD2 | High current light flashing | MTM |  | Solved by Giorgio, one relay was blocked. |
| Wednesday _13_A | TBD1 | SSW at warm : saturation of the signal in the power supply | MTM |  | Nicolay called. Investigation will be pursued tomorrow. Stephane decide to report SSW measurements at warm after the cold test. |
| Wednesday _13_A | TBC1 | Cryo test. | ACR |  | Magnet kept on stand by |
| Wednesday _13_A | TBC1 | Diode test.: first trial: No Vtano, VTcatho signals recorded . Test repeated : No data for High Field heaters. | AB/CO | lf | Richard called : cables disconnect by maintenance people. Solved. Stephane looked for data in lf (transient) but no data: Magnet is protected but discharges data not visible. Stop the test and Richard called. Data stored in lf but in archieved mode: problem with lf DAQ? Swith off/on the crates, restart DAQ, trigger one HF discharge. It works. Quench repeated. |
| Wednesday _13_A | TBB1 | SSW on TBBI: work station not working : one hard disk crashed (machine 33). | AB/CO |  | Richard called Magnus. Solved for this time. |
| Thursday_14_M | TBF1 | IAP @cold: freesing of curremnt leads. Test stop | ACR |  | Tprobe faulty. Solved by ACR team |
| Thursday_14_A | TBD1 | Sun Screen not working? | MTM |  | Connector disconnected. Solved |
| Thursday_14_A | TBF1 | Diode test: faulty quench at 150 A on 2100 magnet | MTM |  | Checked by Stephane and Richard. Outside the coil, in the bus bar Repeatedd with reduced ramp rate 20 A/s. OK |
| Thursday_14_A | TBD1 | Problem with powering CD circuit | IT |  | Server problem. Solved. |
| Thursday_14_N | TBD1 | Not possible to power EF circuit | MTM AB/CO |  | Not correct inductance put in the power seeting. TEMA hung. Many times. Then sunday OK but quenching 3 times below nominal |
| Friday_15_A | TBD1 | MQ strength: Process hung “checking motor status”. Slow PA abort at 11850 A | MTM IT |  | Switch off the motors, reset of the motor controller |
| Friday_15_N | TBA2 | 3224 magnet : Faulty quench when PC switched in stand by mode : inductance value not cortrectly selected. | MTM |  |  |
| Saturday_16_A | SM18 | Oxygen deficiency in SM18 2% below the normal (level was at 19 .1 %): Alarm level 1 (for information) | MTM |  | A.Siemko saked to keep the main entrance door opened. Alarm cleraed 2 h after. |
| Saturday_16_N Sunday _17_M, A | TBD1 | Wire broken during XY measurements in AP2. Server crashed. XY measurements: Values out of tolerances. Wire not coming in the right position. Resistance value not correct (too low,0.1 to 0.3 mOhm). | MTM |  | Relaunched. Stephane, Richard called. Advise to change the DB file. No change. Richard found that wire is touching the anticryostat. Repeated with a smaller path. Repeated, results good and no problem with resistance but still not coming in the right position.: reason : No good alignment bewteen short anticryostat and magnet. |
| Saturday_17_A | TBB1 | Label of the power cable GH and IJ corcetors missing. | MTM |  | A.Siemko asked to keep the main entrance door opened. |
| Sunday_17_A | TBA2 | After quench number 6 faulty quench when we start the ramp (10 A) switching in stand by mode. | AB/PO |  | Richard came and investigated the problem : inside the power supply RMA. He called AB/PO. AB/PO piquet rest the digitla controller. |
| Sunday_17_A | TBB1 | Not possible to power CD circuit. | MTM |  | Richard investigated the problem :with PO team he managed to power the sextupole disabling the quench detection and the feedback loop. It was found that correct inductance to be used in 5 mH and not 18 mH as foreseen. |
| Sunday_17_N | TBC1 | MBAL3234: During first training quench one heater YT121, jump did not discharged completely in the middle of dischage (250 ms after). Vt saturated at 250 V. | MTM |  | Stephane informed. Test stopped.He advise to check: -Resistance of heaters -Electrical integrity. |

# Text boxes

- Light green : Connect (up to Cryo pump down)	24 h

- Blue :  Wait + Cool down				26 h

- Ivory: Tests at Cold					36 h

- Red :  Wait + Warm up					12 h

- Dark Green: Disconnect					12 h