Vc/25-Oct-04

### Week44 starting 25 oct 04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 25Oct 04  ~11.30 hrs

| 4 | A1 | MBAL3226 | PT 6.4 Training 4 | 1.9 |
| --- | --- | --- | --- | --- |
| 7 | A2 | MBAL3230 | Prep 5 Pumping + Cool Down | 2.35 |
| 3 | B1 | SSS068 | Stretched Wire Cold SC12 | 1.9 |
| 11 | B2 | SSS064 | Finished Ready to go Final scan | 298.6 |
| 6 | C1 | MBBL1150 | PT 5.1 1.5 KA Quench LF | 1.9 |
| 1 | C2 | MBBL3164 | PT 12 Warm Up | 188.1 |
| 10 | D1 | SSS014 | CR 1 Leak Test | 297.1 |
| 9 | D2 | SSS065 | CR 1 Leak Test | 297.8 |
| 2 | E1 | MBBL2098 | PT 6.9 Training 9 | 40.2 |
| 12 | E2 | MBBL1128 | ICS 4 Final connection | 298.3 |
| 5 | F1 | MBAL1158 | PT 2 HV Cold Test | 1.9 |
| 8 | F2 | MBAR3049 | Prep 5 Pumping + Cool Down | 95.5 |

10/25/2004 11:23:29 AM    Temperature data are taken from TBSM18 site

Coordinator this week: Pierre P.; MTM support on call :  (16-3602).

13 Magnet tests [ 11 dipoles( 2 with MM)+ 2 SSS +  0 SSSS]

includes 3224 with Thermal cycle so effectively 12 Magnets, i.e.,  12 Disconnected after tests last week ( Sat Midnight to Sat midnight)

SSS & Stretched Wire ( ONLY on d2 at warm from now on) nowhere else

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

## RESULTS FROM LAST WEEK

## Tests

| Magnets under Test from 17-10-2004 to 23-10-2004 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA1 | MBBL3131 |  | 14-10-2004 | 71 h. | 29 h. | 34 h. | 21 h. | 8 h. | 21-10-2004 | 168 hours |  |  |
| 2 | TBA2 | MBAL3224 |  | 13-10-2004 | 32 h. | 31 h. | 76 h. | 13 h. | 0 h. | 19-10-2004 | 144 hours |  |  |
| 3 | TBA2 | MBAL3224 |  | 19-10-2004 | 1 h. | 29 h. | 30 h. | 15 h. | 9 h. | 23-10-2004 | 96 hours |  |  |
| 4 | TBB1 | SSS053 |  | 12-10-2004 | 75 h. | 37 h. | 65 h. | 10 h. | 15 h. | 21-10-2004 | 216 hours |  |  |
| 5 | TBC1 | MBAL3234 |  | 15-10-2004 | 27 h. | 26 h. | 24 h. | 40 h. | 5 h. | 20-10-2004 | 120 hours |  |  |
| 6 | TBC2 | MBAL3233 |  | 12-10-2004 | 27 h. | 40 h. | 24 h. | 29 h. | 6 h. | 17-10-2004 | 120 hours |  |  |
| 7 | TBD1 | SSS062 |  | 11-10-2004 | 50 h. | 19 h. | 97 h. | 7 h. | 36 h. | 20-10-2004 | 216 hours |  |  |
| 8 | TBE1 | MBBR1075 |  | 16-10-2004 | 28 h. | 32 h. | 12 h. | 23 h. | 4 h. | 21-10-2004 | 120 hours |  |  |
| 9 | TBE2 | MBAL3207 |  | 13-10-2004 | 25 h. | 28 h. | 33 h. | 17 h. | 7 h. | 18-10-2004 | 120 hours |  |  |
| 10 | TBF1 | MBAL1156 |  | 17-10-2004 | 21 h. | 35 h. | 15 h. | 21 h. | 14 h. | 22-10-2004 | 120 hours |  |  |
| 11 | TBF1 | MBAL2100 |  | 11-10-2004 | 33 h. | 35 h. | 30 h. | 30 h. | 20 h. | 17-10-2004 | 144 hours |  |  |
| 12 | TBF2 | MBAL3208 |  | 19-10-2004 | 19 h. | 29 h. | 36 h. | 15 h. | 6 h. | 23-10-2004 | 96 hours |  |  |
| 13 | TBF2 | MBAL3227 |  | 14-10-2004 | 22 h. | 24 h. | 39 h. | 17 h. | 6 h. | 19-10-2004 | 120 hours |  |  |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBL3131 | 11720 A. (D2-L-S01) | 12058 A. (D1-U-S01) |  | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAL3224 | 10231 A. (D1_L_S12) | 10637 A. (D2-L-S01) | 11854.6 A. (D2-U-S01) | 11935 A. (D2_U) | 12200 A. (D2_U_S01) | 11966 A. (D2_U_S01) | 12417 A. (D1-L-S12) | 12542 A. (D2-U-S01) | 12616 A. (D1-L-S01) |  | - | - | - |
| 3 | MBAL3224 | 11732 A. (D2_U_S01) | 11971 A. (D2-U-S01) | 12356 A. (D2_U_S12) | 12519 A. (D1-U-S01) | 12585 A. (D1_L) |  | - | - | - | - | - | - | - |
| 4 | SSS053 | 12129 A. (QE_12) | 12067 A. (QI_12) |  | - | - | - | - | - | - | - | - | - | - |
| 5 | MBAL3234 | 12341 A. (D1-U) |  | - | - | - | - | - | - | - | - | - | - | - |
| 6 | MBAL3233 | 9987 A. (D1_U) | 9590 A. (D2-L) | 12049 A. (D1-U) | 12321 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - | - |
| 7 | SSS062 | 11994 A. (QI-34) | 12806 A. (QI-34) |  | - | - | - | - | - | - | - | - | - | - |
| 8 | MBBR1075 | 12561 A. (D2-U) | 12774 A. (D1-L) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAL3207 | 10073 A. (D2 L) | 11257 A. (D1-U) | 12063 A. (D1_L) | 12857 A. | - | - | - | - | - | - | - | - | - |
| 10 | MBAL1156 | 12181 A. (D1-L) | 12556 A. (D1-L) |  | - | - | - | - | - | - | - | - | - | - |
| 11 | MBAL2100 | 11834 A. (D2_U) | 12850 A. (No Data) |  | - | - | - | - | - | - | - | - | - | - |
| 12 | MBAL3208 | 11012 A. (CFB-A2) | 11102 A. (CFB-A2) | 11289 A. (CFB-A2) | 11433 A. (D1_U) | 11579 A. (D1_L) | 11805 A. (D1_L) | 11889 A. (D1_U_S04) |  | - | - | - | - | - |
| 13 | MBAL3227 | 10725 A. (D2_U) | 12254 A. (D1_L) |  | - | - | - | - | - | - | - | - | - | - |

Back to Homepage

| From 17-10-2004 to 23-10-2004 |
| --- |
| - | Bench | Magnet Name | shafts | Start Date . | Connect Time | Wait +Cooling | Cold Tests | Wait +Warming | Disconnect Time | End Date . | Total | Q |
| 1 | TBF2 | MBAL3208 | False | 19-10-2004 | 19 h. | 29 h. | 36 h. | 15 h. | 6 h. | 23-10-2004 | 4 days | 7 |
| 2 | TBF2 | MBAL3227 | False | 14-10-2004 | 22 h. | 24 h. | 39 h. | 17 h. | 6 h. | 19-10-2004 | 5 days | 2 |
| 3 | TBF1 | MBAL1156 | False | 17-10-2004 | 21 h. | 35 h. | 15 h. | 21 h. | 14 h. | 22-10-2004 | 5 days | 2 |
| 4 | TBF1 | MBAL2100 | False | 11-10-2004 | 33 h. | 35 h. | 30 h. | 30 h. | 20 h. | 17-10-2004 | 6 days | 2 |
| 5 | TBE2 | MBAL3207 | False | 13-10-2004 | 25 h. | 28 h. | 33 h. | 17 h. | 7 h. | 18-10-2004 | 5 days | 3 |
| 6 | TBE1 | MBBR1075 | False | 16-10-2004 | 28 h. | 32 h. | 12 h. | 23 h. | 4 h. | 21-10-2004 | 5 days | 2 |
| 7 | TBD1 | SSS062 | False | 11-10-2004 | 50 h. | 19 h. | 97 h. | 7 h. | 36 h. | 20-10-2004 | 9 days | 2 |
| 8 | TBC2 | MBAL3233 | False | 12-10-2004 | 27 h. | 40 h. | 24 h. | 29 h. | 6 h. | 17-10-2004 | 5 days | 4 |
| 9 | TBC1 | MBAL3234 | False | 15-10-2004 | 27 h. | 26 h. | 24 h. | 40 h. | 5 h. | 20-10-2004 | 5 days | 1 |
| 10 | TBB1 | SSS053 | False | 12-10-2004 | 75 h. | 37 h. | 65 h. | 10 h. | 15 h. | 21-10-2004 | 9 days | 2 |
| 11 | TBA2 | MBAL3224 | True | 13-10-2004 | 32 h. | 31 h. | 76 h. | 13 h. | 0 h. | 19-10-2004 | 6 days | 9 |
| 12 | TBA2 | MBAL3224 | True | 19-10-2004 | 1 h. | 29 h. | 30 h. | 15 h. | 9 h. | 23-10-2004 | 4 days | 5 |
| 13 | TBA1 | MBBL3131 | True | 14-10-2004 | 71 h. | 29 h. | 34 h. | 21 h. | 8 h. | 21-10-2004 | 7 days | 2 |

PROBLEMS OF LAST WEEK

| Date | Bench | Problem | Type | Application/soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _19_N | TBA1 | During de-excitation test quench at 9.9 A. | MTM |  |  |
| Wednesday _20_M | TBD1 | IAP@warm final: T sensor gives the value of 237.49 K. | MTM |  | Giorgio checked the resistance value : OK Problem of configuration file. |
| Wednesday _13_A | TBA2 | Faulty quench at 39 Amps when the power converter is switched on to “stand by” mode. | MTM |  |  |
| Wednesday _13_A | TBD1 | Disconnection of the SSS62 while HV test final is being conducted. | ICS/MTM |  |  |
| Thursday _14_M | TBD1 | For resistance measurements power supply (18V ,10 A) was missing. | MTM |  | Richard brought a power supply. |
| Friday _22_M | TBE2 | For IAP @cold, the PLC signals were blocked on TBE1 position. | MTM |  | Giorgio reset the PLC. |
| Friday _22_M | TBB2 | Final HV test : Sextupole vs ground fault: investigation. Test stopped at the step quadrupole vs sextupole”unable to put the megger in remote mode” | MTM | HV | Try to switch off/on the Megger and restart the test. No results. Rack changed. Test performed. Finally : magnet warm up and NC opened. |
| Friday _22_N | TBC2 | Tcoil problem (shaft 22-23) TRU 1 | MTM | T-coil | Guy called. Origin? |
| Friday _22_N | TBD2 | Results show transfer function value lower than allowable limits (SW13). Wire broken. Program stuck. | MTM |  | Test re-launched. Stretched wire installed and test re-launched. Same results. Equip. Support consulted. He advised to continue. Test re-launched to center the wire. |
| Saturday _23_M | TBD2 | Wire broken during Rot wire measurements. | MTM |  | Wire replaced. XY position redone. |
| Saturday _23_M | TBD1 | Leak in the L of the SSS014. O-rin joint not good? | ICS? |  | Test coordinator informed. No spare. Magnet warm till Monday morning. |
| Saturday _23_A | TBD2 | MTM gave to ICS the OK for stripping. Vacuum mot broken when ICS tried to open the big bellow. Dangerous. | ICS/ACR/MTM |  | Change of the TTS is requested. |
| Saturday _23_N | TBB2 | MO corrector Voltage taps values are wrong (OK before connection) | ICS? |  | Power supply connections to EF circuit were reversed with the proposed ones. Inversion during the connections?. On MTF values entered with message not OK for CQW2. NC not opened. To be checked and corrected. |
| Saturday _23_N | TBE1 | Spring in sliding sleeve of the return water connector is broken | MTM |  |  |
| Saturday _23_N | TBD2 | WP17: HV test: Test stuck with the massage”unable to put the megger in remote mode”. | MTM | HV | Try to switch off/on the Megger and restart the test. OK |
| Sunday_24_A | TBA1 | Gamelle Temp sensor shows bad values. | MTM |  | Guy called. He advised to continue as no shaft was in the anti-cryostat. |
| Sunday_24_N | TBF1 | HF heaters discharge at 1.5 kA. One heater did not discharge completely. Resistance checked. OK. HV test performed. | MTM |  | Pierre investigated the problem monday morning. |
| Monday_25_M | TBD2 | Sun hung. | AB/CO |  | Nicolay called Magnus Bjork Monday morning. |
| Monday_25_M | TBB1 | Two SPA aborts occurred during XY measurements. | IT |  |  |