Vc/17-Feb-05

### Week 07 starting 14 Feb 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 14 feb 05 @  2/14/2005 4:00:09 PM    PM

LHC SM18 Magnet Test Facility

| 6 | A1 | MBAL2123 | PT 13.1 IAP @ Warm | 294.46 |
| --- | --- | --- | --- | --- |
| 7 | A2 | MBAR3278 | Prep 5 Pumping + Cool Down | 157.95 |
| 8 | B1 | SSS034 | PT 12 Warm Up | 300.28 |
| 3 | B2 | MBAL3165 | PT 6.1 Training 1 | 4.33 HV |
| 9 | C1 | MBAR3286 | Finished Ready to go Final scan | 295.8 |
| 11 | C2 | MBAL3168 | ICS 1 WP04 HV Test Warm | 295.18 |
| 12 | D1 | SSS003 | BEF3 CQW0 resistance measurement | 295.18 |
| 10 | D2 | SSS107 | ICS 6 Disconnect Magnet WP07 | 296.43 |
| 4 | E1 | MBAL3141 | Prep 5 Pumping + Cool Down | 2.80 HV |
| 1 | E2 | MBBL2146 | PT 6.3 Training 3 | 1.90 |
| 5 | F1 | MBAR3285 | Prep 5 Pumping + Cool Down | 4.25 HV |
| 2 | F2 | MBBR3270 | PT 12 Warm Up | 53.7 |

Coordinator this week: J. Miles; MTM support on call :   16-3602 .

14  Magnets Tested   ( 1193 ???)

10  dipoles( 2 with MM)+ 2  SSS(0  with MM) +  2  SSSS

Disconnected after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Situation on Repair :

      - Silver Shoes bench F etc

General Points

e-Traveller & Paper Traveller

Problems   Power Converters  OK ?

Resistances & HV on SSS in 904

AOB

## Tests

| Magnets under Test from 06-02-2005 to 12-02-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA2 | MBAR3278 |  | 28-01-2005 | 1 h. | 23 h. | 16 h. | 22 h. | 13 h. | 07-02-2005 | 240 hours |  |  |
| 2 | TBA2 | MBAR3284 |  | 07-02-2005 | 33 h. | 39 h. | 38 h. | 15 h. | 9 h. | 12-02-2005 | 120 hours |  |  |
| 3 | TBB1 | SSS612 |  | 01-02-2005 | 44 h. | 27 h. | 37 h. | 16 h. | 20 h. | 07-02-2005 | 144 hours |  |  |
| 4 | TBB1 | SSS614 |  | 07-02-2005 | 18 h. | 24 h. | 11 h. | 12 h. | 7 h. | 10-02-2005 | 72 hours |  |  |
| 5 | TBB2 | MBBL1193 |  | 07-02-2005 | - | - | - | - | - | 11-02-2005 | 96 hours |  |  |
| 6 | TBB2 | MBBL2141 |  | 02-02-2005 | 27 h. | 22 h. | 27 h. | 17 h. | 13 h. | 06-02-2005 | 96 hours |  |  |
| 7 | TBC1 | MBAR3281 |  | 03-02-2005 | 27 h. | 28 h. | 43 h. | 13 h. | 10 h. | 08-02-2005 | 120 hours |  |  |
| 8 | TBD1 | SSS127 |  | 05-02-2005 | 47 h. | 14 h. | 11 h. | 9 h. | 8 h. | 09-02-2005 | 96 hours |  |  |
| 9 | TBD2 | SSS098 |  | 03-02-2005 | 49 h. | 23 h. | 28 h. | 7 h. | 30 h. | 08-02-2005 | 120 hours |  |  |
| 10 | TBE1 | MBAR3279 |  | 08-02-2005 | 23 h. | 25 h. | 18 h. | 13 h. | 14 h. | 12-02-2005 | 96 hours |  |  |
| 11 | TBE1 | MBAR3282 |  | 03-02-2005 | 25 h. | 24 h. | 33 h. | 13 h. | 11 h. | 08-02-2005 | 120 hours |  |  |
| 12 | TBE2 | MBBR3215 |  | 06-02-2005 | 34 h. | 25 h. | 23 h. | 14 h. | 4 h. | 10-02-2005 | 96 hours |  |  |
| 13 | TBE2 | MBBR3245 |  | 02-02-2005 | 22 h. | 26 h. | 19 h. | 14 h. | 8 h. | 06-02-2005 | 96 hours |  |  |
| 14 | TBF1 | MBBR2525 |  | 05-02-2005 | 19 h. | 27 h. | 44 h. | 17 h. | 14 h. | 10-02-2005 | 120 hours |  |  |
| 15 | TBF2 | MBAL3104 |  | 05-02-2005 | 22 h. | 45 h. | 24 h. | 14 h. | 8 h. | 10-02-2005 | 120 hours |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAR3278 | 12048.1 A. (D2-U S01) | 12296 A. (D2_U_S01) |  | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR3284 | 8459 A. (D2_L) | 10884 A. (D2_L) | 11726.5 A. (D2-U) | 12310 A. (D2_U) | 12367 A. (D2-U) | 12665.3 A. (D2-L) | 12765.2 A. (D2-L) | 12634 A. (D2_L) | 12807.8 A. (D2_L) |  | - | - | - |
| 3 | SSS612 | 5482 A. (E-P34) | 5820 A. | - | - | - | - | - | - | - | - | - | - | - |
| 4 | SSS614 | 5820 A. | 5820 A. | - | - | - | - | - | - | - | - | - | - | - | - |
| 5 | MBBL1193 |  | - | - | - | - | - | - | - | - | - | - | - | - |  |
| 6 | MBBL2141 | 11228 A. (D1_U) | 12062 A. (D2-L) |  | - | - | - | - | - | - | - | - | - | - |  |
| 7 | MBAR3281 | 11436 A. (D1_U) | 11721.9 A. (D2-U) | 12179 A. (D1 - U) | 12300 A. (D1-U) | 12490.5 A. (D1_U) | 12614 A. (D1_L) | 12711 A. (D1-U) | 12851 A. (D2-L) | 12850 A. | - | - | - | - |  |
| 8 | SSS127 | 12063.6 A. (QI_12-34) | 12228 A. (QE_34) |  | - | - | - | - | - | - | - | - | - | - |  |
| 9 | SSS098 | 11289 A. (QI-34) | 0 A. (No Data) | 12434.2 A. (QE_34) |  | - | - | - | - | - | - | - | - | - |  |
| 10 | MBAR3279 | 12149 A. (D1-U) | 11657.3 A. (D2-U) | 12738.8 A. (D2-U) | 12850 A. | - | - | - | - | - | - | - | - | - |  |
| 11 | MBAR3282 | 9474 A. (D1 - L) | 11697 A. (D2_L) | 11925.7 A. (D1_U) | 12246.1 A. (D2_U) | 12600 A. (D2-L) | 12798 A. (D2-U) | 12837 A. (D2 - U) | 12850 A. | - | - | - | - | - |  |
| 12 | MBBR3215 | 11780 A. (D2_U) | 12746 A. (D1-L) |  | - | - | - | - | - | - | - | - | - | - |  |
| 13 | MBBR3245 | 10647 A. (D1-U) | 11678 A. (D2-L) | 12593 A. (D1 - U) | 12850 A. | - | - | - | - | - | - | - | - | - |  |
| 14 | MBBR2525 | 11618 A. (D1-U-S01) | 12464 A. (D2_L) |  | - | - | - | - | - | - | - | - | - | - |  |
| 15 | MBAL3104 | 12845 A. (D1_L) | 12487 A. (D1-L) | 12798.2 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - |  |

### Week 7feb05 to 13Feb 05

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _08_M | TBA2 | 1.5KA provoked quench on 2123: For quench location shaft signals were not found. | MTM |  | Maryline called : Qloc cable not conned. Qantenna cable were in place. Qloc cables connected to the rack. |
| Tuesday _08_M | TBF1 | 2525 magnet at 4 K. No HV test possible (interlock). Cannot go down to 1.9 K. Quench at 4.2 K to warm up: SSL at 9170 A. | ACR |  | ACR team working on the CFB.PT142 pressure detector not working. Air leak found in safety valves which block the cool down. 10h lost. Magnet warm up without fast de-excitation test. Wait for warming to repair completely. Reparation done Friday. TC informed He advised to proceed with the warm up. |
| Tuesday _08_A | TBD1 | The Vtaps on E lead is broken, that was creating a trigger on the corresponding card of the auxiliairy POTAIM crate. | MTM |  | Short between double output 10 and 12 done by Maryline. |
| Tuesday _08_A | TBA1 | MM on 2123 magnet. Rotation became bad for the two apertures. | ICS? |  | TC informed. LHC cycle stopped. Coupling in the TRU broken. Repaired by Frederic Tuesday. Measurement repeated. One solution to avoid such a problem: when rotating shafts manually push first the fast stop (which switches of the motors) of each aperture, and only then, rotate shafts carefully and slowly by hand to Qloc horizontal position. |
| Tuesday _08_N Thursday_10_M | TBC1 TBF1 | During IAP warm_LF, interlocks: Mag300_x2 and Mag300air_x2 appear. TT821: 294.39K, cryo T is also 294K Same problem. | ACR |  | Origin: cryo team do not put the bench in correct phase at the given time. Magnet has not to be in the shutdown phase, the phase should be "connecting magnet". Maryline asked ACR team to go in the good phase. |
| Wednesday_09_M | TBE2 | SPA at 1000 A: quench at 850A | AB/PO |  | Maryline called.Piquet Power Supply that solved the problem |
| Wednesday_09_A | TBD1 | TCQW0 (resistance measurement) lower voltage than the expected (at given current). Tsensor resistance value give also no the correct value. | AB/CO | IAP | Resistance measurements and checks of cable give no striking results. |
| Wednesday_09_M | TBA1 | Error in DB while generating HR Config"when Test was launched - LHC_Cycle_FT_Time 300s. Shaft is not rotating correctly. | AB/CO-MTM MTM | HWREC | Maryline contacted. She advised to put off HWREC. |
| Thursday _10_A | TBE | T_reading via video monitor not correct. | ACR |  | Jerome corrected the readings |
| Thursday _10_A | TBB2 | Cryo leak on the 1193 magnet (leak in thermal screen) |  |  | 13h00 of stop. Magnet removed. NC opened. Bottom tray to be changed. |
| Thursday _10_A | TBB1 | Scanning of the magnet name not possible. | ICS |  | Maryline found that the name of magnet on the label is not correct. Name entered manually. |
| Friday _11_M Friday _11_N | TBC1 | HV on MB3286 .(MB/ground) failed : I leak exceed 20 micro A (30 micro A) MB 3286: Quench at 4848 A. Test repeated: quench at 6680 A in the clamp | ICS, ACR? |  | TC leads the investigation: CFB insulation or bad connection. TC asks to proceed with the tests carefully. Investigation on the CFB will be done monday. TC informed: he suggested increasing the He level to 80%. Pierre asked to put the magnet in stand by till Saturday morning. TC asked to repeat the Quench: OK. Test went on normally. Results :Insulation of the CFB correct. Insulation damaged at the end of Vtaps |
| Friday _11_M | TBC2 | Pumping to 1.9 K not possible. Purging of the system badly done. | ACR |  | 6 h lost |
| Friday _11_M | TBD2 | Leak on the safety valve of the CFB | ACR |  | 7 h lost |
| Friday _11_M | TBC2 | Server connectivity problem. DAQ softwares not working | IT? |  |  |
| Friday _11_A | TBC2 | Discharge of heaters when we the PC was switch on |  |  | Solved by Maryline |
| Friday _11_A | TBC2 | During Diode test, heaters got discharged. No quench detected. |  |  | Test repeated. |
| Friday _11_A | TBB1 | SSS034: IAP at warm initial: Errors in Temp sensor . |  |  | T coefficient checked by Maryline : not correct. NC opened. |
| Friday _11_A | TBA2 | Training quench 9 on 3284: No quench detected by AQA. Signals seem OK. | AB/CO | AQA | Boris fixed the problem. |
| Friday _11_N | TBB2 | IAP @ warm: Interlock Mag300_x2 and Mag300air_x2 appear. | ACR |  | Cryo team informed. They were performing tests and they will clear the interlock afterward. |
| Friday _11_N Saturday_12_N | TBD1 TBB1 | HV test on SSS032: condensation on Orbital dipoles. HV test on SSS034 failed for the same reason | MTM |  | Fun connected to blow the air and evaporate the condensation. Condensation on the terminals (fun used in another cluster?). |
| Saturday_12_M | TBD1 | QH test on SSS032: Alarm on tfire. | MTM |  | Test repeated: same error. DAQ sampling faulty. Discharge recorded when the sampling frequency is changing. Proceed with the tests. |
| Saturday_12_M | TBA1 | MM: Shaft position alert at high field. | MTM |  | Maryline advised to continue: It can happen when the positioning is close to the acceptance at low field. |
| Saturday_12_M | TBD1 | Powering of CD circuit of SSS032 not possible: stand by error when switching the power supply. | MTM |  | Maryline checked Diagnostic: clamp Vtaps have probably been inversed during soldering. |
| Saturday_12_M | TBC2 | During the training of the 3253 analysis show that the diode is conducting. | MTM |  | TC informed. He asked to check if the FPA is enable and advised to continue. |
| Saturday_12_N | TBC2 | De-excitation test cannot be launched. Problem in arming lf/hf DQA during training | MTM |  | Maryline informed. She suggested resetting the crates, TEMA, the server. No success. The wrong test was charged. Test performed manually. |
| Sunday_13_M | TBA | MXI error : hf, lf , TEMA re-started | AB/CO | TEMA | TEMA was re-started but correct parameters not re-loaded: D0502130039.ha01 and D05130550.ha2 must be transferred from MBAI123 to MBAI123_2. |
| Sunday_13_M | TBB1 | Powering of corrector not possible on SSS034 | AB/PO |  | Maryline informed AB/PO on call. Problem with regulation loop.600 A reached in manual control |
| Sunday_13_M | TBD2 | Trigger on the CD circuit | ICS? |  | Maryline called Diagnostic : Vtaps of the C clamp that is opened probably at the soldering place. |
| Sunday_13_N | TBE2 | Polarity Selector switch has problems at the end position while turning from "Right" to "Left" Polarity. | MTM |  |  |