Vc/7-Mar-05

### Week 09 starting 28 Feb 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 28 feb 05 @ 2/28/2005 10:11:31 AM

| 7 | A1 | MBBL3235 | Prep 5 Pumping + Cool Down | 4.36 |
| --- | --- | --- | --- | --- |
| 2 | A2 | MBAL2129 | PT 6.2 Training 2 | 1.94 |
| 11 | B1 |  |  | 291.33 |
| 1 | B2 | MBBL2121 | PT 6.7 Training 7 | 14.61 |
| 6 | C1 | MBBL1196 | Prep 5 Pumping + Cool Down | 275.73 |
| 4 | C2 | MBAL2151 | PT 12 Warm Up | 95.62 |
| 12 | D1 |  |  | 290.71 |
| 5 | D2 | SSS080 | Prep 5 Pumping + Cool Down | 79.45 |
| 9 | E1 | MBBL2147 | ICS 4 Final connection | 291.6 |
| 10 | E2 | MBAL2148 | CR 1 Leak Test | 92.05 |
| 8 | F1 | MBBL1199 | CR 1 Leak Test | 91.97 |
| 3 | F2 | MBAL2131 | PT 2 HV Cold Test | 2.87 HV |

Temperature data are taken from TBSM18 site

Coordinator this week: V Chohan; MTM support on call :   16-3602 .

20  Magnets Tested ( not counting 1196 CFB Leak found afterwards)

15  dipoles( 1 with MM)+ 5  SSS(0  with MM) +  0  SSSS

Disconnected after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Situation on Repair :

      - Silver Shoes bench F etc

General Points

SSS & SSW on D1 problems on Fri night

Transport (DBS) & ICS & SSS109 on B1 sitting on bench since Sat night

Power Converters  Slow PA & filter by AB-PO

AOB

| Magnets under Test from 20-02-2005 to 26-02-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA1 | MBBL1186 |  |  | 15-02-2005 | 42 h. | 22 h. | 28 h. | 13 h. | 16 h. | 20-02-2005 | 120 hours |  |  |
| 2 | TBA1 | MBBR3291 |  |  | 20-02-2005 | 38 h. | 25 h. | 23 h. | 14 h. | 6 h. | 25-02-2005 | 120 hours |  |  |
| 3 | TBA2 | MBBR3269 |  |  | 18-02-2005 | 44 h. | 24 h. | 46 h. | 16 h. | 8 h. | 24-02-2005 | 144 hours |  |  |
| 4 | TBB1 | SSS109 |  |  | 23-02-2005 | 21 h. | 17 h. | 20 h. | 11 h. | 14 h. | 26-02-2005 | 72 hours |  |  |
| 5 | TBB1 | SSS110 |  |  | 18-02-2005 | 27 h. | 34 h. | 22 h. | 10 h. | 12 h. | 22-02-2005 | 96 hours |  |  |
| 6 | TBB2 | MBAR3288 |  |  | 17-02-2005 | 37 h. | 31 h. | 25 h. | 15 h. | 9 h. | 21-02-2005 | 96 hours |  |  |
| 7 | TBB2 | MBBL1196 |  |  | 21-02-2005 | 37 h. | - | - | - | - | 23-02-2005 | 48 hours |  |  |
| 8 | TBC1 | MBAL3167 |  |  | 21-02-2005 | 41 h. | 24 h. | 27 h. | 16 h. | 9 h. | 26-02-2005 | 120 hours |  |  |
| 9 | TBC1 | MBBR3276 |  |  | 14-02-2005 | 66 h. | 30 h. | 24 h. | 17 h. | 8 h. | 20-02-2005 | 144 hours |  |  |
| 10 | TBC2 | MBAL1080 |  |  | 19-02-2005 | 19 h. | 29 h. | 45 h. | 21 h. | 12 h. | 25-02-2005 | 144 hours |  |  |
| 11 | TBD1 | SSS073 |  |  | 19-02-2005 | 30 h. | 22 h. | 22 h. | 18 h. | 0 h. | 23-02-2005 | 96 hours |  |  |
| 12 | TBD2 | SSS074 |  |  | 15-02-2005 | 56 h. | 23 h. | 35 h. | 8 h. | 25 h. | 21-02-2005 | 144 hours |  |  |
| 13 | TBD2 | SSS108 |  |  | 21-02-2005 | 31 h. | 17 h. | 14 h. | 12 h. | 17 h. | 25-02-2005 | 96 hours |  |  |
| 14 | TBE1 | MBAL3171 |  |  | 17-02-2005 | 25 h. | 42 h. | 18 h. | 15 h. | 23 h. | 22-02-2005 | 120 hours |  |  |
| 15 | TBE1 | MBBL1194 |  |  | 22-02-2005 | 20 h. | 26 h. | 28 h. | 13 h. | 9 h. | 26-02-2005 | 96 hours |  |  |
| 16 | TBE2 | MBBL3138 |  |  | 16-02-2005 | 26 h. | 25 h. | 54 h. | 13 h. | 11 h. | 21-02-2005 | 120 hours |  |  |
| 17 | TBE2 | MBBR3290 |  |  | 21-02-2005 | 22 h. | 31 h. | 17 h. | 14 h. | 14 h. | 26-02-2005 | 120 hours |  |  |
| 18 | TBF1 | MBBL2139 |  |  | 21-02-2005 | 25 h. | 27 h. | 26 h. | 14 h. | 12 h. | 26-02-2005 | 120 hours |  |  |
| 19 | TBF1 | MBBR3289 |  |  | 17-02-2005 | 26 h. | 29 h. | 26 h. | 13 h. | 11 h. | 21-02-2005 | 96 hours |  |  |
| 20 | TBF2 | MBAR3248 |  |  | 15-02-2005 | 39 h. | 28 h. | 17 h. | 14 h. | 8 h. | 20-02-2005 | 120 hours |  |  |
| 21 | TBF2 | MBBL3153 |  |  | 20-02-2005 | 26 h. | 25 h. | 22 h. | 23 h. | 10 h. | 25-02-2005 | 120 hours |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBL1186 | 12217 A. (D2_U_S12) | 12628.6 A. (D1-U-S13) |  | - | - | - | - | - | - | - | - | - | - |
| 2 | MBBR3291 | 10706 A. (D2-L) | 12527 A. (D1_U) |  | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBR3269 | 12584 A. (D1-L-S11) | 0 A. (No Data) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 4 | SSS109 | 12252 A. (QI_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 5 | SSS110 | 11866 A. (QE_12) | 12673 A. (QE _12) |  | - | - | - | - | - | - | - | - | - | - |
| 6 | MBAR3288 | 11488 A. (D1-L) | 12682 A. (D2_L) |  | - | - | - | - | - | - | - | - | - | - |
| 7 | MBBL1196 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBAL3167 | 11174 A. (D1-L) | 11717 A. (D1-U) | 12294 A. (D2-U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 9 | MBBR3276 | 11756 A. (D1- U) | 12580 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 10 | MBAL1080 | 8764 A. (No Data) | 11609 A. (D2-U) | 11968 A. (D2-U) | 12347 A. (D2-U) | 12500 A. (D1_L) | 12498 A. (D1_L) | 12488 A. (D1_U) | 12758 A. (D2_U) | 12728 A. (D1_L) | 12850 A. | - | - | - |
| 11 | SSS073 | 11447 A. (QI-12) | 12126 A. (QE-12) |  | - | - | - | - | - | - | - | - | - | - |
| 12 | SSS074 | 12147 A. (QI_34) | 11936.1 A. (QE_34) | 12531 A. (QE-34) | 122753.1 A. (QI-34) | 12790 A. (No Data) | 12788.6 A. (QE-34) | 12850 A. | - | - | - | - | - | - |
| 13 | SSS108 | 11990 A. (QI-12) | 12577.8 A. (QE-12) |  | - | - | - | - | - | - | - | - | - | - |
| 14 | MBAL3171 | 12180 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 15 | MBBL1194 | 12087 A. (D1_U) | 12686.8 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 16 | MBBL3138 | 9870 A. (D2-U) | 10344 A. (D1-U) | 11587.4 A. (D1-L) | 11784 A. (D2-L) | 12120 A. (D2_L) | 12248 A. (D2_U) | 12388 A. (D2 - L) | 12556 A. (D1-L) | 12587.7 A. (D2-U) |  | - | - | - |
| 17 | MBBR3290 | 12154 A. (D2_L) | 12091 A. (D1 - L) | 12442 A. (D1-U) |  | - | - | - | - | - | - | - | - | - |
| 18 | MBBL2139 | 9922 A. (D1-U) | 12193 A. (D1-U) |  | - | - | - | - | - | - | - | - | - | - |
| 19 | MBBR3289 | 11776 A. (D2 - U) | 12316 A. (D1-L) |  | - | - | - | - | - | - | - | - | - | - |
| 20 | MBAR3248 | 11532.7 A. (D1-U) | 12117 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 21 | MBBL3153 | 10208 A. (D2-L) |  | - | - | - | - | - | - | - | - | - | - | - |

### Week 20 Feb05 to 26Feb 05  (RECORD so Far 20 Magnets/week)

| From 20-02-2005 to 26-02-2005 |
| --- |
| - | Bench | Magnet Name | shafts | Start Date . | Connect Time | Wait +Cooling | Cold Tests | Wait +Warming | Disconnect Time | End Date . | Total | Q |
| 1 | TBF2 | MBAR3248 | False | 15-02-2005 | 39 h. | 28 h. | 17 h. | 14 h. | 8 h. | 20-02-2005 | 5 days | 2 |
| 2 | TBF2 | MBBL3153 | False | 20-02-2005 | 26 h. | 25 h. | 22 h. | 23 h. | 10 h. | 25-02-2005 | 5 days | 1 |
| 3 | TBF1 | MBBL2139 | False | 21-02-2005 | 25 h. | 27 h. | 26 h. | 14 h. | 12 h. | 26-02-2005 | 5 days | 2 |
| 4 | TBF1 | MBBR3289 | False | 17-02-2005 | 26 h. | 29 h. | 26 h. | 13 h. | 11 h. | 21-02-2005 | 4 days | 2 |
| 5 | TBE2 | MBBL3138 | False | 16-02-2005 | 26 h. | 25 h. | 54 h. | 13 h. | 11 h. | 21-02-2005 | 5 days | 9 |
| 6 | TBE2 | MBBR3290 | False | 21-02-2005 | 22 h. | 31 h. | 17 h. | 14 h. | 14 h. | 26-02-2005 | 5 days | 3 |
| 7 | TBE1 | MBAL3171 | False | 17-02-2005 | 25 h. | 42 h. | 18 h. | 15 h. | 23 h. | 22-02-2005 | 5 days | 1 |
| 8 | TBE1 | MBBL1194 | False | 22-02-2005 | 20 h. | 26 h. | 28 h. | 13 h. | 9 h. | 26-02-2005 | 4 days | 2 |
| 9 | TBD2 | SSS074 | False | 15-02-2005 | 56 h. | 23 h. | 35 h. | 8 h. | 25 h. | 21-02-2005 | 6 days | 6 |
| 10 | TBD2 | SSS108 | False | 21-02-2005 | 31 h. | 17 h. | 14 h. | 12 h. | 17 h. | 25-02-2005 | 4 days | 2 |
| 11 | TBD1 | SSS073 | False | 19-02-2005 | 30 h. | 22 h. | 22 h. | 18 h. | 0 h. | 23-02-2005 | 4 days | 2 |
| 12 | TBC2 | MBAL1080 | False | 19-02-2005 | 19 h. | 29 h. | 45 h. | 21 h. | 12 h. | 25-02-2005 | 6 days | 9 |
| 13 | TBC1 | MBAL3167 | False | 21-02-2005 | 41 h. | 24 h. | 27 h. | 16 h. | 9 h. | 26-02-2005 | 5 days | 3 |
| 14 | TBC1 | MBBR3276 | False | 14-02-2005 | 66 h. | 30 h. | 24 h. | 17 h. | 8 h. | 20-02-2005 | 6 days | 2 |
| 15 | TBB2 | MBAR3288 | False | 17-02-2005 | 37 h. | 31 h. | 25 h. | 15 h. | 9 h. | 21-02-2005 | 4 days | 2 |
| 16 | TBB2 | MBBL1196 | False | 21-02-2005 | 37 h. | 100 h. | -99 h. | 99 h. | -99 h. | 23-02-2005 | 2 days | 0 |
| 17 | TBB1 | SSS109 | False | 23-02-2005 | 21 h. | 17 h. | 20 h. | 11 h. | 14 h. | 26-02-2005 | 3 days | 1 |
| 18 | TBB1 | SSS110 | False | 18-02-2005 | 27 h. | 34 h. | 22 h. | 10 h. | 12 h. | 22-02-2005 | 4 days | 2 |
| 19 | TBA2 | MBBR3269 | False | 18-02-2005 | 44 h. | 24 h. | 46 h. | 16 h. | 8 h. | 24-02-2005 | 6 days | 2 |
| 20 | TBA1 | MBBL1186 | True | 15-02-2005 | 42 h. | 22 h. | 28 h. | 13 h. | 16 h. | 20-02-2005 | 5 days | 2 |
| 21 | TBA1 | MBBR3291 | False | 20-02-2005 | 38 h. | 25 h. | 23 h. | 14 h. | 6 h. | 25-02-2005 | 5 days | 2 |

OP statistics for SM18 OP during the period from 21/02/2005 06:00:00 to 28/02/2005 13:00:00

| Lines | n Super Cycle | in Faults | Availabilities (%) |
| --- | --- | --- | --- |
| TBA1 | 143 [h] | 48 [min] 34[s] | 99.43 |
| TBA2 | 143 [h] | 7 [h] 44 [min] 26[s] | 94.59 |
| TBB1 | 143 [h] | 6 [h] 26 [min] 29[s] | 95.5 |
| TBB2 | 146 [h] 50 [min] 44[s] | 15 [h] 26 [min] 30[s] | 89.48 |
| TBC1 | 143 [h] | 1 [h] 08 [min] 34[s] | 99.2 |
| TBC2 | 143 [h] | 10 [h] 00 [min] 34[s] | 93 |
| TBD1 | 143 [h] | 12 [h] 02 [min] 39[s] | 91.58 |
| TBD2 | 143 [h] | 28 [min] 34[s] | 99.67 |
| TBE1 | 143 [h] | 28 [min] 34[s] | 99.67 |
| TBE2 | 143 [h] | 15 [h] 05 [min] 55[s] | 89.44 |
| TBF1 | 143 [h] | 14 [h] 09 [min] 22[s] | 90.1 |
| TBF2 | 143 [h] | 16 [h] 58 [min] 33[s] | 88.13 |
| TOTAL: | 1719 [h] 50 [min] 44[s] | 100 [h] 48 [min] 44[s] | 94.14 |
| Faults Groups | Faults Names | Duration |
| Cryogenics | Cryo NOT OK | 4 [h] 59 [min] 18[s] |
|  | Miscellaneous | 11 [h] 27 [min] 12[s] |
| Electronics | ----- | 01 [h] 30 [min] |
| HV insulation | ----- | 11 [h] 13 [min] 20[s] |
| HW recognition | ----- | 30 [min] 30[s] |
| Hardware | Miscellaneous | 1 [h] 56 [min] 52[s] |
|  | PLC SE | 01 [h] 02 [min] |
|  | Power converters | 8 [h] 30 [min] 11[s] |
| ICS | ----- | 02 [h] |
| Miscellaneous | ----- | 21 [h] 47 [min] 24[s] |
| Protection systems | ----- | 4 [h] 53 [min] 18[s] |
| Software | Acq programs | 07 [h] |
|  | Test master | 03 [h] 19 [min] |
| Trigger | ----- | 5 [h] 17 [min] 55[s] |

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _22_A | TBC2 | AQA current reading and HF current reading have 200A of difference. | AB-CO |  | Meantime Giorgio advised to continue, writing both value from Vmeter and AQA. AQA changed the ADC card. |
| Tuesday _22_N | TBF2 | Training quench of MB3153 at 10550 A. Red alarms: DTV , Iearth.. | MTM |  | HV test performed at cold hereafter. Lf heaters not insulated. Quench at 1.5 kA lf was also not OK (Iearth alarm, Resistance too high). |
| Wednesday_23_M | TBB2 | Cryo leak on the 1196 magnet |  |  | Magnet removed. NC opened. |
| Wednesday_23_N Thursday _24_M | TBE, TBC | Automatic recognition of the MB name not working. | ? | HV | Name entered manually. TEMA had not been launched once before. |
| Wednesday_23_N | TBF1 | Hf provoked quench at 1.5 kA on MB2139. no quench detected. Quench repeated | AB/CO |  | Signals checked and are OK MXI errors occurred. Error during arming. Switch off all the 3 crates. Then OK |
| Thursday_24_N | TBD1 | HWREC configuration files missing. | MTM | HWREC | Giorgio came and created the files. |
| Thursday_24_N Friday_25_N |  | Problem in pumping TBD1, TBE1, TBB1 (cold compressor?) Same problem. | ACR |  | Stop of powering magnets (0h.30) |
| Thursday_24_N | TBD1 | MM1 on MQ114: slow PA occurred. | AB/PO |  | FGC Digital interface changed in RM.D by Q.King. (Analog filter present which can avoid spurious signals) |
| Thursday_24_N | TBD1 | MM1 on MQ114: Bad absolute signal in sector 10-11 of aperture 2 | MTM |  | Problem fixed by Maryline friday Morning (connector pin not well connected). |
| Friday_25_N Saturday_26_A | TBD1 | Not possible to power SSS73 | AB/PO |  | Giorgio advised to change the CPU card (Dig.Con loop)with that of RMF.OK Giorgio installed a spare card in TBD. Informed PO and Q.King in order to re-establish the normal configuration |
| Saturday_26_M | TBE2, TBF1 | Name confusion of magnet between E2 (1199) and F1 bench (2148) | ICS |  | Giorgio, ICS informed. Correction performed on the travellers and on SMTMS system. |
| Saturday_26_M | TBD1 | Strength meas. wrong | MTM |  | TC informed. He found that a cable in the Keithley was faulty. Measurement repeated. OK after the fourth trial. |
| Saturday_26_N | TBD1 | Training 3 on SSS73 (second run) | MTM |  | File saved in the wrong folder (Test 1) |
| Sunday_27_M | TBA2 | Shaft 29/30 installed for MM. ICS informed OP team leader that shaft29 is hardly rotating. | MTM |  | Giorgio proposed to leave the shaft in MM position. He suspected that the problem came from a bas alignment in short/long anticryostats |
| Sunday_27_A | TBA1 | Tanticryostat lower than 20 degrees. No power heating. | MTM |  | Giorgio informed. He performed many checks and changed the cable from the fixed box in the CFB side to the short anticryostat. Then OK. |
| Monday_28_M | TBD1 | SSS100: Magnet name not correct. | MTM |  | Fixed by Maryline (correct name taken from MTF). |
| Monday_28_M | TBF1 | RMF could not be powered | MTM |  | Fast stop pushed (intervention for the change of the DICO card). Fast stop removed. Then OK. |

Top of Form

Bottom of Form