vc/21-Jul-05

### Week 29  starting 18 July 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  17 July 05 @: 7/18/2005 1:08:55 PM

| 3 | A1 | MBBL2189 | Prep 5 Cool Down | 102.35 |
| --- | --- | --- | --- | --- |
| 6 | A2 | MBAL2051 | Prep 5 Cool Down | 260.84 |
| 7 | B1 | SSS199 | ICS 4 Final connection | 300.46 |
| 10 | B2 | SSS036 | Prep 2.2 IAP @ warm HF | 301.17 |
| 5 | C1 | MBAR3369 | Prep 5 Cool Down | 289.19 |
| 4 | C2 | MBBL3085 | PT 13.1 IAP @ Warm | 299.11 |
| 2 | D1 | SSS217 | PT 12 Warm Up | 100.57 |
| 1 | D2 | SSS617 | Prep 5 Cool Down | 3.73 HV |
| 9 | E1 | MBAL3109 | ICS 4 Final connection | 301.35 |
| 11 | E2 | MBAR3373 | PT 14 Magnet MAPS | 301.89 |
| 12 | F1 | MBBL2206 | PT 14 Magnet MAPS | 300.55 |
| 8 | F2 | MBBL3126 | Prep 5 Cool Down | 300.82 |

Temperature data are taken from TBSM18 site

Coordinator this week: Marco;MTM support 16-3602

14 complete Magnet Tests cycles   (no ROBTC this week )

11 dipoles( 2 with MM )+ 2 SSS( 1  with MM & SSW ) +  1 SSSS

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- General Points  :

- Special SSSS (Jacques)

- Special Tests D1: 217

- Special Tests B1 : Connection cryostat(CC)

- AOB

## Tests

| Magnets under Test from 10-07-2005 to 16-07-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBBR3365 |  |  | 08-07-2005 | 26 h. | 19 h. | 25 h. | 16 h. | 12 h. | 12-07-2005 | 98 h. | Stripping |  |  |
| 2 | TBA2 | MBAR3306 |  |  | 11-07-2005 | 30 h. | 25 h. | 16 h. | 16 h. | 16 h. | 15-07-2005 | 103 h. | Stripping |  |  |
| 3 | TBB1 | SSS174 |  |  | 10-07-2005 | 31 h. | 15 h. | 13 h. | 11 h. | 13 h. | 13-07-2005 | 83 h. | Stripping |  |  |
| 4 | TBC1 | MBAL1245 |  |  | 11-07-2005 | 39 h. | 26 h. | 18 h. | 12 h. | 21 h. | 16-07-2005 | 116 h. | Stripping |  |  |
| 5 | TBC1 | MBBL2197 |  |  | 07-07-2005 | 27 h. | 23 h. | 20 h. | 14 h. | 15 h. | 11-07-2005 | 99 h. | Stand By |  |  |
| 6 | TBC2 | MBBL3156 |  |  | 09-07-2005 | 37 h. | 31 h. | 34 h. | 15 h. | 12 h. | 15-07-2005 | 129 h. | Stripping |  |  |
| 7 | TBD1 | SSS203 |  |  | 29-06-2005 | 46 h. | 42 h. | 126 h. | 10 h. | 41 h. | 10-07-2005 | 265 h. | Stripping |  |  |
| 8 | TBD2 | SSS643 |  |  | 11-07-2005 | 32 h. | 12 h. | 7 h. | 16 h. | 26 h. | 15-07-2005 | 93 h. | Stand By |  |  |
| 9 | TBE1 | MBAR3323 |  |  | 05-07-2005 | 45 h. | 34 h. | 15 h. | 14 h. | 18 h. | 10-07-2005 | 126 h. | Stripping |  |  |
| 10 | TBE1 | MBBR3292 |  |  | 11-07-2005 | 31 h. | 30 h. | 26 h. | 17 h. | 18 h. | 16-07-2005 | 122 h. | Stripping |  |  |
| 11 | TBE2 | MBAL1244 |  |  | 09-07-2005 | 31 h. | 24 h. | 17 h. | 15 h. | 20 h. | 13-07-2005 | 107 h. | Stand By |  |  |
| 12 | TBF1 | MBAL3114 |  |  | 09-07-2005 | 33 h. | 27 h. | 17 h. | 16 h. | 9 h. | 13-07-2005 | 102 h. | Stripping |  |  |
| 13 | TBF2 | MBAR3349 |  |  | 10-07-2005 | 30 h. | 23 h. | 52 h. | 12 h. | 17 h. | 16-07-2005 | 134 h. | Stripping |  |  |
| 14 | TBF2 | MBBL1238 |  |  | 05-07-2005 | 39 h. | 25 h. | 14 h. | 14 h. | 18 h. | 10-07-2005 | 110 h. | Stripping |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR3365 | 10720 A. (D2-U-S01) | 12652 A. (D1_L_S13) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR3306 | 8780 A. (D1-U) | 12713 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 3 | SSS174 | 11834.1 A. (QE_34) | 12230 A. (QE-12) | 12398.9 A. (QI-34) |  | - | - | - | - | - | - | - | - | - |
| 4 | MBAL1245 | 12375 A. (D1-L) | 12355.1 A. (D2_U) | 12772 A. (D2-L) |  | - | - | - | - | - | - | - | - | - |
| 5 | MBBL2197 | 10396 A. (D2-L) | 10895 A. (D1-U) | 12542 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 6 | MBBL3156 | 9947 A. (D2-U) | 11381 A. (D1-U) | 11937 A. (D2 - U) | 12087 A. (D2 - U) | 12409 A. (D2 - L) | 12624.2 A. (D2-U) | 12755 A. (D1_L) | 12851 A. (D2_L) | 12850 A. | - | - | - | - |
| 7 | SSS203 | 12068 A. (QE_34) | 12318 A. (QE_12) | 12421 A. (QI_34) |  | - | - | - | - | - | - | - | - | - |
| 8 | SSS643 | 5650 A. (MQ_I_12) | 5820 A. | - | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAR3323 | 12271 A. (D1-L) | 12668 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBR3292 | 12591 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 11 | MBAL1244 | 11779.6 A. (D1_L) | 12495 A. (D1-L) | 12850 A. (D2-L) |  | - | - | - | - | - | - | - | - | - |
| 12 | MBAL3114 | 10041 A. (D2-U) | 12330 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 13 | MBAR3349 | 0 A. (No Data) | 10226 A. (D2_U_S13) | 10992 A. (D1-L-S01) | 12848.5 A. (D1_L_S01) | 12850 A. | - | - | - | - | - | - | - | - |
| 14 | MBBL1238 | 10903.9 A. (D1_U) | 12493.4 A. (D1_L) | 12459 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |

### SSW was done at warm , at  cold & again at warm on SSS203 on D1 = 265 hrs  total

SM18 Operation issues – July 2005, Thu 14 to Tue 19

| Date | TB | Magnet | Team | Problem | Solution |
| --- | --- | --- | --- | --- | --- |
| Wed 13, 01:56 | C2 | 3156 | AB/CO | Server not responding | Sun reset by MTM op (Florence ?) |
| Thu 14, 10:00 |  |  | AT/ACR | Cryo is slow | No solution. First priority given to SSS217 (TBD1) for long-term fatigue test. |
| Thu 14, 16:25 | C1 | 1245 | AT/MTM | Q during SPA @ 1672A | Marco suggests to repeat test (magnet safety not in danger) |
| Fri 15, 09:20 | B2 | 204 | AT/MTM | 1.3V offset in Q-I-E | Marylin investigates, no result ? |
| Fri 15, 10:09 | D1 | 217 | AT/MTM | Nominal current not reached during EF corrector powering | Eric switched to the right configuration. |
| Fri 15, 19:58 | A1 | 2189 | AT/MTM | (Markus) | Richard corrects wrong gains of Potaim card 3, Ch. 1 |
| Fri 15, 22:20 | D1 | 217 | AT/MTM | SPA after 9 minutes @ Iultimate | No explanation found, probable cryo instability (test repeated) |
| Sat 16, 02:20 | B2 | 204 | AT/MTM | Q during SPA @ 11410A. Test repeated, and the Q occurred a second time. | Richard investigates and finds a probable short on a parallel protection resistor. The trigger threshold is temporarily increased by a factor 3 to allow the SPA to proceed. Later warm measurements, however, are OK and do not confirm this hypothesis. Magnet put in standby. |
| Sat 16, 08:30 | A1 | 2189 | AT/MTM | Q during SPA @ 10220A. | Test was repeated successfully. |
| Sat 16, 13:28 | F1 | 2206 | AT/MTM | False trigger on HF. LF show error loading config file. (Guy ?) | Unexplicable. |
| Sat 16, 16:21 | E1 | 3292 | ICS | ROCLA arrives early on the bench (same as on A2 bench on Fri) | Is this a problem ? |
| Sat 16, 16:40 | A1 | 2189 (?) | AT/MTM | Q during SPA @ 8293A. | Unexpla |
| Sun 17, 13:56 | C2 | 3085 | AT/MTM | Q in the busbars @ PT5.2. | Richard finds a very symmetric quench, which is detected only outside of the magnet. Go on with the test. |
| Sun 17, 23:37 | B2 | 036 | ICS | Connections appear to have been re-labeled. | Re-labeling is correct (sick magnet). |
| Sun 17, 04:56 | B2 | ?? | AT/MTM | Unable to launch IAP final due to cryo interlock. (Eric ?) | OK after TEMA reset. |