### N. CHOHAN/E. VEYRUNES/01-August-05

### Week 31  starting 01 Aug 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  01 August 05 : 8/1/2005 3:40:33 PM

| 6 | A1 | MBAL2079 | Prep 5 Cool Down | 290.98 |
| --- | --- | --- | --- | --- |
| 4 | A2 | MBBR3381 | Prep 5 Cool Down | 2.35 |
| 10 | B1 |  |  | 298.04 |
| 12 | B2 |  |  | 298.49 |
| 9 | C1 | MBBR3311 | ICS 1 WP04 HV Test Warm | 297.41 |
| 3 | C2 | MBAL1227 | PT 12 Warm Up | 205.88 |
| 8 | D1 |  |  | 297.86 |
| 11 | D2 | SSS607 | ICS 4 Final connection | 297.77 |
| 5 | E1 | MBAL1178 | Prep 3 CDW1 HV | 299.11 |
| 2 | E2 | MBAR3368 | PT 13.2 Resist. Meas. | 302.52 |
| 7 | F1 | MBAR3375 | ICS 3 Traveller after warm test | 297.15 |
| 1 | F2 | MBBR3379 | PT 13.2 Resist. Meas. | 299.65 |

Coordinator this week: Nicolay Smirnov; Federico Chiusano MTM support 16-3602

16 complete Magnet Tests cycles

12 dipoles ( 3 with MM )+ 4 SSS(without MM & SSW )

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

General Points :

- Special S4 (Jackie)

- Rotary Switch for Corrector powering (awaiting Giorgio?).

- Cluster F “INTERCOM Box” repair (awaiting Giorgio?).

Some details  for the  last  month’s (July 05)  tests output:

- Early July (29June—10July) SSS203 had SSW done at warm,  cold & warm again – a time consuming exercise for ssw systems tests; + it had full shafts m’ments as well

- 2051  :[ tested 9 days Between  15 July-24 July]

FOUR  4.4K SSL Tests were  done (= ~12 hrs).

:’ Optical tests’ Effect of Field on light tests (floor level)   6 hrs

    - -Extra HV Vclamp vs dipole.

- Fatigue Test SSS217 on D1 ( extra ~62 Hours). Total ~ 9 Days

- 3336 : Warm and Cold SSW in a dipole  ( > 38 Hours).  Weekend  magnet cold  kept to do cold SSW on Monday , config files, Survey issues,  experts missing etc

- Silver Shoe Repair on D2 before bringing in Q4 (sss607)

So Bench D2 empty for this  repair work over weekend 23rd july + some weekdays 25/26 july

- Over the weekend of 30/31 July no further work could be be done on D2 because connection by experts was stopped on Fri evening 29th July  & would only resume on Monday 1 Aug

- Benches B1 & B2 need conversion to Dipole &/or Connection cryostat because no more SSS ‘s available. Hence Benches remained empty substantially since weekend of 30/31July05

- New Type of correction connections on SSS meant lot of problems on ICS side & several re-openings after connection( c17 D19 , E13 ,F11  INSTEAD of previous) & much time Lost in connection

In July, the arc-SSS [Wait+cooling time]  went up to avrg. 31 hrs instead of ~ 20 hr avrg in previous months due to SSS199 on B1 in cohabitation with B2 and SSS036  having many HV tests during cooldown(during working hrs Mon-Fri), blocking any useful progress on B1 bench SSS199  in cooling down faster even though process was launched

| Magnets under Test from 24-07-2005 to 30-07-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBAR3371 |  | 25-07-2005 | 35 h. | 31 h. | 30 h. | 18 h. | 8 h. | 30-07-2005 | 122 h. | Stripping |
| 2 | TBA1 | MBBL1233 |  | 20-07-2005 | 37 h. | 24 h. | 18 h. | 14 h. | 21 h. | 25-07-2005 | 114 h. | Stripping |
| 3 | TBA2 | MBAL2051(2) |  | 15-07-2005 | 49 h. | 67 h. | 68 h. | 19 h. | 20 h. | 24-07-2005 | 223 h. | Stand By |
| 4 | TBA2 | MBAL2170 |  | 24-07-2005 | 30 h. | 21 h. | 37 h. | 23 h. | 18 h. | 30-07-2005 | 129 h. | Stripping |
| 5 | TBB1 | SSS173 |  | 23-07-2005 | 38 h. | 14 h. | 16 h. | 8 h. | 14 h. | 26-07-2005 | 90 h. | Stripping |
| 6 | TBB2 | SSS036(5) |  | 17-07-2005 | 11 h. | 92 h. | 34 h. | 11 h. | 26 h. | 25-07-2005 | 174 h. | Stand By |
| 7 | TBB2 | SSS195 |  | 25-07-2005 | 48 h. | 14 h. | 20 h. | 9 h. | 10 h. | 30-07-2005 | 101 h. | Stand By |
| 8 | TBC1 | MBBR3360 |  | 22-07-2005 | 28 h. | 21 h. | 14 h. | 12 h. | 18 h. | 26-07-2005 | 93 h. | Stripping |
| 9 | TBC2 | MBBL3121 |  | 23-07-2005 | 41 h. | 25 h. | 26 h. | 15 h. | 12 h. | 29-07-2005 | 119 h. | Stripping |
| 10 | TBD1 | SSS152 |  | 22-07-2005 | 40 h. | 15 h. | 19 h. | 8 h. | 22 h. | 26-07-2005 | 104 h. | Stand By |
| 11 | TBE1 | MBBL3115 |  | 22-07-2005 | 35 h. | 21 h. | 21 h. | 13 h. | 27 h. | 27-07-2005 | 117 h. | Stripping |
| 12 | TBE2 | MBAL1207 |  | 24-07-2005 | 36 h. | 22 h. | 16 h. | 15 h. | 10 h. | 28-07-2005 | 99 h. | Stripping |
| 13 | TBE2 | MBAL1243 |  | 18-07-2005 | 25 h. | 43 h. | 37 h. | 16 h. | 13 h. | 24-07-2005 | 134 h. | Stripping |
| 14 | TBF1 | MBBL1195 |  | 26-07-2005 | 33 h. | 21 h. | 17 h. | 22 h. | 10 h. | 30-07-2005 | 103 h. | Stripping |
| 15 | TBF1 | MBBR3336 |  | 18-07-2005 | 62 h. | 14 h. | 74 h. | 15 h. | 23 h. | 26-07-2005 | 188 h. | Stripping |
| 16 | TBF2 | MBAR3367 |  | 22-07-2005 | 63 h. | 23 h. | 14 h. | 14 h. | 31 h. | 28-07-2005 | 145 h. | Stripping |
| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| 1 | MBAR3371 | 12850 A. (D1-U-S13) | 12850 A. | - | - | - | - | - | - | - | - |
| 2 | MBBL1233 | 12133.5 A. (D1_L) | 12527.2 A. (D2_L) | 12850 A. (D1_L) |  | - | - | - | - | - | - |
| 3 | MBAL2051 | 11995 A. (D1-MRB) | 12592 A. (CF-S04-A) | 12640 A. (D1-U-MRB) | 12639.2 A. (D1-U) | 12645 A. (D1-U) | 12649.4 A. (D1_U) |  | - | - | - |
| 4 | MBAL2170 | 11565 A. (D1-L-S01) | 12228 A. (D2-U-S01) | 12443 A. (D1-U-S01) | 12636 A. (D2_L_S01) |  | - | - | - | - | - |
| 5 | SSS173 | 12130.3 A. (QI--12) | 12329.9 A. (QI-34) | 12534.7 A. (QE_34) |  | - | - | - | - | - | - |
| 6 | SSS036 | 12281 A. (QE-34) | 12818 A. (QI-12) | 12800 A. (QI-12) |  | - | - | - | - | - | - |
| 7 | SSS195 | 11103 A. (QI-12) | 12108 A. (QI-12) | 12761 A. (QI-12) |  | - | - | - | - | - | - |
| 8 | MBBR3360 | 12136 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - |
| 9 | MBBL3121 | 9596 A. (D1_U) | 12050.8 A. (D1-U) | 11746 A. (D1_L) | 12651 A. (D1-U) | 12829.8 A. (D2-U) | 12850 A. | - | - | - | - |
| 10 | SSS152 | 12129 A. (QI_34) | 12291 A. (QI_12) | 12548 A. (QE-12) |  | - | - | - | - | - | - |
| 11 | MBBL3115 | 10691.1 A. (D1_L) | 11786 A. (D1-U) | 12351 A. (D2-L) | 12850 A. | - | - | - | - | - | - |
| 12 | MBAL1207 | 12536 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - |
| 13 | MBAL1243 | 11703 A. (D1-L) | 11842.4 A. (D1_L) | 12133 A. (D2-L) | 12297 A. (D2-L) | 12437 A. (D1-U) | 12588 A. (D1_L) | 12667.2 A. (D1-L) | 12824.6 A. (D1-L) | 12850 A. | - |
| 14 | MBBL1195 | 12342 A. (D2-L) | 12867 A. | - | - | - | - | - | - | - | - |
| 15 | MBBR3336 | 10515.2 A. (D2-U) | 11971 A. (D2_U) | 12193 A. (D2-U) | 12439.5 A. (D1_U_S11) | 12745 A. (D1_L_S02) | 12850 A. | - | - | - | - |
| 16 | MBAR3367 | 9603.9 A. (D2_L) | 12323 A. (D2 - L) | 12573.3 A. (D2-U) |  | - | - | - | - | - | - |

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _26_A | TBA1 | ICS informed that resistance R2 of short anticryostat (22)in Ap.2 not OK. | MTM |  | Salem is being informed. |
| Tuesday _26_A | TBC2 | Problem with the polarity switch. Difficult to change from right to left | MTM |  | AB/PO has solved the problem. |
| Tuesday _26_A | TBD1 | Cryo problem: Compressor problem, not able to pump. | ACR |  | After 2 hours Cryo OK. |
| Tuesday _26_N | TBF2 TBC2 | Water Leak (Mark with a brown tape for F2, TCR has been called for C2 according Richard indication) | MTM |  | Leak always present on Monday 01 August for C2, Mechanics people of SM18 has been informed. |
| Wednesday _27_A | TBF2 | Federico called, concerning quench currents on 3rd and 4th training of MBBR3336. voltmeter values show 15 amps higher than HF (AQA) values. He asks us to modify CDPT file, via SMTMS, to show the AQA current. | MTM |  | Resolved for next quench, may be a offset in voltmeter. |
| Wednesday _27_N | TBB2 | PC fault. We can't launch PT4. On PC rack downstairs, PC FAST is active on interlock module and not resetable (even in local). We will inform equipment support around 07h00 but suspect PO crew has to come. | OP |  | Stop button was press after PO intervention. |
| Thursday _28_M Saturday_30_M | TBA1 TBE1 | MBAR3371 SPA at 1406 during PT 5.1 provoked quench at 1500A. Cryo interlock not OK. water condensation on current leads | ACR/ MTM |  | Fun used to reduce the condensation. |
| Thursday_28_N Saturday_30_M | TBB1 | PROBLEM WITH HV RACK (XMT.MY95). NO COMMUNICATION BETWEEN PLCSE AND PLC HV. PROBLEM MAY BE WITH THE HV RACK AND NO SPARE HV RACK IS AVAILABLE SO TEST HAS BEEN POSTPONED FOR THE TIME BEING. (SSS173)-Only one Mobile Rack(XMT.MY93) is available for HV. After F1, test has been launched on B1. | MTM |  | Richard Situation ? |
| Sunday _31_A | TBA2 | Magnet detrained in the warm-up quench (3rd Ramp). Test coordinator advised to perform another training quench (4th Ramp). | MTM |  | Magnet reach ULTIMATE 4th ramp. |
| Sunday _31_N | TBC2 | De-Excitation. The Power application did not stop at 12000A, it continued ramping to 12850 (Good magnet!) The configuration was correct in Tema, but the Target Current was 12850 in the Power application. | MTM |  | ? |

# Text boxes

Green Connect + Pump down /Blue :  Wait + Cool down	Ivory: Tests at Cold (36 hr)Red :  Wait + Warm up (12 hr)	  Dark Green: Disconnect (8 hr)