### CHOHAN /12-sept 05

### Week 37 starting 12 Sept 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  12 Sept 05 : 9/12/2005 3:32:43 PM

| 6 | A1 | MBAL3391 | PT 6.1 Training 1 | 13.36 |
| --- | --- | --- | --- | --- |
| 9 | A2 | MBAL3402 | ICS 4 Final connection | 296.25 |
| 2 | B1 | MBAL1230 | Prep 5 Cool Down | 126.43 |
| 8 | B2 | MBBL1197 | Prep 5 Cool Down | 93.66 |
| 7 | C1 | MBBL1217 | PT 6.2 Training 2 | 4.40 HV |
| 10 | C2 | MBAL2138 | Prep 5 Cool Down | 299.56 |
| 11 | D1 | SSS293 | ICS 3 Traveller after warm test | 295.8 |
| 5 | D2 | SSS606 | PT 6.14 Training 14 | 2.35 |
| 4 | E1 | MBAL3392 | PT 13.2 Resist. Meas. | 303.05 |
| 1 | E2 | MBBL2188 | PT 12 Warm Up | 10.64 |
| 3 | F1 | MBAL2177 | PT 6.3 Training 3 | 1.90 |
| 12 | F2 | MBBL2143 | ICS 4 Final connection | 295.18 |

Tempr. from TBSM18 site

Coordinator this week: marco; MTM support Richard 16-3602

17 complete Magnet Tests cycles

Only 14 dipoles ( 2 with MM )+ 1 SSS(without MM & SSW )

+1 ssss (606)  underwent Thermal cycle   Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Special  Points :

- B2 & B1 back to SSS?  { B1 after 1230 is over ]

- Special SSS 606(Q5) on D2

- 1017 coming?

## Tests

| Magnets under Test from 04-09-2005 to 10-09-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBBR3333 |  |  | 03-09-2005 | 33 h. | 24 h. | 51 h. | 14 h. | 25 h. | 10-09-2005 | 147 h. | Stripping |  |  |
| 2 | TBA2 | MBBL1188 |  |  | 02-09-2005 | 38 h. | 38 h. | 18 h. | 18 h. | 12 h. | 07-09-2005 | 124 h. | Stripping |  |  |
| 3 | TBB1 | MBBR3382 |  |  | 31-08-2005 | 74 h. | 29 h. | 29 h. | 17 h. | 12 h. | 07-09-2005 | 161 h. | Stripping |  |  |
| 4 | TBB2 | MBBL2144 |  |  | 30-08-2005 | 49 h. | 22 h. | 26 h. | 19 h. | 21 h. | 05-09-2005 | 137 h. | Stripping |  |  |
| 5 | TBB2 | MBBL2199 |  |  | 05-09-2005 | 39 h. | 23 h. | 22 h. | 21 h. | 9 h. | 10-09-2005 | 114 h. | Stripping |  |  |
| 6 | TBC1 | MBBL2218 |  |  | 05-09-2005 | 22 h. | 20 h. | 22 h. | 16 h. | 9 h. | 08-09-2005 | 89 h. | Stripping |  |  |
| 7 | TBC1 | MBBR1258 |  |  | 30-08-2005 | 37 h. | 22 h. | 29 h. | 20 h. | 38 h. | 05-09-2005 | 146 h. | Stripping |  |  |
| 8 | TBC2 | MBAL2174 |  |  | 01-09-2005 | 42 h. | 21 h. | 18 h. | 15 h. | 17 h. | 06-09-2005 | 113 h. | Stripping |  |  |
| 9 | TBC2 | MBBL1187 |  |  | 06-09-2005 | 26 h. | 22 h. | 15 h. | 22 h. | 15 h. | 10-09-2005 | 100 h. | Stripping |  |  |
| 10 | TBD1 | SSS250 |  |  | 05-09-2005 | 32 h. | 38 h. | 19 h. | 14 h. | 26 h. | 10-09-2005 | 129 h. | Stripping |  |  |
| 11 | TBD1 | SSS252 |  |  | 31-08-2005 | 34 h. | -34 h. | 67 h. | 7 h. | 37 h. | 05-09-2005 | 111 h. | Stand By |  |  |
| 12 | TBD2 | SSS606 |  |  | 24-08-2005 | 222 h. | - | - | - | - | 08-09-2005 | 369 h. | Stand By |  |  |
| 13 | TBE1 | MBBL2183 |  |  | 03-09-2005 | 44 h. | 31 h. | 17 h. | 17 h. | 9 h. | 08-09-2005 | 118 h. | Stripping |  |  |
| 14 | TBE2 | MBBR1260 |  |  | 03-09-2005 | 41 h. | 27 h. | 28 h. | 15 h. | 18 h. | 08-09-2005 | 129 h. | Stripping |  |  |
| 15 | TBF1 | MBAR3354 |  |  | 01-09-2005 | 28 h. | 26 h. | 20 h. | 26 h. | 8 h. | 05-09-2005 | 108 h. | Stripping |  |  |
| 16 | TBF1 | MBBL1240 |  |  | 05-09-2005 | 29 h. | 24 h. | 20 h. | 14 h. | 11 h. | 09-09-2005 | 98 h. | Stripping |  |  |
| 17 | TBF2 | MBAL1222 |  |  | 01-09-2005 | 40 h. | 29 h. | 35 h. | 14 h. | 8 h. | 07-09-2005 | 126 h. | Stripping |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR3333 | 9741.9 A. (D2-L-S01) | 11969 A. (D2-L-S01) | 12731 A. (D1-L-S01) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 2 | MBBL1188 | 11925.7 A. (D2_L) | 12763 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBR3382 | 12391.4 A. (D1_U) | 12311.6 A. (D2-U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBL2144 | 10540 A. (D2_L) | 11227 A. (D2_L) | 11958 A. (D2_L) | 12319 A. (D2-L) | 12650 A. (D1_U) | 12829 A. (D2_L) | 12850 A. | - | - | - | - | - | - |
| 5 | MBBL2199 | 11670.2 A. (D1-L) | 12507.5 A. (D2-U) | 12644 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 6 | MBBL2218 | 12425 A. (D2_U) | 12644 A. (D1-U) | 12822 A. (D2-L) |  | - | - | - | - | - | - | - | - | - |
| 7 | MBBR1258 | 12068 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBAL2174 | 11275.2 A. (D2_L) | 11611.6 A. (D1_U) | 12424 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 9 | MBBL1187 | 11850 A. (D1_L) | 12513 A. (D1-L) | 12736 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |
| 10 | SSS250 | 11574 A. (QE-12) | 12248.4 A. (QE_34) | 12424.6 A. (QI_12) |  | - | - | - | - | - | - | - | - | - |
| 11 | SSS252 | 10967 A. (QE-34) | 12120 A. (QI-34) | 12193 A. (QI_12) |  | - | - | - | - | - | - | - | - | - |
| 12 | SSS606 | 3485 A. (MQM-1-In) | 3821 A. (MQM-1-In) | 4033 A. (MQM-2-Ex) | 4099 A. (MQM-1-In) | 4165 A. (MQM-2-In) | 4209 A. (MQM-2_Ex) | 4224 A. (MQM-2-E) | 4236 A. (MQM-E-1) | 4251 A. (MQM-In-1) | 4265 A. (MQM-Ex-1) | 4336 A. (MQM-In-2) | 4367 A. (MQM_I_1) | 4395 A. (MQM_I_2) | 4417 A. (MQM-E-1) | 4437 A. (MQM-I-1) |  |
| 13 | MBBL2183 | 10815 A. (D1_L) | 12255 A. (D2_L) | 12477 A. (D2_U) |  | - | - | - | - | - | - | - | - | - |  |  |  |
| 14 | MBBR1260 | 10130 A. (D2-L) | 11709 A. (D2_U) | 11827 A. (D2_L) | 12472 A. (D1_U) | 12343.1 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - |  |  |  |
| 15 | MBAR3354 | 9931.2 A. (D1_U) | 11760 A. (D2-L) | 12746 A. (D2_L) | 0 A. (No Data) | 12850 A. | - | - | - | - | - | - | - | - |  |  |  |
| 16 | MBBL1240 | 11308 A. (D1-L) | 12193 A. (D2_L) | 12324 A. (D1-U) |  | - | - | - | - | - | - | - | - | - |  |  |  |
| 17 | MBAL1222 | 12635 A. (D1_L) | 12761.2 A. (D2_L_S01) | 12850 A. | - | - | - | - | - | - | - | - | - | - |  |  |  |

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Wednesday _07_M | TBC | Could not switch on the power converter | AB/PO |  | OK after re-connecting the serial cable on the PC control panel. (Not restored after calibration?) |
| Wednesday _07_A | TBA2 | AQA analysis was not possible because the files where not copied correctly to the storage disk. | AB/CO | AQA | Giorgio copied the file in the right storage folder. |
| Thursday_08_A | TBC2 | Config files have been generated manually due to an error in the MTF concerning temperature gage attached under 1256. | CRI | MTF | HWREC off during the test and magnet name entered manually. Two TT821 were present. |
| Saturday _10_M | TBA1 | Problem of magnet naming in HWREC. | MTM | HWREC | Maryline gave by phone the procedure; magnet name is MBAL3391 |
| Saturday _10_M | TBF2 | SPA occurred at 12000 A on MB1239 | ? |  | No cryo fault. |
| Saturday _10_M | TBF2 | PLCSE-PLCHV connection problems | AB/CO |  | Maryline informed. She advised to reset the PLCSE and the server. |
| Sunday_11_M | TBE1 | MB3392: 1.5 kA protection quench test. No alarm but the graphs of voltage, current and Tau are not usual. The Tau jump value is 1.0. | MTM | AQA | Maryline informed. She advised to proceed with the tests. |
| Sunady _11_N | TBD1 | Configuration files contains oracle errors in HWREC launching IAP on D1. | MTM | HWREC | Maryline informed Monday morning.Giorgio forgot to update the DICO of the PC 60 A. |