### VC- /Week 45 starting 06 Nov  06

### SM18 Operation Meeting (Tuesdays) 07 Nov 06

Bench status  on Monday 06-Nov-2006 at: 11/6/2006 12:30:27 PM

| 11 | A1 | MBBR2400 | ICS 3 Traveller after warm test | 293.3 |
| --- | --- | --- | --- | --- |
| 4 | A2 | MBBL1405 | Prep 5 Cool Down | 1.90 |
| 3 | B1 | SSS366 | FS12 MQ Strength @5000 | 1.90 |
| 12 | B2 |  |  | 293.74 |
| 6 | C1 | SSS362 | PT 12 Warm Up | 176.91 |
| 7 | C2 | SSS047 | PT 14 Magnet MAPS | 293.83 |
| 8 | D1 | SSS521 | PT 14 Magnet MAPS | 292.94 |
| 5 | D2 | SSS670 | Prep 1 Lyre Test | 293.74 |
| 1 | E1 | MBAR2405 | PT 12 Warm Up | 232.19 |
| 9 | E2 | MBBR2401 | ICS 3 Traveller after warm test | 293.65 |
| 10 | F1 | MBBL1407 | PT 14 Magnet MAPS | 292.49 |
| 2 | F2 | MBAR1412 | PT 13.2 Resist. Meas. | 294.1 |

CONFIG :  D 6 - AS 2 -  IRSSS 4 ;

Supervisor: ;                        Eq support 16-3602 :

12 Magnet Tests completed ( 8 Magnet Stripped )

6 Dipoles tests	(1413 with MM incl correctors, SSW etc)

3 Arc-SSS (308, 036, 237 )

2  500-series (514 ( MQTL poor powering,   515 – 11 Q’s  to ultimate  + CQW2

pblm)

1  600-series [ 679  (381 hrs)–  : tests done by Eq Sup ; no results in SMTMS ]

General Points:

- Situation from ICS ( POOR) :  Personnel,

  - ROCLA hrs from next week etc

- Situation from Cryogenics:  J-P Lamboy or ACR Rep :

- Situation SSSS  :D1 & D2 issues J Halik

- A.O.B..

| Magnets under Test from 29-10-2006 to 04-11-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA2 | MBAR1413 |  |  | 26-10-2006 | 28 h. | 33 h. | 93 h. | 24 h. | 23 h. | 03-11-2006 | 201 h. | Stripping |  |  |
| 2 | TBB1 | SSS514 |  |  | 27-10-2006 | 40 h. | 16 h. | 43 h. | 12 h. | 23 h. | 02-11-2006 | 134 h. | Stand By |  |  |
| 3 | TBB2 | SSS515 |  |  | 24-10-2006 | 32 h. | 20 h. | 61 h. | 11 h. | 37 h. | 31-10-2006 | 161 h. | Stand By |  |  |
| 4 | TBC1 | SSS036 |  |  | 30-10-2006 | 28 h. | 15 h. | 25 h. | 9 h. | 34 h. | 04-11-2006 | 111 h. | Stripping |  |  |
| 5 | TBC1 | SSS308 |  |  | 23-10-2006 | 23 h. | 29 h. | 12 h. | 10 h. | 41 h. | 30-10-2006 | 115 h. | Stripping |  |  |
| 6 | TBC2 | SSS237 |  |  | 26-10-2006 | 35 h. | 17 h. | 36 h. | 6 h. | 14 h. | 31-10-2006 | 108 h. | Stripping |  |  |
| 7 | TBD2 | SSS679 |  |  | 17-10-2006 | 44 h. | 36 h. | 257 h. | 19 h. | 25 h. | 02-11-2006 | 381 h. | Stand By |  |  |
| 8 | TBE1 | MBAR1411 |  |  | 29-10-2006 | 28 h. | 21 h. | 20 h. | 14 h. | 16 h. | 02-11-2006 | 99 h. | Stripping |  |  |
| 9 | TBE1 | MBBR2325 |  |  | 22-10-2006 | 32 h. | 44 h. | 35 h. | 17 h. | 33 h. | 29-10-2006 | 161 h. | Stand By |  |  |
| 10 | TBE2 | MBAL2350 |  |  | 24-10-2006 | 45 h. | 24 h. | 34 h. | 15 h. | 24 h. | 31-10-2006 | 142 h. | Stripping |  |  |
| 11 | TBF1 | MBAR2372 |  |  | 24-10-2006 | 35 h. | 27 h. | 15 h. | 19 h. | 31 h. | 31-10-2006 | 127 h. | Stripping |  |  |
| 12 | TBF2 | MBAR2270 |  |  | 27-10-2006 | 30 h. | 29 h. | 17 h. | 15 h. | 30 h. | 01-11-2006 | 121 h. | Stripping |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAR1413 | 9932.7 A. (D1-L) | 12675.8 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 2 | SSS514 | 11388.3 A. (QI-34) | 12012.2 A. (QE_12) | 12621 A. (QI_12) |  | - | - | - | - | - | - | - | - | - |
| 3 | SSS515 | 11407.9 A. (QI_12_C5) | 12004.1 A. (QI_34_N5) | 12214.3 A. (QI_34_C5) | 12324.4 A. (QI_12_C5) | 12366.7 A. (QI_12_N5) | 12464.6 A. (QE_34_C5) | 12539.1 A. (QI_34_C5) | 12557.3 A. (QI_34_C5) | 12686.5 A. (QI_34_N5) | 12786.6 A. (QI-12_C1) | 12850 A. | - | - |
| 4 | SSS036 | 12472.2 A. (QE_34) | 12826.5 A. (QE_34) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 5 | SSS308 | 12132.6 A. (QI_12) | 12577.1 A. (QE_34) | 12747.3 A. (QE_12) |  | - | - | - | - | - | - | - | - | - |
| 6 | SSS237 | 11999.8 A. (QE_12) | 12505.2 A. (QE_34) | 12675.9 A. (QI_12) |  | - | - | - | - | - | - | - | - | - |
| 7 | SSS679 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 8 | MBAR1411 | 11381.8 A. (D1_L) | 12900 A. | - | - | - | - | - | - | - | - | - | - | - |
| 9 | MBBR2325 | 11581.3 A. (D1_U) | 12349.9 A. (D2_U) | 11737 A. (D2_U) | 11367.7 A. (D2_U) | 12133.5 A. (D2_U) | 10819.9 A. (D2_U) | 11805.3 A. (D2_U) | 11750.3 A. (D2_U) | 11665.1 A. (D2_U) |  | - | - | - |
| 10 | MBAL2350 | 11173.3 A. (D1_U) | 12279.2 A. (D2-L) | 12859 A. | - | - | - | - | - | - | - | - | - | - |
| 11 | MBAR2372 | 11925.7 A. (D1_L) | 12137.2 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 12 | MBAR2270 | 11373.1 A. (D2_L) | 12599.5 A. (D1_L) | 12802.3 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |

1413 had Long MM;  Long Connect /disconnect due to ICS;  679 was in hands of Experts…not  OP team

V.Chohan (04_Nov’ 06)

Statistics for end October.06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

Prediction on 3rd-October 06 For Termination by end 2006 : Desired Magnets & Desired Bench Configurations

V.Chohan (04_Nov’ 06)

Statistics for end October.06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

CRYO TIMES

V.Chohan (04_Nov’ 06)

Statistics for end October.06

ICS TIMES

V.Chohan (04_Nov’ 06)

Statistics for end October.06

ICS TIMES

V.Chohan (04_Nov’ 06)

Statistics for end October.06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

4.5K Operation Special SSS’s :Test Times for Magnetic M’ments With Anticryostat  Inserts  and Magnets  Without Magnetic Measurements

V.Chohan (04_Nov’ 06)

Statistics for end October.06

Percentage of Magnets Tested and Remaining till end October 06

V.Chohan (04_Nov’ 06)

Statistics for end October.06

Percentage of Magnets Tested and Remaining till end October 06