### VC- /Week 46 starting 20 Nov  06

### SM18 Operation Meeting (Tuesdays) 21 Nov 06

Bench status  on Monday 20-Nov-2006 at: 11/20/2006 4:09:03 PM

| 3 | A1 | MBAL1402 | PT 6.4 Training 4 | 1.90 |
| --- | --- | --- | --- | --- |
| 6 | A2 | MBAR1372 | Prep 5 Cool Down | 73.23 |
| 8 | B1 | SSS517 | PT 14 Magnet MAPS | 295.8 |
| 4 | B2 | SSS650 | PT 6.7 Training 7 | 4.32 HV |
| 12 | C1 | SSS363 | PT 14 Magnet MAPS | 294.64 |
| 10 | C2 | SSS064 | ICS 2 Connect Magnet (ICS) | 295.36 |
| 11 | D1 | SSS671 | PT 13.2 Resist. Meas. | 296.34 |
| 2 | D2 | SSS675 | Stretched Wire Cold SC12 | 1.90 |
| 7 | E1 | MBAL1416 | Prep 5 Cool Down | 122.71 |
| 5 | E2 | MBAL2282 | PT 6.4 Training 4 | 1.90 |
| 1 | F1 | MBAR1341 | PT 12 Warm Up | 114.55 |
| 9 | F2 | MBBR2325 | PT 13.2 Resist. Meas. | 297.41 |

CONFIG :  D 6 - AS 2 -  IRSSS 4 ;

Supervisor: Gijs (gilbert) ;        Eq support 16-3602 :

12 Magnet Tests completed ( 8 Magnet Stripped )

7 Dipoles tests	( all signed stripping)

3 Arc-SSS (  064 ok in HV but voltage tap open )

0 500-series (  )

2  600-series [ 670 (264 hrs)  671 with MM (187 hrs) now retest without antiCryo]

General Points:

- Work load & 8 benches free on last Tues & full excessive work on Fri/sat/sun !

- SSS064 why & what ?

- 671/670/650   all 4.4K magnets & poor perf

- 517 Corrector powering (  ~20 quenches . .!)

- HV tests :iCS WP04, WP07 , e-traveller, ICS rack ,   Dipole & SSS

- Situation from Cryogenics:  J-P Lamboy or ACR Rep :

- Situation SSSS  :D1 & D2 issues J Halik

- A.O.B

| 4 | A1 | MBBR2395 | PT 13.2 Resist. Meas. | 299.65 |
| --- | --- | --- | --- | --- |
| 12 | A2 | MBAR2403 | Prep 5 Cool Down | 4.44 HV |
| 10 | B1 |  |  | 295.54 |
| 2 | B2 |  |  | 296.07 |
| 11 | C1 | SSS064 | PT 13.2 Resist. Meas. | 295.8 |
| 5 | C2 |  |  | 295.8 |
| 6 | D1 | SSS671 | PT 6.8 Training 8 | 4.62 |
| 9 | D2 |  |  | 296.25 |
| 1 | E1 | MBAL1394 | ICS 3 Traveller after warm test | 296.97 |
| 7 | E2 |  |  | 296.88 |
| 3 | F1 |  |  | 294.1 |
| 8 | F2 |  |  | 294.73 |

11/15/2006 12:23:58 AM

| Magnets under Test from 12-11-2006 to 18-11-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBBR2395 |  |  | 11-11-2006 | 32 h. | 19 h. | 12 h. | 17 h. | 19 h. | 15-11-2006 | 99 h. | Stripping |  |  |
| 2 | TBA2 | MBAR2403 |  |  | 10-11-2006 | 94 h. | 20 h. | 30 h. | 17 h. | 18 h. | 17-11-2006 | 179 h. | Stripping |  |  |
| 3 | TBB1 | SSS366 |  |  | 02-11-2006 | 45 h. | 16 h. | 136 h. | 8 h. | 17 h. | 13-11-2006 | 222 h. | Stripping |  |  |
| 4 | TBC1 | SSS064 |  |  | 09-11-2006 | 35 h. | 20 h. | 56 h. | 6 h. | 31 h. | 15-11-2006 | 148 h. | Stand By |  |  |
| 5 | TBC2 | SSS371 |  |  | 07-11-2006 | 32 h. | 25 h. | 18 h. | 6 h. | 15 h. | 13-11-2006 | 96 h. | Stripping |  |  |
| 6 | TBD1 | SSS671 |  |  | 08-11-2006 | 56 h. | 29 h. | 84 h. | 18 h. | 0 h. | 16-11-2006 | 187 h. | Not Found or Thermal cycle |  |  |
| 7 | TBD2 | SSS670 |  |  | 03-11-2006 | 109 h. | 65 h. | 57 h. | 15 h. | 18 h. | 14-11-2006 | 264 h. | Stand By |  |  |
| 8 | TBE1 | MBAL1394 |  |  | 14-11-2006 | 21 h. | 23 h. | 15 h. | 15 h. | 26 h. | 18-11-2006 | 100 h. | Stripping |  |  |
| 9 | TBE1 | MBBR2391 |  |  | 08-11-2006 | 26 h. | 19 h. | 14 h. | 18 h. | 16 h. | 13-11-2006 | 93 h. | Stripping |  |  |
| 10 | TBE2 | MBAR2406 |  |  | 10-11-2006 | 15 h. | 35 h. | 14 h. | 16 h. | 10 h. | 14-11-2006 | 90 h. | Stripping |  |  |
| 11 | TBF1 | MBAL1415 |  |  | 07-11-2006 | 31 h. | 19 h. | 12 h. | 17 h. | 21 h. | 13-11-2006 | 100 h. | Stripping |  |  |
| 12 | TBF2 | MBAR1361 |  |  | 08-11-2006 | 30 h. | 21 h. | 14 h. | 17 h. | 17 h. | 13-11-2006 | 99 h. | Stripping |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR2395 | 11819.8 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAR2403 | 11293.5 A. (D1_U) | 12636 A. (D1-L) | 12194 A. (D1-U) | 12828.7 A. (D1-L) | 12832.8 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - |
| 3 | SSS366 | 11617.1 A. (QI_34) | 12288.2 A. (QI_34) | 12596.3 A. (QI_34) | 12609.5 A. (QE_34) |  | - | - | - | - | - | - | - | - |
| 4 | SSS064 | 11978.1 A. (QI_12) | 12190.3 A. (QI_12) | 12296.9 A. (QE_34) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS371 | 12165.1 A. (QE_12) | 12845.3 A. (QE_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS671 | 3496 A. (MQY2-INT) | 3558.1 A. (Ext-2) | 3618.6 A. (MQYInt_1) | 3611.3 A. (Int_MQY1) | 3615.1 A. (Int_MQY) | 3619.1 A. (Int_MQY1) | 3640.1 A. (Int_MQY2) | 3645.6 A. (I_MQY_1) | 3648.2 A. (Int_MQY2) | 3660.5 A. (Int_MQY1) | 3661.2 A. (I_MQY_2) | 3674.7 A. (I_MQY_1) |  |
| 7 | SSS670 | 3509.8 A. (Int_MQY2) | 3628.7 A. (Int_MQY2) | 3652.5 A. (I-MQY-1) | 3655.6 A. (Int MQY2) | 3678.1 A. (Int MQY2) | 3739.5 A. (Ext MQY2) | 3743.1 A. (Int_MQY2) | 3762.4 A. (Int_MQY2) | 3774.7 A. (E-MQY-2) | 3779.7 A. (I_MQY_1) | 3785.2 A. (E_MQY_2) | 3780.7 A. (E_MQY_2) | 3785.3 A. (I_MQY_2) | 3794.4 A. (Int_MQY1) |  |
| 8 | MBAL1394 | 10504.6 A. (D1_U) | 12458 A. (D2_U) | 12665 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |  |  |
| 9 | MBBR2391 | 11046.8 A. (D2_L) | 12286.1 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |  |  |
| 10 | MBAR2406 | 12073.1 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |  |  |
| 11 | MBAL1415 | 11642.6 A. (D1_L) | 12210.4 A. (D1_L) | 12413 A. (D1-L) |  | - | - | - | - | - | - | - | - | - |  |  |
| 12 | MBAR1361 | 11384.9 A. (D1_U) | 12699.7 A. (D1_U) | 12713.5 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |  |  |

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_14_M | TBC1 | SSS064 : IAP error 2 warm (PT13.1) | MTM |  | Richard consulted: Test repeated with potaim card adjustment. Error of offset could be removed on 3rd attempt. But error remained on IAP_QE value. Proceed for CQW2. |
| Tuesday_14_M | TBC1 | Voltage found floating in CQW2. | MTM |  | Richard found voltage tap EE211 is open by checking resistance from IFS box. NC to be opened. |
| Tuesday_14_N | TBB1 | SSS366: Magnet could not be scanned as it had no front cover. |  |  |  |
| Wednesday_15_A | TBA2 | MB2403 : The MB detrained by more than 500 A. | MTM |  | TC decided to go for ultimate before warming up. |
| Wednesday_15_N | TBA2 | MB2403: During ramp of training quench a slow PA on power supply has done (error on Power Supply is No PC permit and PLC_SE OK). | AB/PO |  | Current ramp re-launched. |
| Thursday_16_N | TBB1 | Cryo Not OK-no flow in the current leads. | ACR |  | Walve found closed. Reopen: test can proceed. |
| Friday_17_N | TBD1 | SSS671: Cryo OK not stable at 4.5 K. | ACR |  | OK after four hours (magnet in priority one). |
| Saturday_18_M | TBF2 | MB2325: Ext2 Interlock on the PC. Cannot change the PC to TBF2. | MTM |  | Federico contacted. He found the emergency stop pushed. |
| Saturday_18_A | TBA2 | MB1372: Trying to contact ICS for LYRA test for the last one hour but there is no response | ICS |  |  |
| Saturday_18_A | TBF2 | MB2325: MM1 error (encoder) in shaft position | MTM |  | Federico called. Solved by Federico (front subD connectors were not connected). |
| Saturday_18_A | TBA2 | MB2403: HV test at cold before powering failed Dipole vs Ground. | MTM |  | Federico called. He advised to perform all the steps then the 1.5kA provoked quench then repeat the HV test to see improvements. OK after the two quenches. |
| Saturday_18_A | TBF2 | MB2325: Current reading in MMP missing in aperture 1 | AB/CO |  | Federico changed the DIGIO card (same problem) then he disconnect/reconnected the 2 lemo cables inside main PS. Measurements OK. |
| Saturday_18_N | TBA1 | MB1403: Angle difference errors during MM1. Shaft is not rotating well in aperture1 | MTM |  | Stéphane called Sunday. He asked to GHH values of RMS of rotation. GHH replies that there is no alert apart from angle difference. Stéphane advised to continue. Be careful, in fact RMS was at 3.7% in RED! |
| Sunday_19_M | TBB2 | SSS650: Quench location could not be interpreted from AQA even though rise of main voltage signals are prominent due to improper name of potaim card signals in AQA. | MTM | AQA | TC and Federico called. Tests are being continued. Location information shall be updated later |
| Sunday_19_A | TBD1 | SSS671: Poor performance of the MQY (3766 A after Quench 13). | MTM |  | TC advised to warm _up the magnet after the 13rd training quench. |
| Sunday_19_N | TBB2 | SSS650: Improper names of channels already found in IAP at warm | MTM |  | Federico forced the regeneration. of all config files with HWREC and he triggered a blank HF file to check the results. Results OK. |
| Monday_20_M | TBD1 | SSS671: No data after IAP at warm (after cold test). Test repeated: Same result. | MTM | IAP | Giorgio checked file from lf off and validated the results. He found wrong configuration of files for some unknown reason. |