### SEKS-SSR-EV- /Week 5 starting   29 Jan 07

### SM18 Operation Meeting (Tuesdays) 13 Feb  07

Bench status  on Monday 12-Feb-2007

Situation on the test benches ;

-MB2267, MB2425 warmed up. 2 MB for the machines:

-MB2426 (on test) and MB2394 (coming on E1 bench).

-2 500- SSS to be tested : SSS529 (thermal cycle) and SSS530 cooling down

-1 Arc SSS on cold test (SSS374)

-MM on SSS374 and SSS529 (restricted MM program).

Situation from Cryogenics:  J-P Lamboy (connector damaged on D1, long cooling in TBF2)

Situation of mechanics  : J Halik

General Points:

- Test coordination by M. Buzio from Wednesday mid-day.

- MQTL in SSS531: Stopped at 9 training quenches,500 A (not nominal, 300 A enough)

- Thermal cycle rules for SSS529 (not conform for MQ and MQTL).

4  Magnet Tests completed () + 1 run on SSS529;

2 Dipoles tests

2 arc SSS

### Quench Information

### Case of SSS529 (MQ)

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Wednesday_07_M | TBF2 | MBAR 2267 was not cooling down, Cryo replied that magnet was in the same phase as in night after quench and they will started cooling now. | ACR |  | Tuning of the cryo parameters to be done. One night lost. |
| Wednesday_07_M | TBB2 | SSS531: CD-corrector powering could not be done. PC Aux error in PLCSE. | MTM |  | Solved by Salem. |
| Wednesday_07_M | TBE2 | MB2426 :Leak found during capillary test (M2 line) | ACR |  | Joint with default. Lionel checked the other ones available for ICS. Magnet disconnected and reconnected. |
| Wednesday_07_A | TBB1 | SSS374: Abnormal voltage tap signal shapes during IAP (Prep 2.2). | MTM |  | Salem contacted. He informed that the configuration files need to be corrected for this magnet. Done in the next morning. |
| Wednesday_07_A | TBB1 | SSS374: HV could not be launched due to wrong cryo phase interlock. | ACR |  | Salem solved the problem with ACR team next morning. |
| Wednesday_07_A | TBD1 | SSS529: EF corrector powering – 600A power converter is not going to standby mode, shows some 'bad state error'. | AB/PO |  | Salem contacted. He reset the power supply. |
| Thursday_08_M | TBB1 | SSS374 : CQW1 HV cannot be uploaded. Link to MTF from this is not available, may be blocked | TS |  |  |
| Thursday_08_A |  | In HV rack MY95 temperature sensor and humidity sensor not found. | MTM |  |  |
| Friday_09_M | TBF2 | MB2267: Loss of cryo-OK during LHC cycle. | ACR |  | Return BP to high. Quench and test to be re done. |
| Friday_09_M | TBA1 | MB1334: Lyra call came without WP04. | MTM |  | Stéphane asked to go on with connection WP04 was executed by Richard. |
| Friday_09_A | TBD1 | SSS529: Connectors on the CFB damaged. | TCR |  | SSS warming up naturally. Thermal cycle executed Monday after repair. |
| Monday_12_A | TBF1 | MB2425: HV test AP, HV Rack (MY92) unable to launch HV Test (Dipole-Ground) due to PLC-HV communication failure. |  |  | Solved by Salem, changing the HV rack. |